## Slide 1: MLO Discovery Signaling
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Problem statement
A non-AP MLD should be able to gather information about an AP MLD and all the links it supports upon receiving a beacon from any AP of the MLD

## Slide 3: What info. needs to be advertised?
An AP of an AP MLD shall advertise at least the following information to aid discovery:
  Complete information of advertising AP
    such as capabilities and operational parameters
  MLD-level Information
    such as identity, authentication scheme(s), etc
    This is common to all the APs
  Complete or partial information of other APs of the MLD
This contribution discusses the framework to support efficient advertisement of MLO capabilities
  A subsequent contribution discusses the actual element/fields to carry this information

## Slide 4: Classification of information
Advertising link’s Information
  Carried same as today for legacy compliance
    individual elements (e.g., EHT/HE/(V)HT Cap/Op elements)
MLD (common) information
  Applies to all APs of the MLD
Per-link information
  Carries information of all APs of the MLD other than the advertising AP
  This information can be partial or complete
    See later slides for details
Advertising Link’s Information (AP 1)
MLD Common
AP 2
AP 3
AP 4
Information of other APs of the MLD
Individual elements

## Slide 5: Per-link information: Complete vs Partial
An AP may include complete or partial information of another link
  Each approach has its pros and cons.
Complete profile of a link
  AP’s beacon includes full information about another link
  Pros: non-AP gets all the information on one link (avoids scanning the other link)
  Cons: can lead to beacon bloating
Partial profile of a link
  AP’s beacon identifies the link (Op Class, Channel, BSSID) and provides basic information (including indication of critical updates).
  Pros: prevents beacon bloating
  Cons: non-AP STA may need to scan the other link
MLO framework should allow both options

## Slide 6: Inheritance Model
An MLD is expected to have certain parameters that are same for multiple links
When advertising complete information, an inheritance model (same as 11ax Multi-BSSID feature) is recommended
  To prevent duplication of information and address beacon bloating
  Any parameter not advertised in a link’s profile is the same as the advertising link
Other properties from multiple BSSID feature, such as profile straddling and non-inheritance, would apply here.

## Slide 7: Benefits of the framework
The framework discussed in this contribution is extensible and would be applicable in other scenario
  Active scanning: Probe Req/Resp frames use this framework to provide capabilities information
  ML Setup: Frames exchanged during ML setup use this frame to carry exhaustive information of all the links.
    The information advertised during discovery is expected to be rudimentary compared to that exchanged during setup
Advertising Link’s Information (STA 1)
MLD Common
STA 2
STA 3
STA 4
Information of other STAs of the MLD
Individual elements

## Slide 8: Summary
This contribution discusses the topic of multi-link capability advertisement and provides a flexible framework to carry an MLD’s information.
Further, the contribution proposes a couple of schemes to help reduce frame bloating
  Advertising STA may use an inheritance model to avoid duplication of information advertised for other links.
    Inheritance model same as 11ax multiple BSSID feature
  Advertising STA may advertise partial information of other links
    Identify the link and provide rudimentary information

## Slide 9: SP #1
Do you agree to classify the information that an MLD provides in its mgmt. frames, during discovery and ML setup, as described below?
  Advertising link’s Information
    Capabilities and Operational parameter of the STA transmitting the frame
  MLD (common) Information
    Information common to all the STAs of the MLD
  Per-link information
    Capabilities and Operational parameter of all other STAs of the MLD other than the advertising STA
  Y:
  N:
  A:

## Slide 10: SP #2
Do you support that the MLO framework should follow an inheritance model (as described for 11ax multiple BSSID feature) to prevent frame bloating when advertising complete information of other links?
  Note: this includes properties such as profile straddling across multiple elements and non-inheritance
  Y:
  N:
  A:

## Slide 11: SP #3
Do you support that an AP MLD may advertise partial information of other links to prevent frame bloating?
  Y:
  N:
  A:

## Slide 12: SP #4
Do you support that a STA of non-AP MLD shall include in its Probe Request an indication that it supports MLO operation?
  Y:
  N:
  A:

## Slide 13: SP #5
Do you support that an AP of an AP MLD shall not include MLO information (i.e., MLD/common info. and info. of other links of the AP MLD) when responding, with an individually addressed Probe Response frame, to a Probe Request frame from a non-AP STA that has not indicated support for MLO?
  Y:
  N:
  A:

## Slide 14: Appendix

## Slide 15: Inheritance Model
Advertising Link’s Information (STA 1)
Common/MLD
STA 2
STA 3
STA 4
Information of other STAs of the MLD (link profiles)
Capabilities and parameters different from the advertising link
Non-inheritance

## Slide 16: Related motion
[Motion 32]  AP MLD advertises capability and operational parameters for multiple links
  802.11be defines mechanism(s) for multi-link operation that enables the following:
    Indication of capabilities and operating parameters for multiple links of an AP MLD.
    Negotiation of capabilities and operating parameters for multiple links during a single setup signaling exchange.
[Motion 21]  AP and non-AP MLDs provide their capabilities and operational parameters for multiple links
  802.11be supports a mechanism for multi-link operation:
    An AP affiliated with an AP MLD can indicate the capabilities and operational parameters for one or more STAs of the multi-link device.
    A non-AP STA affiliated with a non-AP MLD can indicate the capabilities for one or more non-AP STAs of the non-AP MLD.
    Specific information of capabilities and operational parameters of multi-link device is TBD.
[Motion 26]  advertise MLD/common information
  A MLD can indicate capability to support exchanging frames simultaneously on a set of affiliated STAs to another MLD.
[Motion 38]  advertise common information such as STR capabilities
  A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
    NOTE 1 – The 2 links are on different channels.
    NOTE 2 – Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.