## Slide 1: Proposals on unused bandwidth utilization
Date: 2020-03-16
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  |  | matthew.fischer@broadcom.com

## Slide 2: Abstract
This contribution discusses changes required to enable a device to transmit on the DL or enable transmission on the UL, on any subset of channels that are a part of its operating bandwidth and are idle, even when the primary channel is busy.
Two scenarios are considered:
Scenario 1: Untriggered transmissions: Device finds the primary channel busy, either due to transmissions within its own BSS or OBSS, but still performs CCA on the other channels and transmits on these channels on completion of CCA.
Scenario 2: Triggered transmissions: Device (a AP in this case) triggers UL transmissions but realizes that a subset of the channels has not been utilized by the non-AP STA(s) (due to CCA failure or other reasons), in which case the device regains the unoccupied channels for its own DL/UL transmissions.
Prerequisites:
Device should be capable of performing CCA on channels in presence of transmission/reception on other channels.
Transmissions that exclude the primary channel should be allowed.

## Slide 3: Scenario 1: Untriggered transmissions when the primary channel is not idle (1)
APs or non-AP STAs can make use of the scheme.
Types of busy detection and corresponding actions.
  When the primary channel is busy due to transmissions from own BSS1
    Transmission on the channels that have been reacquired and the ongoing transmission on the primary channel should have the same end time. This helps realigning the availability of primary and other channels for wideband operation and aids any other devices in the network that are not capable of performing independent Tx/Rx/CCA on the channels.
  When the primary channel is busy due to transmission from OBSS1
    It is desirable that the transmission on the channels that have been reacquired and the ongoing transmission on the primary channel have the same end time, so that devices that are unable to do CCA on the primary channel due to transmission on other channels have an opportunity to reoccupy the primary channel
  When the primary channel is detected busy using only ED
    It is still useful to occupy the unused channels. The primary channel may be due to transmissions from another technology, for which the duration of transmission may not be available. In this case, the device can either transmit for an entire TXOP or have shorter bursts of transmission while polling the primary periodically
1 The BSS/OBSS distinction is made via preamble detection.

## Slide 4: Scenario 1: Untriggered transmissions when the primary channel is not idle (2)
To be able to transmit on any combination of remaining channels, full CCA needs to be running on each of the 20 MHz channels. This is required by the ETSI harmonized standard for 5 GHz (EN 301893).
  However, whenever the device wins access on any one channel using full CCA, it is allowed to do PIFS CCA on the other channels and transmit on the set of idle channels, if the set of channels are part of an 802.11 bonded channel set.
  Another option is to start the full CCA after the device determines the primary channel is busy and some other channels are idle. However, this may delay gaining access to these channels.
If the device needs to align the end of its own transmission with the end of ongoing transmission on the primary channel, it needs to read the duration from the PHY header of the primary channel transmission. The device can either start its own transmission on the other channels after it reads the duration from the PHY header or it can start with a short packet until the duration information is available.
  As proposed in IEEE 802.11-20/0362r0 , a mode can be defined to enable a device to transmit consecutive AMPDUs, separated by SIFS gap or even without any gap, with any immediate Block Ack from the receiver after each AMPDU. This will allow the device to meaningfully occupy the medium with transmission of short AMPDU(s) until it is reads the duration of the current Primary channel transmission.

## Slide 5: Scenario 2: Triggered transmissions when the primary channel is not idle (1)
This case arises at the AP when it triggers multiple non-AP STAs using OFDMA or a non-AP STA using multi-RU allocations and some of the triggered UL PPDUs are not transmitted by the intended non-AP STAs due to failure of CCA or any other reasons
  The CCA failure case arises when the AP mandates CCA in the SIFS gap between the trigger and UL transmission by setting CS Required to 1.
  Multi-RU support in 802.11be can lead to a situation where for example, only one 40 MHz RU of two allocated 40 MHz RUs is occupied.
Spectrum utilization can be improved in the AP regains the unused channels.
However, the AP has to restart transmitting on the unused channel(s) soon enough, in order to satisfy channel occupancy rules of operating within the same TXOP.
As per the current ETSI harmonized standard for 5 GHz, the AP has to reacquire the channel and start transmissions within 25us of the end of the trigger transmission. The decision to transmit can be based on Energy Detection for the last 9us in the 25us gap.
If the AP delays access to the channel beyond 25 us of the end of the trigger, it can do a 25us PIFS CCA to reoccupy the channel. However, a gap > 25us is not permitted by ETSI harmonized standard.
As in the earlier scenario, it is beneficial for the AP to align the end times of such transmissions with the transmission on the primary channel. It is easy for the AP to do so since it is aware of the duration of the ongoing primary channel transmission (since the AP itself transmitted the trigger that set the duration).