## Slide 1: Proposals On Unused Bandwidth Utilizations
Date: 2020-08-26
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom | S1, Wipro Electronic City SEZ, Bangalore, 560100 |  | sndhu.verma@broadcom.com
Shubhodeep Adhikari |  |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  | 250 Innovation Dr, San Jose, CA 95134 |  | matthew.fischer@broadcom.com
Vinko Erceg |  |  |  | vinko.erceg@broadcom.com
Kaiying Lu | Mediatek |  |  | Kaiying.Lu@mediatek.com
James Yee |  |  |  | james.yee@mediatek.com
Notes: November 2012

## Slide 2: Abstract
A proposal to allow the utilization of some portion of the operating bandwidth when another portion of the operating bandwidth has been detected as BUSY

## Slide 3: Problem Statement
If the primary 20 MHz channel is busy, a STA does not transmit on any of the portion of the operating bandwidth, even when those portions are IDLE
Such inefficient bandwidth utilization in 802.11 is increasingly problematic with increasing operating bandwidth
  A busy 20MHz primary channel prevents a STA from accessing 300 MHz of remaining bandwidth, even when it is IDLE
Competing unlicensed technologies operating in the same bands, such as LAA and NR-U, do not have such limitations
  They are able to utilize any combination of idle channels
A “channel” in this presentation denotes a 20MHz bandwidth unit as defined by regulations and the 802.11 and other unlicensed standards.

## Slide 4: Solution
The problem of inefficient bandwidth usage can be alleviated by allowing a STA to transmit on any subset of channels that are a part of its operating bandwidth if they are idle
  And other qualifying conditions are met

## Slide 5: TXOP Initiation
While competing for access, an AP or non-AP STA finds the primary 20 MHz channel is BUSY
  MyBSS or OBSS transmission
Proposal: While the primary is BUSY, the STA performs CCA on other channels in its operating bandwidth and transmits on the channels where CCA completes successfully

## Slide 6: Considerations For Access Method
The access method which allows the use of unutilized portions of the operating bandwidth needs to:
  Ensure fairness to other devices attempting to use the channels
    E.g. randomized access process
  Adhere to regulatory rules

## Slide 7: Proposed Access Method for non-Primary Channels (1)
Regardless of the reason for the BUSY primary channel:
  MyBSS, OBSS or unknown, e.g. ED
CCA shall be performed on the other channels in the operating bandwidth
Option 1: A device starts full CCA on other channels after it determines the primary is busy
  E.g. suitable for devices which cannot perform full CCA in parallel on multiple channels
  Such sequential CCA can delay gaining access on the idle non-primary channels

## Slide 8: Proposed Access Method for non-Primary Channels (2)
Option 2: A device performs full CCA in parallel on multiple channels in its operating bandwidth, including the primary. If the primary is BUSY, CCA continues on other channels
  This is suitable for devices that can perform full CCA in parallel on multiple channels
  Reduces the delay in gaining access to non-primary channels
Definition of “Full CCA”
  ED or ED+PD
    With EDCA-style truncated exponential backoff
    NAV

## Slide 9: Proposed Access Method for non-Primary Channels (3)
For either option, when a device completes full CCA on any non-primary channel while the primary channel is BUSY:
  If the set of channels for which full CCA has completed is part of an 802.11 bonded channel set, perform PIFS CCA on the remaining channels and transmit on those that are found to be IDLE
  If the set of channels for which full CCA has completed is not part of an 802.11 bonded channel set, transmit only on those that complete full CCA together or at about the same time (e.g. using self-defer to align transmissions on the channels)

## Slide 10: Precedence of The Access Method
The behavior described here is specified by the ETSI harmonized standard for 5 GHz (EN 301 893)
The behavior is predicted to be copied into the ETSI rules for 6GHz
Both options are supported by LAA and NR-U.

## Slide 11: Alignment between Primary and Non-primary Transmissions (1)
Transmissions on any non-primary channels should end at the same time as the BUSY of the primary channel, because:
  Allows access on the primary 20 MHz channel to devices which cannot sense the primary channel while transmitting on the non-primary channel
  Allows fair access to devices that only perform Full CCA on the primary 20 MHz channel, by making wider bandwidths available to them
  Allows potential transmitters and recipients to operate using single RX and TX resources
  Minimizes loss of channel state information corresponding to the primary channel
This is possible when PPDU length and/or NAV information is known for the BUSY primary subchannel

## Slide 12: Alignment between Primary and Non-primary Transmissions (2)
When primary channel BUSY duration information is not available
  E.g. ED based BUSY, e.g. non-802.11 technology, no NAV, no PHY LENGTH
Participating STA may:
  Utilize non-Primary channels anyway
    Potentially be required to re-align, per other rules, if it experiences deafness on the primary channel
  Transmit short bursts on the non-primary channels while periodically polling the primary channel
    E.g. a compromise deafness solution

## Slide 13: NAV Loss Mitigation (1)
There may be loss of NAV information in the following cases:
  On the non-primary channels if a STA that is capable of Full CCA in a sequential manner only chooses such non-primary channels for transmission.
  On the primary channel when a STA returns to it for Full CCA after transmitting on the non-primary channels when the primary channel was busy
    There is no loss of NAV information if the STA had a non-zero PPDU length or a non-zero NAV on the primary channel and ended its transmission on the non-primary channels before or at the same time and resumed CCA on the primary channel.

## Slide 14: NAV Loss Mitigation (2)
Mitigation techniques:
  Use a lower ED threshold for CCA on the non-primary channels
  Use RTS/CTS for all TXOPs where the channel monitoring has been interrupted
  Limit retries for a period of time

## Slide 15: Straw Poll 1
Do you support the inclusion of the following in the SFD for R2:
  Non-primary transmission: The concept in which an AP that finds the primary channel to be busy under TBD conditions, can employ techniques to access and transmit on the idle non-primary channels under TBD conditions
  Y/N/A

## Slide 16: Straw Poll 2
Do you support the inclusion of the following in the SFD in R2:
  To handle missed NAV information on non-primary channels before selecting them for transmission when performing non-primary transmission, that the following mechanisms should be used:
    EDCA uses a lower (TBD) ED threshold
    TXOPs are initiated on the non-primary subchannels with an RTS/CTS exchange
Y/N/A

## Slide 17: Straw Poll 3
Do you support the inclusion of the following in the SFD in R2:
  On returning to the primary subchannel after transmitting using non-primary transmission, a device shall start a MediumSyncDelay timer for the primary subchannel, unless it had a non-zero PPDU length or non-zero NAV on the primary channel and ended the TXOP on the non-primary channel(s) within that non-zero time
  The MediumSyncDelay timer expires after a TBD duration or if the STA receives a PPDU with a valid MPDU or receives a PPDU with a valid TxOP_duration, whichever happens first
  While the MediumSyncDelay timer is running the device is allowed to attempt to initiate up to TBD (>=1) TxOPs using RTS and a TBD ED threshold
Y/N/A

## Slide 18: Reference
[1] Draft P802.11REVmd_D3.4
[2] Draft P802.11ax_D6.1