## Slide 1: Multi-link Power Save Discussion
Date: 2020-03-15
Authors:

## Slide 2: Introduction
Multi-link operation (MLO) is a key feature of the 802.11be standard development
Power save is an important topic of MLO
In this contribution, we review multi-link power saving and present extreme low power multi-link operating mode

## Slide 3: Multi-link Power Save – Motions Recap
Each non-AP STA affiliated with a non-AP MLD that is operating on an enabled link maintains its own power state/mode.
An AP of an AP MLD may transmit on a link a frame that carries an indication of buffered data for transmission on other enabled link(s)
A non-AP MLD monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s).

## Slide 4: Multi-link Power Saving
Enabling multiple links and running power save mode independently on each link might not be the preferred multi-link power save operation
In some implementations, even when a single link is in awake state, the upper MAC needs to be turned on
In worst case, the power saving might be negligible if the sleep cycles are unsynchronized
However, synchronizing power saving mechanisms e.g. TWT over multiple links introduces additional complexity at the AP MLD as tighter synchronization is required in multi-link BSS management
Therefore, for a non-AP MLD, a practical power save mode is to enable only a single link and activate power saving mode on that link.

## Slide 5: Extreme Low Power Multi-link Operation mode
We propose extreme low power multi-link operation mode as the 802.11be non-AP MLD operating mode in which the non-AP MLD enables a single link among the setup links and the non-AP MLD runs power save mechanism(s) on that link.
  Exact name of this mode is TBD
We denote this enabled link as Anchor link and it is in reference to a non-AP MLD
Option 1: Fixed Anchor link
  Negotiated during multi-link setup
Option 2: Dynamic Anchor link
  Dynamically selected by non-AP MLD and not selected a priori
  AP MLD can provide recommendations
AP MLD includes info of basic operation (such as traffic indication, BSS parameter updates, etc.) of all setup links to a non-AP MLD on the anchor link
  Beacons/Probe Responses on anchor link provide other links’ info for this non-AP MLD on anchor link
  Mechanisms to avoid Beacon bloating presented in [3]

## Slide 6: Switching to/from Extreme Low Power MLO Mode
We propose 802.11be shall define fast transition mechanism (e.g. Switch frame) for a non-AP MLD to switch to and from the extreme low-power multi-link operation mode.
  In contrast to sending per-link enable/disable messages and power save mode indication
Switching to extreme low power MLO mode
  Switch frame by non-AP MLD can be transmitted on any enabled link
  Switch frame shall include the Anchor link identifier if the switch frame transmitted on another link
  TID-to-link mapping is updated to all TIDs mapped to the anchor link
Switching out of extreme low power MLO mode
  Option 1: TID-to-link mapping is updated to the mapping prior to switching into extreme low power MLO mode
  Option 2: Non-AP MLD explicitly indicates the TID-to-link mapping in the message for switching out of extreme low power MLO mode

## Slide 7: Summary
Enabling only a single link and activating power save mechanisms is a practical MLO power save mode
Require efficient fast transition mechanism for switching to and from extreme low power MLO mode
Anchor link can be fixedat multi-link setup or dynamically selected by non-AP MLD including recommendations from AP MLD

## Slide 8: Straw Poll #1
Do you support that 802.11be shall define an extreme low power multi-link operation mode for non-AP MLDs?
  Exact name of the mode is TBD
  Details provided in slide 5 and 6

## Slide 9: Straw Poll #2
Which of the following options do you support as default TID-to-link mapping update mechanism for a non-AP MLD switching out of extreme low power MLO mode?
  Option 1: TID-to-link mapping is remapped to the mapping prior to switching into extreme low power MLO mode
  Option 2: Non-AP MLD explicitly indicates the TID-to-link mapping in the message for switching out of extreme low power MLO mode
  Abstain

## Slide 10: References
[1] 11-19-1262-07-00be-specification-framework-for-tgbe
[2] 11-19-1405-07-00be-multi-link-operation-channel-access-discussion
[3] 11-19-0226-00be-mlo-constraint-indication-and-operating-mode

## Slide 11: Straw Poll #3
Do you support that 802.11be shall define a mechanism for switching into and out of extreme low power multi-link operation mode for non-AP MLDs?