## Slide 1: Secure LTF Attacker Simulation
Date: 2020-03-03
Authors:

## Slide 2: PHY Security
Attacker tries to modify the measured range
  Make STA appear closer to AP to fake proximity detection
  Spoof time-stamps t2 or t4 to achieve that
Focus on physical layer attack
  Assume that MAC level is authenticated/encrypted
  Includes time-stamps t1/t4 feedback to initiator

## Slide 3: Integrity Attack Scenario
First line security
  Use secure LTF (sequence unknown to attacker)
  Replace Cyclic Prefix (CP) with zero-padded Guard Interval (to reduce structure)
Attack types
  Replay attack: for both Cyclic Prefix or Guard Interval, attacker repeats first quarter portion of secure LTF with offset
  Brute-force attack: attacker tries to guess the secure LTF
  Noise only: performance in low SNR or attacker caused SINR

## Slide 4: Attacker Type 1
Guard Interval (GI) Replay Attack
  Attacker will listen to first quarter portion of LTF
  Then try to change measured t2 or t4 by re-transmitting the first quarter with timing advance at the end
  Will affect overlap-add based receiver
First quarter
Copy
Waveform for channel measurement
Waveform transmitted by attacker
Timing advance

## Slide 5: Attacker Type 2
Brute Force Attack
  Attacker will try to change measured t2 or t4 by guessing the secure LTF and transmitting with timing advance
  Attack efficacy depends on likelihood of high cross-correlation between sequences A and B
LTF Sequence A
Waveform for channel measurement
Waveform transmitted by attacker
Timing advance
LTF Sequence B

## Slide 6: Attacker Type 3
Performance in Noise
  Even without an attacker the likelihood of triggering a false proximity detection increases with decreasing SNR
  Attacker can send interference to artificially lower SNR
  Used as a baseline to compare effectiveness of attacks
Measures of PHY security
  If brute-force attack achieves no worse performance as noise-only
  If replay attack achieves no worse performance than brute-force

## Slide 7: Example: GI Replay Attack
Setup
  40 MHz, overlap-add receiver
  LTF with random QPSK symbols
  True delay 250 ns
  AWGN Channel
  Attacker delay -33 ns
  0 dB SINR
  Peak appears at -6 dB
  Amplitude normalized

## Slide 8: Receiver FFT Processing
In practice use FFT
  Frequency domain channel
  Typical frequency spacing of
  Signal observed on
LTF 1
Rx Signal
Tx Signal
LTF 2
LTF 1
LTF 2
Guard Interval (GI)
Receiver
Processing
T’ = T+TGI
Channel Spread

## Slide 9: Time Domain Channel Estimates
Frequency domain channel estimate are discrete
Estimate time domain channel, by taking inverse FFT
Always cyclic convolution
  Cyclic with period T, due to frequency spacing of
  Can move attacker to front since FFT window

## Slide 10: Double Size Receiver FFT Processing
Need larger FFT window
  Easiest is double size FFT
  Use frequency spacing of 1/(2T)
  Half samples are original subcarriers
LTF
Receiver
Processing
T’ = T+TGI
Zero
Padding
T-TGI
FFT Window 2T

## Slide 11: Calculation of Signal
Odd subcarriers are
Example

## Slide 12: Tx Signal Spectrum
Spectrum at 1/T spaced subcarriers (QPSK)
Spectrum at 1/(2T) spaced subcarriers (QPSK)

## Slide 13: Secure LTF Modulation
Power on “odd” subcarriers not uniform
  Power random, depends mostly on neighboring subcarriers
  Modulation affects power distribution
BPSK not shown
  Poor security
π/2-BPSK unique
  Less small values
QPSK fairly representative
  Even π/4-QPSK similar

## Slide 14: Secure LTF Channel Estimation
FFT output is not unit norm
  How to best estimate the channel?
  Trade off between channel distortion and noise amplification
Does channel distortion matter?
  Correlator is matched filter (SNR optimal)
  Last presentation showed correlation peak is not affected
  Does distortion matter for MUSIC based first path algos?

## Slide 15: Secure LTF Performance Study
Use IEEE 802.11 channel model ‘D’
  Generated based on underlying 2.5 ns tap quantization
  Interpolated to 320 MHz channel impulse response
  Simulated in complex baseband, up-sampled to 320 MHz
  4x1 Channel, SNR 18 dB
Signal model/receiver
  11ac signal design (pilots/dc/etc), but with GI instead of CP
  Double size FFT, zero padded from T’ to 2T
  Performance base line is using only “even” subcarriers, equivalent to overlap-add (OLA) processing
RTT performance
  Assume symmetric ToA error distribution on both t2/t4
No attacker
  Security performance simulated separately

## Slide 16: Model ‘D’, NLOS, 40 MHz
Correlator has some performance loss
Little difference to QPSK

## Slide 17: Model ‘D’, LOS, 40 MHz
Correlator has small performance loss
Mostly same

## Slide 18: Model ‘D’, NLOS, 80 MHz
Correlator has some performance loss
Little difference to QPSK

## Slide 19: Model ‘D’, LOS, 80 MHz
Correlator has some performance loss
Little difference to QPSK

## Slide 20: Security Study
Use AWGN Channel
  Interpolate Tx signal 4x
  SINR attacker vs signal, SNR noise vs. signal
No attacker
  Look at spurious peaks in noise only
  SNR=0 dB
Brute-force attack
  Attacker “guesses” LTF
  SINR=0 dB, SNR=18 dB
Replay attack
  Re-transmits first quarter of LTF
  SINR=0 dB, SNR=18 dB

## Slide 21: No Attacker : 40 MHz
QPSK – OLA as baseline
Double size FFT has 1 dB gain
π/2-BPSK - similar gain
Less noise amplification loss
noise
amplification
loss
full channel
processing gain

## Slide 22: No Attacker : 80 MHz
Mostly similar to 40 MHz
A bit better than 40 MHz
noise
amplification
loss
full channel
processing gain

## Slide 23: Brute-Force Attack : 40 MHz
QPSK brute-force match noise only
Loss for Inverse+MMSE
π/2-BPSK modulation has 2 dB loss against noise only, little noise ampl.
noise
amplification
loss
noise only
noise only
BPSK
loss

## Slide 24: Brute-Force Attack : 80 MHz
Noise only and QPSK brute-force match
BPSK modulation has 2 dB loss against brute-force attack
noise
amplification
loss
noise only
noise only
BPSK
loss

## Slide 25: Replay Attack : 40 MHz
Correlator almost completely suppresses attacker
Both MMSE and Inverse better than equivalent noise only
attacker
canceled
unmitigated
attack
attacker
equal
to noise

## Slide 26: Replay Attack : 80 MHz
Both Inverse and MMSE better
Less improvement over 40 MHz
attacker
equal
to noise
attacker
canceled
unmitigated
attack

## Slide 27: Conclusion
Presented results for secure LTF
  Modulation types QPSK and π/2-BPSK
  Three channel estimators, Correlator, Inverse, and MMSE
Location estimation performance
  For FFT peak finding algos no significant impact in any case
  For MUSIC based algos, some loss with Correlator
Attacker resilience
  π/2-BPSK has 2 dB loss for brute-force attack, but less noise amplification with both inverse and MMSE
  Both modulation reject replay attack below equivalent noise level

## Slide 28: PAPR Study
PAPR for random QPSK modulated LTF
PAPR for Golay 8PSK modulated LTF

## Slide 29: Performance of Golay Sequence
Brute force attacker, 0 dB SINR