## Slide 1: On Brute Force Attack to 11z Secured Mode
Date: 2020-03-06

## Slide 2: Background
A concern was raised as to the strength of the secured mode against time-domain brute force (computational intensive) attack at the sub-symbol level
This submission addresses the concern related to CID 3911

## Slide 3: Content
Recap of 11az secured mode
Recap of the brute force attack
Requirements of the attack
Implementation specific solutions

## Slide 4: PHY Level Protection (1/2)
Protection is achieved by sounding signal randomization and consistency check
Large sets of randomized sounding signals are generated e.g. 2×109 and 8×1012 for 20 and 160 MHz channels, respectively
  Randomized sounding symbols vary from symbol to symbol
  The randomization is on both frequency and time domains i.e. 8PSK modulation and random CSD
Legacy portion
HE portion

## Slide 5: PHY Level Protection (2/2)
Receiver checks whether the channels estimated from multiple sets of sounding symbols are the same
If the attack signal is not the genuine sounding signal, it generates fake channel arrivals widely spread in the time domain. Furthermore, the fake channel arrivals vary from sounding to sounding because the attack signal can’t follow the sounding signal variation consistently
Spoofed 1st tap
True 1st tap
Noise level
True 1st tap
Noise level
With Legacy LTF symbols
With random sounding symbols
Concentrated, high power spoofed taps
Suppressed, low power spoofed taps

## Slide 6: Brute Force Attack
Attacker detects which sounding signal is being sent by analyzing the beginning portion of the signal
Once detected, attacker sends the remaining portion of the sounding signal ahead of the genuine transmitter
S(2x109)
t(2x109)
S(k)
t(k)
S(1)
t(1)
…
S(k)
t(k)
…
Billions or trillions of correlators
Find the matched signal and send the latter portion with a time shift

## Slide 7: Remarks
Listen before attack
  The transmitted attack signal is always partial i.e. missing the beginning portion
Inherent problem for OFDM
  There are other ways to attack OFDM sounding signal

## Slide 8: Requirements of the Attack
Detection rate needs to be high e.g. 50%. Otherwise, consistency check catch the attack e.g. after 8 repetitions
Received signal needs to be interference-free and distortion-free. Otherwise, detection rate gets affected
  Result in visible horn antennas
High complexities e.g. billions or trillions of correlators are needed to meet the stringent delay requirement
  Check 2×109 ~ 8×1012 sequences within few microseconds e.g. 4×10-6 seconds
  For example, 1.6×1016 ~ 6.4×1020 multiplications per second

## Slide 9: Requirements of the Attack (2/2)
Synchronize to the attenuated, received signal
Handle the unknown windowing function
Time
Windowing function unknown to the attacker
Align the attenuated and tampered signal with the stored sequences

## Slide 10: Fending off the Attacker
There are simple ways against the attack without changing 802.11az spec
The Transmitter can introduce interferences, distortions, and fake sounding signal to the beginning portion of the sounding signal
The Receiver can identify the partial sounding signal transmitted by the attacker and trigger an alert

## Slide 11
Example of adding one delayed signal [1]
Signal 1
Signal 2
Signal 3
Signal 4
HE-STF
Signal 1’
Signal 2’
Signal 3’
Signal 4’
HE-STF
TX antenna 1
β •
•
Signals shifted by linear delay
TX power splitting and random phase rotation
March 2020

## Slide 12
No effect to time of arrival measurement
Since the delayed transmission only introduces multipaths after the first channel arrival, it doesn’t affect the time of arrival (ToA) estimation
β
Multipaths for TX signal
not delayed
Estimated multipaths
Multipaths for TX signal
delayed
Delay
ToA
ISI Introduced by Transmitter (2/3)
March 2020

## Slide 13
ISI Introduced by Transmitter (3/3)
The introduced ISI makes the received signal does not match with any of the signals stored in the correlators
The attacker needs to jointly estimate the sounding signal and the introduced phases, magnitudes, and delays for removing the ISI with a multiplied complexity
The attacker can not use the legacy LTF to estimate the introduced phases, magnitudes, and delays for removing the ISI because the delayed transmissions are not applied to the legacy LTF
Legacy portion
HE portion

## Slide 14
March 2020
Time
Zero power CP
Intended sounding signal
Preceding, covering sounding signal that the attacker locks on
A fake sounding signal different from the intended one is sent ahead of the intended one such that the attacker locks onto the fake for the sequence search

## Slide 15
Detecting List-before-Attack Type of Attacks
The attack signal generating the fake first channel arrival is always incomplete i.e. missing the beginning portion
Receiver can detect the incompleteness of the signal corresponding to the first channel arrival and trigger an alert [2]
s(k)
t(k)
t(k)
Genuine signal
Attack signal

## Slide 16
Recap of Attack Detection (1/2)
Receiver estimates the channel assuming sounding signals are complete
Estimated channel arrivals below noise/interference level are removed
s(k)
t(k)
t(k)
Genuine signal
Attack signal
s(k)
t(k)
Received superimposed signal
Estimated channel
t(k)
Noise/interference level
Fake 1st arrival
Genuine 1st arrival

## Slide 17
Received signal is reconstructed using the estimated channel arrivals above threshold
The reconstructed signal is subtracted from the received signal
Large residual triggers an alert
S(k)
t(k)
Received superimposed signal
Estimated channel above threshold
t(k)
Fake 1st arrival
Genuine 1st arrival
S(k)
t(k)
Reconstructed received signal
t(k)
S(k)
Noise/interference level
Large residual
Residual signal after subtraction
Recap of Attack Detection (2/2)

## Slide 18: Conclusion
The feasibility of the attack is questionable
  Use of horn antennas
  Access to Wi-Fi PHY
  Ability to make architecture HW changes to incorporate a huge amount of correlators and feed into transmission
  Cost of HW development (how many GFLOPs ?)
There are low cost ways to deal with the attack
  Transmitter sends covering signal protecting the beginning portion of the sounding signal
  Receiver identifies the presence of partial attack signal
  Solutions are proprietary without any spec change

## Slide 19: Reference
[1] Qinghua Li, Feng Jiang, Jonathan Segev, et al., “On Unintentional Beamforming,” IEEE 802.11-19/2032r4
[2] Feng Jiang, Qinghua Li, Jonathan Segev, et al., “Replay Attack Detection Using LTF with Zero Prefix,” IEEE 802.11-18/0208r0
[3] Apple Inc., “Computational Attacks on 11az PHY Secure Ranging.”

## Slide 20: Backup

## Slide 21: Other considerations…(even without considering 11az changes)
The requirement on the attacker are quite high:
  Attack cost: non-recurring cost
    Attacker has to have access to 802.11ax PHY.
    Attacker has to be able to make HW architecture and FW changes to 802.11ax PHY to support:
      Insertion of sampler at the correct timing reading of the Ranging NDP frame Legacy and HE portions.
      HW and memory to compute of correlators of brute force (including 109 sequences storing for 20MHz, >1012 for 160MHZ).
      Injection of synthesized symbol with highest correlation back into Tx path with Timing Advance control mechanism
  Attack cost: recurring
    Attacker relies on LOS assuming AWGS flat channel.
    Most likely would have to use horn antennas (physically large and expensive)

## Slide 22: Other considerations…
Reduced set brute force correlator (reduced computation):
  In [3] the author proposes to simplify the computation by trying only 1/100 reducing computation to 1% at the expense of success rate reduced to 1%.
  This approach is fallacy from attacker side:
    11az support multi LTF symbol per frame each LTF symbol sequence is independent,
    Reduced brute force attack can easily be fended off using 11az Repetition.
    Repetition = 2 will yield 1/104 probability, repetition of 3 will yield 1/106 ,repetition 4 will yield 1/108 effectively making the attack negligible at almost no medium cost (8usec per repetition to maximum of 64).