## Slide 1: Multi-link Setup Follow Up II
Date: 2020-03-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang |  |  |  | 
Laurent Cariou |  |  |  | 
Daniel F Bravo |  |  |  | 
Arik Klein |  |  |  | 
Danny Alexander |  |  |  | 
Danny Ben-ari |  |  |  | 
Ghosh Chittabrata |  |  |  | 
Notes: September 2012

## Slide 2: Background
Multi-link setup has a lot of progress, and we try to progress on the remaining items
  Allow only one STA in MLD framework
  Container for multi-link setup
  Differentiation with STA level association
  Relation with Authentication request/response

## Slide 3: MLD framework
It is TBD for a MLD to have only one STA in IEEE MLD definition
Multi-link device (MLD): A device that has more than one affiliated STA and has one MAC SAP to LLC, which includes one MAC data service.
NOTE 1 – The device can be logical.
NOTE 2 – It is TBD for a MLD to have only one STA.
NOTE 3 – Whether the WM MAC address of each STA affiliated with the MLD is the same or different is TBD.

## Slide 4: Why allow only one STA in MLD framework
In a special case, only one link may be setup for whatever implementation specific reasons, which is not allowed in the current SFD
Allowing one STA in MLD framework enables a non-AP MLD to setup only one link using the same framework
There are confusions about number of links being setup and capability, and that has been clarified in previous motion

## Slide 5: Proposal
Multi-link device (MLD): A device that has one or more more than one affiliated STA and has one MAC SAP to LLC, which includes one MAC data service.
NOTE 1 – The device can be logical.
NOTE 2 – It is TBD for a MLD to have only one STA.
NOTE 3 – Whether the WM MAC address of each STA affiliated with the MLD is the same or different is TBD.

## Slide 6: Container for Multi-link Setup
We think it is reasonable to reuse the container of legacy association for various multi-link setup
  Reuse association request/response for multi-link setup request/response
  Reuse disassociation for multi-link teardown
  Reuse Reassociation request/response for multi-link resetup request/response
  Reuse authentication request/response for multi-link SAE exchange and multi-link Open System authentication
Reasons:
  Multi-link advertisement is done through a new element based on the IEEE motion rather than a new frame, which enables us to reuse existing frame
  BA negotiation reuses ADDBA request/response
  4-way handshake reuses EAPOL
  It seems that we decide not to use the frame to differentiate multi-link operation

## Slide 7: Example of Multi-link Resetup: Change Configuration of existing MLD

## Slide 8: Example of Multi-link Resetup: Move to another AP MLD
AP
1
AP
2
AP MLD 1
EHT non
-
AP
Non
-
AP MLD
Multi
-
link setup request
Multi
-
link setup response
EHT non
-
AP
2
AP
1
AP
2
AP MLD 1
EHT non
-
AP
EHT non
-
AP
2
Link
1
Link
2
Non
-
AP MLD
AP
2
.
1
AP
2
.
2
AP MLD
2
EHT non
-
AP
Non
-
AP MLD
Multi
-
link resetup request
Multi
-
link resetup response
EHT non
-
AP
2
AP
2
.
3
EHT non
-
AP
3
AP
2
.
1
AP
2
.
2
AP MLD
2
EHT non
-
AP
Non
-
AP MLD
EHT non
-
AP
2
AP
2
.
3
EHT non
-
AP
3
Link
1
Link
2
Link
3

## Slide 9: Ambiguity of Multi-link Setup between two MLDs
There maybe an ambiguity of differentiating STA level setup (legacy association) or MLD level setup when we reuse association request/response
Proposal:
  for an association request sent by an EHT non-AP STA affiliated with an non-AP MLD to another EHT AP affiliated with an AP MLD, the association request shall be treated as multi-link setup request

## Slide 10: Relation with Authentication request/response
We agree to exchange MLD address during ML setup.
Under SAE, we agree to use MLD address to compute key, so exchange MLD address during authentication request/response is also needed.
  AP that supports SAE also needs to advertise MLD address in Beacon and probe response.
Since links are setup after multi-link setup, same link is used for authentication request/response exchange and multi-link setup request/response exchange

## Slide 11: Conclusion
We propose the following to further progress on the topic of multi-link setup:
  Allow only one STA in MLD framework
  Reuse current container for setup, resetup, teardown, authentication
  Clarify that between two MLDs, there is only one mode of setup operation
  Clarify MLD address indication under SAE method

## Slide 12: Straw Poll #1
Do you support the following?
  Reuse association request/response for multi-link setup request/response
  Reuse disassociation for multi-link teardown
  Reuse Reassociation request/response for multi-link resetup request/response
  Reuse authentication request/response for multi-link SAE exchange and multi-link Open System authentication
  for an association request sent by an EHT non-AP STA affiliated with an non-AP MLD to another EHT AP affiliated with an AP MLD, the association request shall be treated as multi-link setup request

## Slide 13: Straw Poll #2
Do you support the following?
  An AP that is part of an AP MLD that supports SAE authentication shall include the MLD address in beacon and probe response frames it transmits.
  EHT MLD shall indicate its MLD MAC address during authentication request/response exchange
  Same link is used for authentication request/response exchange and multi-link setup request/response exchange

## Slide 14: Straw Poll #3
Do you support to revise the following paragraph in 11be SFD as follows:
  Multi-link device (MLD): A device that has one or more more than one affiliated STA and has one MAC SAP to LLC, which includes one MAC data service.
  NOTE 1 – The device can be logical.
  NOTE 2 – It is TBD for a MLD to have only one STA.
  NOTE 32 – Whether the WM MAC address of each STA affiliated with the MLD is the same or different is TBD.