## Slide 1: Thoughts on RU Aggregation and Interleaving
Date: 2020-03-05
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
We have made good progress on RU aggregation design
  Encoding structure
    For each STA, there is only PSDU per link
    For LDPC, there is only one encoder for each PSDU
  RU aggregation rules and supported combinations
    Small RU combinations (e.g. RU 26+52, 26+106) and large RU combinations (e.g. RU484+242)
This presentation will discuss the interleaving schemes for RUs and aggregated RUs

## Slide 3: High Level Thoughts
For RU and aggregated RU BW < = 80MHz, prefer joint interleaving within RU and aggregated RU for better diversity
  Reuse existing Dtms for existing size RU
  Define new Dtm for each aggregated RU within 80MHz
For RU and aggregated RU BW > 80 MHz, two options
  Option 1: New Dtm for each RU and aggregated RU size
  Option 2: 80MHz segment parser + interleaving within 80MHz

## Slide 4: New Dtm for RU Aggregation within 80 MHz
Dtm only depends on the combined RU size, regardless of the location and size of each RU
  E.g. RU242+242(=20MHz+20MHz) and RU484 (=40MHz) will use same Dtm
Within 80MHz, need to define new Dtm for the cases of
  RU26+52 and RU26+106 for small RU aggregation
  RU484+242 for large RU aggregation
Dtm design is directly related to the number of combined data tones from RU aggregation.
  Need to first decide # of pilots after aggregation, remaining will be data tones

## Slide 5: New Dtm for Small RU Aggregation
Propose to keep all the pilot tones for small RU aggregation
  Only 2/4/4 pilots go with small RU26/52/106. Changing 1or 2 pilot tones to data doesn’t provide much gain.
Optimal Dtm value choice is generally proportional to BW and insensitive to small variation
Dtm design for RU26+52 = A-RU 78
  # of pilots = 2+4=6 and # of data tones =72=18*4
  Preferred interleaving parameters: Dtm=4, Ncol=18
Dtm design for RU26+106 = A-RU132
  # of pilots = 2+4=6 and # of data tones = 126=2*3*3*7
  Preferred interleaving parameters: Dtm=6, Ncol=21
RU Size | NSD | NCOL | DTM
26 | 24 | 24 | 1
52 | 48 | 16 | 3
78 | 72 | 18 | 4
106 | 102 | 17 | 6
132 | 126 | 21 | 6
242 | 234 | 26 | 9

## Slide 6: RU484+242: Dtm Design
RU484+242 = A-RU726
  # of data tones = 702=2*3*3*3*13
  Preferred interleaving parameters: Dtm=18
RU Size | NSD | NCOL | DTM
26 | 24 | 24 | 1
52 | 48 | 16 | 3
78 | 72 | 18 | 4
106 | 102 | 17 | 6
132 | 126 | 18 | 7
242 | 234 | 26 | 9
484 | 468 |  | 12
726 | 702 |  | 18
996 | 980 |  | 20

## Slide 7: Interleaving for >80 MHz RU
Option 1: New Dtm for each aggregated RU BW
  There are many of them
  Moreover, for some aggregated BW like 120MHz, RU484+996 and RU (484+242)+RU (484+242) have different number of data tones so need to define multiple Dtms
Option 2: per 80MHz segment parser + joint interleaving within 80MHz
  Diversity benefit from joint interleaving over 80MHz segment is minor, especially with more antennas
  Compliant with existing 11ac/ax per 80 MHz segment parser design. However, due to potential puncturing, each 80 MHz segment may contain different number of bits. Segment parser design needs to be revised to support this
  We prefer this approach

## Slide 8: Three Options of 80 MHz Segment Parser
Sequential parser
  For each OFDM symbol, assign the coded bits to the 1st 80MHz segment first. After it fills up, move on to the 2nd 80MHz segment, and so on
Round robin parser
  Round robin even distribution bits among all 80MHz segments: NBPSCS/2 coded bits to 80MHz segment 1 followed by NBPSCS/2 to 80MHz segment 2, etc. When a smaller 80MHz segment fills up, all the remaining bits are further round robin distributed among remaining larger segments
Proportional round robin parser
  Similar to the round robin, except there is allocation ratio, mi, among different 80MHz segment
  (NBPSCS/2) m1 coded bits to 80MHz segment 1 followed by (NBPSCS/2)m2 to 80MHz segment 2, etc. If an 80MHz segment fills up, all the remaining bits are proportionally round robin distributed with the same ration among remaining segments
Expect proportional round robin scheme has the best performance due to most evenly distribution of bits

## Slide 9: Summary
Interleaving schemes for 11be are discussed
We propose
  Joint interleaving for RU and aggregated RU with BW<= 80 MHz
    New Dtm values for RU26+52, RU26+106 and RU 242+484
  Per 80MHz segment parser for RU and aggregated RU with BW > 80MHz

## Slide 10: Straw Poll 1
Do you support joint interleaving for RU and aggregated RU size <=80 MHz
  Y
  N
  A

## Slide 11: Straw Poll 2
Do you support the new LDPC interleaver parameter for RU52+26, RU106+26 and RU484+242
  Y
  N
  A
RU Size | NSD | DTM
26 | 24 | 1
52 | 48 | 3
78 | 72 | 4
106 | 102 | 6
132 | 126 | 6
242 | 234 | 9
484 | 468 | 12
726 | 702 | 18
996 | 980 | 20

## Slide 12: Straw Poll 3
For RU or aggregated RU size > 80MHz, do you support using per 80MHz segment parser?
  Y
  N
  A

## Slide 13: Straw Poll 4
Do you agree the segment parser bit distribution sequence starts from the lowest frequency location to the highest frequency, just like in 11ac/ax?
  Y
  N
  ABS