## Slide 1: Sequence number and BA operation with larger BA buffer size
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Large BA Buffer Size and Large MPDU Number in A-MPDU
>160MHz BW, >8 Nss and the future extensions (x8 increase @ 320MHz+16 SS+2 links) mean that the larger A-MPDU size, larger BA TX buffer, longer scoreboard context bitmap, and larger BA reorder buffer are required:
  Option 1: <=1024 BA buffer size and <=1024 MSDUs/A-MSDUs within an A-MPDU (x 4 of 256 BA).
    New BA variant to support <=1024 BA bitmap (new 512, 1024 bitmaps).
      Alternatively the maximal BA bitmap can be <= 256 and multiple Block Ack Bitmaps can be used for a TID of a recipient.
  Option 2: <=2048 BA Buffer size and <=2048 MSDUs/A-MSDUs within an A-MPDU (x 8 of 256 BA).
    New BA variant to support <=2048 BA bitmap, updated scoreboard context control rules (new 2048 bitmap).
      Alternatively the maximal BA bitmap can be <= 256 and multiple Block Ack Bitmaps can be used for a TID of a recipient.
  Option 3: <=4096 BA Buffer size and <=4096 MSDUs/A-MSDUs within an A-MPDU (x16 of 256 BA) (new 4096).
    New BA variant to support <=4096 BA bitmap additional sequence number bits in BA, updated scoreboard context control rules.
      Alternatively the maximal BA bitmap can be <= 256 and multiple Block Ack Bitmaps can be used for a TID of a recipient.
      The BA can carry partial sequence number bits, e.g. 12-bit LSB sequence number.
    BAR format change to carry the additional sequence number bits.
    Additional sequence number bits in QoS Data frames.
  We are ok with option 1.

## Slide 3: Methods to Indicate New BA Bitmap Length
The Fragment Number field in Block Ack Starting Sequence Number Control indicates the additional BA Bitmap length of 512, 1024 in Compressed BA, unicast Multi-STA BA, or Multi-STA BA in EHT PPDU.

## Slide 4: Methods to Decrease BA Overhead
Instead of non-HT duplicated PPDU to carry BA, wider BW VHT/HE/EHT PPDU can be used to carry the BA.
  The TXOP holder that transmits the BA in a PPDU other than non-HT duplicated PPDU may transmit CF-End in non-HT duplicated PPDU if there is no other frame exchange in the TXOP.
  This is suitable in BSS with wider operating BW, e.g. in 5/6GHz band.

## Slide 5: Methods to Decrease BA Overhead
Shorter Block Ack Bitmap can be used if the sequence number difference of the acknowledged QoS Data frames are smaller, e.g.
  256-bit Block Ack Bitmap can be used when the negotiated BA buffer size is 1024, and the acknowledged QoS Data frames are 255 frames from Sequence Number 1000 to 1254.
When a BAR whose Starting Sequence Control field has a value (Value1) larger than WinStartB and WinStartR is used to solicit the Block Ack, the future transmitted QoS Data frame with Sequence Number that are smaller than Value1 can’t be correctly acknowledged per scoreboard context and discarded in reorder buffer. The following rules can solve the issue:
    For block ack agreement that is not a protected block agreement:
      Treat BAR same as in protected block ack agreement, or
      Redefine BAR: the initiator of BAR can indicate whether it wants the recipient of BAR to shift the WinStartB and WinStartR or not.

## Slide 6: Methods to Decrease BA Overhead (Cont’d)
Multiple Block Ack Bitmaps for a TID of a recipient can also decrease the BA length in some cases.
  In the case where the negotiated BA agreement has 768 BA buffer size and the allowed lengths of Block Ack Bitmap field include 32, 64, 128, 256, 512, 1024, 2048, two Per AID TID Info fields with 256-bit Block Ack Bitmap and 512-bit Block Ack Bitmap can decrease the BA length.
    Three Per AID TID Info fields with 256-bit Block Ack Bitmap can decrease the BA length.
  In a Multi-STA BA that are addressed to 11ax STAs and the EHT STAs that negotiated >256 BA buffer size, multiple Per AID TID Info fields with 256-bit Block Ack Bitmap for a TID of a EHT STA may be required.
    Otherwise 11ax STAs may not be able to decode the Per AID TID Info fields in the Multi-STA BA.
    An alternative solution is that in a Multi-STA BA a Per AID TID Info field with >256-bit Block Ack Bitmap is after the Per AID TID Info fields with <=256-bit Block Ack Bitmaps.
  This can also be used for differentiating the bitmaps from different links if required.

## Slide 7: Methods to Decrease BA Overhead (Cont’d)
Partial all 1s acknowledgement can be used to decrease the Multi-STA BA size.
  A QoS frame is acknowledged by a Multi-STA BA frame if the following conditions are true:
    three Per AID TID Info fields whose AID11 and TID are same respectively are continuously placed in the Multi-STA BA,
    The Ack Type of the first Per AID TID Info field and The Ack Type of the third Per AID TID Info field are 0 (with BA Bitmap).
    The Ack Type of the second Per AID TID Info field is 1 (without BA Bitmap and Block Ack Starting Sequence Control).
    The sequence number of the frame is no less than the sum of the value in Starting Sequence Number field of the first Per AID TID Info field and the length of Block Ack Bitmap in bits.
    The sequence number of the frame is less than the value in Starting Sequence Number field of the third Per AID TID Info field.
2
32
2
2
32
2
2
Sequence Number field is 0
256-bit Block ck Bitmap
Sequence Number field is 800
The QoS Data frames with sequence number od 256 to 799 are correctly received.
Per AID TID Info fields with same values in AID11 fields and same values in TID fields

## Slide 8: Methods to Decrease BA Overhead (Cont’d)
Partial All 0s acknowledgement:
  A QoS frame are not acknowledged by the Multi-STA BA frame if the following conditions are true:
    Two Per AID TID Info fields whose AID11 and TID are same respectively are continuously placed in a Multi-STA BA,
    The Ack Type of the first Per AID TID Info field and The Ack Type of the second Per AID TID Info field are 0 (with BA Bitmap).
    The sequence number of the frame is no less than the sum of the value in Starting Sequence Number field of the first Per AID TID Info field and the length of Block Ack Bitmap in bits.
    The sequence number of the frame is less than the value in Starting Sequence Number field of the second Per AID TID Info field.
2
32
2
32
Sequence Number field is 0
256-bit Block ck Bitmap
Sequence Number field is 800
Per AID TID Info fields with same values in AID11 fields and same values in TID fields

## Slide 9: Straw Poll 1
Do you support that an EHT STA can carry BA frame in wider BW PPDU other than non-HT PPDU to decrease the BA transmission overhead?
  The wider BW follows the responding BW rules.

## Slide 10: Straw Poll 2
Do you support that in a Multi-STA Block Ack frame, multiple consecutive Per AID TID Info fields with the same TID can be addressed to the same recipient (same AID). In this case, their bitmaps are concatenated to form a contiguous bitmap of 512 or 1024 for the recipient.
  The SSN, except the one in the first Per AID TID Info field, may be ignored by the recipient.

## Slide 11: Straw Poll 3
Do you support that for block ack agreement that is not a protected block agreement, the initiator of BAR can indicate whether it wants the recipient of BAR to shift the WinStartB and WinStartR or not?