## Slide 1: Preamble puncture indication for non-OFDMA transmission
Date: 2020-03-13
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Yan Xin | Huawei |  |  | 
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 
Rob Sun | Huawei |  |  | 
Junghoon Suh | Huawei |  |  | 
Osama Aboul-Magd | Huawei |  |  | 

## Slide 2: Introduction and Recap
RU allocation subfield is not needed for non-OFDMA transmission, including both SU and MU-MIMO transmissions.
For punctured non-OFDMA transmissions, MRU aggregation indication is equivalent to preamble puncture indication.
In [1], the author has a very good summary of the punctured patterns that have passed the motion so far. And provide 3 options for preamble puncture indication.
In this contribution, we will share our view on how to indicate preamble puncture information for non-OFDMA cases.

## Slide 3: Preamble puncture patterns
As mentioned in [1], the following patterns have passed the motion assuming P20 is not punctured:
Mode | Aggregated BW | Description
1-6 (6) |  | 20/40/80/80+80 or 160/240 or 160+80/160+160 or 320
7-9 (3) | 60MHz | 1x11, 11x1, 111x
10-12 (3) | 120MHz | 11xx1111, 1111xx11, 111111xx
13-19 (7) | 140MHz | 1x111111, 11x11111, …, 1111111x
20-21(2) | 160Mhz | 1111 xxxx 1111, 1111 1111 xxxx
22-26(5) | 200Mhz | 11xx 1111 1111, 1111 xx11 1111, …, 1111 1111 11xx
27-29(3) | 240Mhz | 1111 xxxx 1111 1111, 1111 1111 xxxx 1111, 1111 1111 1111 xxxx
30-36 (7) | 280MHz | 11xx 1111 1111 1111, …, 1111 1111 1111 11xx

## Slide 4: Preamble puncture patterns
There are several other mode with one hole or two holes[2-3], which we think are also very important for high dense scenarios [4], or 6GHz or DFS channels.
PPDU BW | Agg. BW | Combinations | Notes
80 MHz | 40 | 20+20 (1xx1) | One hole of 40MHz
160 MHz | 100 | 40+(40+20) | One hole of 60 MHz Two holes: 40 MHz and 20 MHz
 | 120 | (20+20)+80 | One hole of 40 MHz
 |  | (40+20)+(40+20) | One hole of 40 MHz Two holes of 20 MHz each
240 MHz | 220 | 140+80 | One hole of 20MHz
 | 200 | 140+60 | Two holes: 20 MHz each One hole: 40 MHz
 | 180 | 120+60 and 140+40 | Two Holes: 40MHz and 20Mhz One hole: 60MHz

## Slide 5: Preamble puncture patterns
More modes:
Hence, a indication method which can support a more flexible and efficient usage of spectrum resource with simple implementation on the indication of puncture patterns is preferred.
PPDU BW | Agg. BW | Combinations | Notes
320 MHz | 300 | 160+140 | One hole of 20MHz
 | 280 | 140+140 | Two 20 MHz holes One 40MHz hole
 | 260 | 140+120 and 160+100 | Two holes: 20 and 40MHz; One hole: 60 MHz
 | 240 | 120+120 | Two holes: 40MHz each One hole: 80 MHz

## Slide 6: Preamble puncture indication
Opt1: bitmap - a most flexible and straightforward method
  16-bit, 12-bit and 8-bit bitmaps for respective 320MHz, 240MHz and 160 MHz BWs
  unavailable 20MHz spectrum shall not cross the 20MHz channel boundary
  484-tone RUs shall not cross the 40MHz and 80MHz boundaries
  996-tone RUs shall not cross the 80MHz boundary
  RUs to be aggregated are indicated in a straightforward way with simple implementation. No look-up table is needed to be implemented and stored to indicate flexible RU combinations.
Examples of bit map indication are shown as below:
  one hole of 20 MHz in 320 MHz (bit map: 10111111111111)
  two holes of 20 MHz and 40 MHz in 320 MHz (bit map: 1011001111111111)

## Slide 7: Preamble puncture indication
Opt2: RU segment - another flexible and straightforward method
RU aggregation can be indicated with a series of RU segments in an order, which are arranged
from the start to the end of the operating channel bandwidth. Each RU segment represents a 242-,
484- or 996-tone RU.
RU availability | RU size | Bit representation for RU segment
Unavailable | 242 | 00
Available | 242 | 01
Available | 484 | 10
Available | 996 | 11
  - 16-bit, 14-bit and 12-bit bitmaps for respective 320MHz, 240MHz and 160 MHz BWs
  - unavailable 20MHz spectrum shall not cross the 20MHz channel boundary
  - 448-tone and 996-tone RUs shall not cross the 80MHz boundary
  - RU segment indication is per 80 MHz basis. Indication of RU aggregation for bandwidth
  larger than 80 MHz (e.g., 320 MHz) can be a concatenation of indications for 80 MHz.
  - RUs to be aggregated are indicated in a straightforward way with simple implementation.
  Only a two-bit RU segment indication table is needed for flexible RU combinations.

## Slide 8: Preamble puncture indication
Opt2: RU segment - another flexible and straightforward method (cont’d)
Examples of RU segment indication are shown as below:.
- One hole of 20 MHz in 320 MHz (16-bit representation: 0100101111110000)
- Two holes of 20 MHz each in 320 MHz (16-bit representation: 0001101110010011)
- One hole of 60 MHz in 320 MHz (16-bit representation: 1111010000001100)

## Slide 9: Preamble puncture indication
Opt3: Since RU allocation subfield has 8 bit, a method would be use this 8 bit to indicate the puncture pattern.
The following method is proposed, there exists two subfields, each one is used to indicate one punctured hole in one of the 160MHz:
An example is shown as below:
Puncture indication for 1st 160Mhz (4 bit) | Description | Entries
0-7 | 20MHz is punctured | 8
8-11 | 40MHz is punctured | 4
12-13 | 80MHz is punctured | 2
14 | No puncture | 1
15 | Reserved | 1
Puncture indication for 2st 160Mhz (4 bit) | Description | Entries
0-7 | 20MHz is punctured | 8
8-11 | 40MHz is punctured | 4
12-13 | 80MHz is punctured | 2
14 | No puncture | 1
15 | Reserved | 1
Indication:
0000
0010

## Slide 10: Preamble puncture indication
The two table method allows a very simple logic/very small-size tables. And the preamble puncture indication occupies the same bits as the RU allocation subfield.
The two table can also be used for 160MHz and 80MHz separately when BW=240MHz, and for 80MHz and 80MHz when BW=160MHz.
Puncture indication for 1st 80Mhz (4 bit) | Description | Entries
0-3 | 242-tone RU is punctured | 4
4-6 | 484-tone RU is punctured (including middle 484-tone RU) | 3
7 | 996-tone RU is punctured | 1
8 | No puncture | 1
9-15 | Reserved | 7
Puncture indication for 2st 80Mhz (4 bit) | Description | Entries
0-3 | 242-tone RU is punctured | 4
4-6 | 484-tone RU is punctured (including middle 484-tone RU) | 3
7 | 996-tone RU is punctured | 1
8 | No puncture | 1
9-15 | Reserved | 7

## Slide 11: Preamble puncture indication
The proposed method can be used for both EHT-SIG and trigger frame:

## Slide 12: Summary
Three simple methods for preamble puncture indication are considered.
Bitmap is the most flexible and straightforward indication method.
RU segment approach uses a multiple of 2 bits to indicate the available/unavailable RU segments per 80 MHz basis.
The two table method allows a very simple logic/very small-size tables. And the preamble puncture indication occupies the same bits as the RU allocation subfield.

## Slide 13: Straw Poll #1
Do you support for 11be, there shall exist at least one puncture pattern with two holes across the PPDU bandwidth?

## Slide 14: Straw Poll #2
Do you support the preamble puncture indication method as follows?
  There exists two subfields, when BW =320Mhz, each one is used to indicate one punctured hole in one of the 160MHz;
  when BW = 240Mhz, one is used to indicate one punctured hole in the 160MHz, the other is used to indicate one punctured hole in the other 80Mhz;
  when BW = 160Mhz, each one is used to indicate one punctured hole in one of the 80MHz.
  Y
  N
  A

## Slide 15: Straw Poll #3
Do you support the bitmap method described above for RU aggregation indication?
  Y
  N
  A

## Slide 16: Straw Poll #4
Do you support the RU segment method described above for RU aggregation indication?
  Y
  N
  A

## Slide 17
[1] 11-20-0285-01-00be-su-ppdu-sig-contents-considerations
[2] 11-20-0048-00-00be-ru-aggregation-for-240mhz-and-320mhz
[3] 11-19-1908-04-00be-multi-ru-support
[4] 11-19-1190-03-00be-improved-preamble-puncturing-in-802-11be
References