## Slide 1: LDPC Tone Mapper for Multiple RU Aggregation
Date: 2020-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
TGbe agreed on the following texts
  “Only allowed small-RU combinations are RU106+RU26 and RU52+RU26”
  “For LDPC coding, for combined RUs sent to a user with RU size less than 242-tone, a single tone mapper shall be used”
In this contribution, we propose LDPC tone mapping distances for small-RU combinations
To this end, we evaluate PER performances for various tone mapping distances

## Slide 3: LDPC Tone Mapper
In 11ax, LDPC tone mapping distance for each RU is defined as follows
Given the values above and the number of pilots for each RU, we can select the candidates for DTM and DTM_DCM of 26+52 and 26+106 combinations as follows
  Note that NSD is 72 and 126 for 26+52 and 26+106, respectively, assuming the same number of pilots as in 11ax
 | 26+52 | 26+106
DTM | 3,4,6 | 6,7,9
DTM_DCM | 1,2,3 | 3,7,9

## Slide 4: Simulation Assumptions
Channel model: TGnD NLoS
Data size: 200 Bytes
Antenna technology
  SISO without or with DCM
  4x2 MIMO, 2 spatial streams without DCM
MCS
  Without DCM: MCS0, MCS1, MCS3, MCS5
  With DCM: MCS0, MCS1, MCS3
Ideal feedback for MIMO beamforming
No hardware impairments

## Slide 5: Simulation Results (1/3)
26+52 without DCM
SISO
MIMO

## Slide 6: Simulation Results (2/3)
26+106 without DCM
SISO
MIMO

## Slide 7: Simulation Results (3/3)
With DCM
SISO
SISO
26+52
26+106

## Slide 8: Discussion
We don’t see any big performance difference among different tone mapping distances in each MCS for both 26+52 and 26+106 combinations with or without DCM
We propose unified LDPC tone mapping distances for small RU combinations which may be beneficial to implementation
  Note that these values are also the same as those of 106-tone RU
 | 26+52 | 26+106
DTM | 6 | 6
DTM_DCM | 3 | 3

## Slide 9: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  LDPC tone mapping distance for small-RU aggregation
Y/N/A: //
 | 26+52 | 26+106
DTM | 6 | 6
DTM_DCM | 3 | 3