## Slide 1: Prioritized EDCA Channel Access Over Latency Sensitive Link(s) In MLO
Date: 2020-03-09
Authors:
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook Inc. | 1 Hacker way, Menlo Park, CA |  | chunyuhu@fb.com

## Slide 2: Abstract
Multi-link operation (MLO) as part of key 11be features enables flexible traffic steering and load balancing
This contribution proposes:
  Differentiated services over MLO, specifically, support of one or a subset of links allocated for latency sensitive traffic*, known as:  Latency Sensitive Link(s)
  Prioritized EDCA channel access over latency sensitive links
  * While the main traffic carried by the link(s) is latency sensitive, there can be some portion of traffic for general purpose data transfer.

## Slide 3: Background
EHT aims at improving support for time sensitive networks
  This project will improve the latency and jitter of WLAN. [1]
General requirements [2]:
  Intra-BSS latency in range < 10 ms (e.g. ~3-5ms for real-time video)
  Jitter variance < 2.5ms
  Packet loss: nearly lossless
  Bandwidth: 10s or 100s of Mbps, multi-Gbps for uncompressed cases
MLO framework supports:
  Multi-link aggregation  increase throughput
  Asynchronous/synchronous transmission  increase channel access opportunity in presence of legacy/OBSS traffic
  Uni-directional TID-to-Link mapping
  Dynamic link enabling/disabling.
Still some gap remains: support many latency sensitive traffic streams in the same BSS, and in multiple such BSS’s
Load balancing Differentiated service over different link(s)

## Slide 4: Traffic Characteristics (1)
The latency sensitive applications can be characterized by one or more DL and/or UL streams with the following parameterized model:
  The packets arrive in a bursty fashion, with a periodic interval T. T is a stable variable, and can be considered as a constant over minutes or longer.
    E.g. video display traffic is driven by the refreshing/sync rate, 60/72/90/120 Hz, translating to 16.7/13.9/11.1/8.3 ms period
  The amount of traffic within each interval can vary, but can be qualified by a stable average over seconds or longer.
  Example: a VR rendering stream is characterized by the following parameters:
    Resolution: 4K – 3840x2160
    # of frames: one or more displays
    Bits/pixel: 24 bits/pixel
    Compression ratio (CR): decided by codec and content.
    Refreshing rate: 60/72/90/120 Hz
Amount of traffic can vary from interval to interval
Notes: CR=100, 1 frame => 120 Mbps

## Slide 5: Traffic Characteristics (2)
An application/system can have combinations of such streams of different parameters.
  It can also contain other best effort streams that are more spontaneous/aperiodic.
  It can also have some application level of control traffic
Example: a VR device with hand controllers
  Use case 1: gaming
  Use case 2: virtual video conference
  Use case 3: virtual classroom
  Transfer data: video, voice, file …
See https://lilyotron.blog/2018/04/12/the-top-10-vr-apps-for-remote-workers/ for some fancy app

## Slide 6: Network Topology
For each stream of the application, the direction of traffic can be
  AP  non-AP device
  Non-AP device  AP
  Non-AP device  tethered peer device that may or may not associate with the same AP
Also consider the case where two or more BSS have to operate on the same channel as results of limited spectrum availability e.g.

## Slide 7: Differentiated Services over Different Links in MLO
MLO supports:
  Directional TID-to-Link mapping [3]
  Link enable/disable through negotiation/handshake [4]
   These enables various possible configurations.
Configuration Example 1 | Configuration Ex. 2 | Configuration Ex. 3

## Slide 8: Configuration Descriptions (of Previous Page)
Configuration 1 (device based):
  Non-AP MLDs carrying latency sensitive traffic as major traffic operate over one or a subset of links
  Note: a MLD having latency sensitive traffic may also have some other associated data traffic
Configuration 2 (TID based):
  Map one set of TIDs to one subset of links, and rest TIDs to other links.
Configuration 3 (direction based):
  Some links are dedicated for UL using triggering; and rest links for other traffics.

## Slide 9: Latency Sensitive Links
Specifically, propose an operating mode in MLO, where
  AP MLD, based on association and traffic dynamics, can steer latency sensitive traffic over a subset of links using any suitable configurations (separate contribution)
  Referred as Latency sensitive link(s)
Provide more predictable and prioritized medium access to the latency sensitive traffic or devices whose majority of traffic is latency sensitive
  See NEXT

## Slide 10: Prioritized EDCA Access to Time Slotted Channel
AP defines additional set EDCA parameters other than default SU/MU EDCA parameters:
  One for latency sensitive traffic streams. Only admitted STAs can use them over designated time slots
   Prioritized EDCA access
Over the link, the time is divided into TBD-granularity time slots (e.g. 1ms, 512 usec) per TBD-interval (e.g. BEACON).
  AP assigns the membership of one or multiple slots based on the handshake with STA and/or its scheduling of DL traffic. The owner(s) of a slot can access the medium with prioritized EDCA parameters; otherwise, they have to conform to a different set of EDCA parameters.

## Slide 11: Details: Channel Access
A slot can be assigned to one or more STAs for DL/UL/Peer transmissions
For slots not assigned:
  All STAs operating over the link can contend the access using the default EDCA parameters
For slots assigned to one or more STAs (referred as owners):
  The owners access these slots using a second set of EDCA parameters to gain more deterministic and low latency (prioritized) access.
  Other STAs (not assigned to these slots) can still access the slots, but with lower prioritized access. There are two options:
    Option-1: using the first/default set of EDCA parameters
    Option-2: using a third set of EDCA parameters/behavior in order to make sure the owner to gain enough priority.
Advantage of not exclusive access to slots:
  Traffic is hardly constant: it can vary over time even for the same stream. E.g. a video frame size can vary frame by frame after compression.
  Unused time in slots is still open for non-owners to access – not wasting bandwidth.
  Less stringent requirement on the scheduling algorithm.
Notes: Notes:
Need to count in possible retry. One slot between two groups.

## Slide 12: Management of Time Slots over Latency Sensitive Links
AP accepts non-AP MLD’s request with direct assignment of slots and/or traffic requirement and assign one or more contiguous/non-contiguous slots
  AP may take into account of STA’s capability to decide if performing DL/UL MU transmission and decide if grouping a few STAs/slots together
  Non-AP MLD can request slots for the communication between itself and other peer (MLD) devices
AP can assign slots for traffic originated from AP itself
  However, for some application running a device, the client device may know the traffic characteristic better as designed for.
The requesters/owners of the slots should monitor their traffic dynamics and update the reservation as needed.
AP monitors the utilization of slots, and may force release or change assignments
AP broadcasts this information in form of bitmap to share across intra-/inter-BSS STAs
  Help distribute contention among the set of STAs with latency sensitive traffic
  Allow APs of different BSS’s to coordinate
Notes: 1) Simplification: in order to get into R1.
2) Broadcast TWT
Let STA to set which slots to join. AP does admission control only.  R1
Give example of a simplified

## Slide 13: What It Does and What It Does NOT
It provides STAs requiring more stringent latency a higher probability of QoS delivery without hurting network performance in absence of such STAs
It tries to distribute access for STAs of higher priority to different time slots to avoid contention among themselves
  Increase capacity for a network containing many latency sensitive devices
It does NOT define a scheduling algorithm for applications
  Each device/application have to characterize their traffic pattern at their best knowledge or via prediction and come up with intended slots to sign up. This can include their own originated traffic, the traffic to be received, or peer-to-peer communications.

## Slide 14: More Discussion
The proposed prioritized EDCA can be supported without MLO
But MLO has more flexibility and can provide more benefits
The scheme can be a key component in the multi-AP coordination feature in 11be.

## Slide 15: References
[1] 11-18-1233-07-0eht-eht-draft-proposed-csd
[2] 11-18-2009-06-0rta-rta-report-draft.docx
[3] 11-19-1924-01-00be-multilink-steps-for-using-a-link.pptx
[4] 11-19-1904-03-00be-mlo-link-management-follow-up.pptx

## Slide 16: Straw Poll 1
Support Differentiated Quality of Service over different links in Multi-link Operation

## Slide 17: Straw Poll 2
Defines a mechanism of prioritized EDCA access to time-slotted channel

## Slide 18: Straw Poll 3
Define a Latency Sensitive Link in Multi-Link Operation as one or a subset of links over which STAs use a prioritized EDCA access to time-slotted channel mechanism to provide differentiated quality of service.

## Slide 19: Backup Slides
(TBD: Comparisons with RAW/11ah)