## Slide 1: Prioritized EDCA Channel Access Over Latency Sensitive Link(s) In MLO
Date: 2020-03-09
Authors:
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook Inc. | 1 Hacker way Menlo Park, CA |  | chunyuhu@fb.com
Payam Torab |  |  |  | torab@ieee.org

## Slide 2: Abstract
Multi-link operation (MLO), a key 11be feature, enables flexible traffic steering and load balancing
This presentation targets at improving latency performance with the following key design:
  Define and provide differentiated services over MLO links, and specifically, allocating a subset of MLO links for latency sensitive traffic*, referred as
         Latency Sensitive Links
  A prioritized EDCA channel access scheme over latency sensitive links
* While the main traffic carried by the link is latency sensitive, there can be some portion of traffic for general purpose data transfer originated from the same device; it’s also possible to allow regular traffic if there is excessive bandwidth available.

## Slide 3: Background
EHT aims at improving support for time sensitive networks
  This project will improve the latency and jitter of WLAN. [1]
General requirements [2]:
  Intra-BSS latency in range < 10 ms (e.g. ~3-5ms for real-time video)
  Jitter variance < 2.5ms
  Packet loss: nearly lossless
  Bandwidth: 10s or 100s of Mbps, multi-Gbps for uncompressed cases
MLO framework supports:
  Dynamic link enabling/disabling.
  Uni-directional TID-to-Link mapping
  Multi-link aggregation  increase throughput
  Asynchronous/synchronous transmission  increase channel access opportunity in presence of legacy/OBSS traffic
Still gaps remain in supporting many latency sensitive traffic streams/connections in the same BSS, and in multiple such BSS’s
Differentiated services overs different links
More practical to do more for latency sensitive traffic yet service regular traffic as well
Notes: We are exploring the direction of differentiated services over different links enabled by MLO, and we believe now it becomes more practical to do more for latency sensitive traffic yet service regular traffic as well.

## Slide 4: Traffic Characteristics (1)
A latency sensitive traffic stream can be characterized by the following parameterized model:
  Packets arrive in a bursty fashion, with a periodic interval T
    T is a stable variable and can be considered constant over minutes or longer
    E.g. video display traffic is driven by the refresh/sync rate, 60/72/90/120 Hz, translating to 16.7/13.9/11.1/8.3 ms period (CBR / VBR)
  Amount of traffic within each interval is variable but has a stable average over seconds or longer
  Example: a VR rendering stream is characterized by the following parameters:
    Refreshing rate: 60/72/90/120 Hz
    Resolution: 4K – 3840x2160
    # of frames: one or more displays
    Bits/pixel: 24 bits/pixel
    Compression ratio (CR): decided by codec and content.
     with CR=100, 1 frame per 16.7ms, throughput ~ 120 Mbps
Amount of traffic can vary from interval to interval
Notes: CR=100, 1 frame => 120 Mbps

## Slide 5: Traffic Characteristics (2)
A latency sensitive application/system can have combinations of such streams of different parameters.
  It can also contain other best effort data stream that are more spontaneous/aperiodic.
  It can also have some application level of control traffic
Example: a VR device with hand controllers
  Use case 1: gaming
  Use case 2: virtual video conference
  Use case 3: virtual classroom
  Transfer data: video, voice, file …
See https://lilyotron.blog/2018/04/12/the-top-10-vr-apps-for-remote-workers/ for some fancy app

## Slide 6: Network Topology
For each stream of the application, the direction of traffic can be
  AP  non-AP device (DL)
  Non-AP device  AP (UL)
  Non-AP device  tethered peer device that may or may not associate with the same AP (peer-to-peer) *
Also consider the case where two or more BSSs operate on the same channel as results of limited spectrum availability e.g.
*: this is a typical architecture for wearable AR/XR applications [5]

## Slide 7: Differentiated Services over Different Links in MLO
MLO supports:
  Directional TID-to-Link mapping [3]
  Link enable/disable through negotiation/handshake [4]
   These enables various possible configurations.
Propose the capability of supporting differentiated services for different sets of links
Configuration Example 1 | Configuration Ex. 2 | Configuration Ex. 3
Notes: Right now different BSS can have different capability but

## Slide 8: Description of Configurations in Previous Page
Configuration 1 (device based):
  Non-AP MLDs carrying latency sensitive traffic as major traffic operate over one or a subset of links
  Note: a MLD having latency sensitive traffic may also have some other associated data traffic
Configuration 2 (TID based):
  Map one set of TIDs to one subset of links, and rest TIDs to other links.
Configuration 3 (direction based):
  Some links are dedicated for UL using triggering; and rest links for other traffics.

## Slide 9: Latency Sensitive Links
Define an operating mode in MLO, where
  AP MLD, based on association and traffic dynamics, can steer latency sensitive traffic over a subset of links using a suitable configuration (details TBD)
  Referred as Latency sensitive links
Over such links, provide more predictable and prioritized medium access to the latency sensitive traffic or devices whose majority of traffic is latency sensitive
  (Guideline: light-weighted scheduling, flexible enough to accommodate traffic and network dynamics, mixture of regular/prioritized clients, avoid losing peak throughput performance etc.)
  See NEXT

## Slide 10: Prioritized EDCA Access to Time Slotted Channel
AP defines new set of EDCA parameters in addition to default SU/MU EDCA parameters (referred as regular EDCA parameters):
  For latency sensitive traffic streams. Only admitted STAs can use them over designated time slots
   Prioritized EDCA access
Over the link, time is divided into TBD-granularity slots (e.g. ½ , 1, 2 …TU) per TBD-interval (e.g. BEACON).
  AP shares the slot occupancy info in simple form of bitmap carried in IE (Beacon/Probe response/etc.)
  AP assigns the membership of one or multiple slots based on the handshake with STA and its own scheduling of DL traffic.
  More details in next two slides.

## Slide 11: Details: Channel Access
A slot can be assigned to one or more STAs for DL, UL, or Peer transmissions
  Note: we expect to allow a non-AP STA can register traffic for its communication with its tethered STA(s)
  AP can group STAs over same slots such that MU transmission can be conducted for increased efficiency
For slots not assigned:
  1: all STAs operating over the link can contend the access using the regular EDCA parameters
For slots assigned to one or more STAs (referred as owners):
  2: The owners access these slots using a second set of EDCA parameters to gain more deterministic and low latency (prioritized) access.
  3: Other STAs (not assigned to these slots) can still access the slots but use different access policy. For example (details to be further defined/discussed in next step):
    Option-1: using the regular EDCA parameters
    Option-2: using a third set of EDCA parameters/behavior in order to make sure the owner to gain enough priority.
    Other options: ?
Advantages of non-exclusive access to slots:
  Traffic is hardly constant: it can vary over time even for the same stream (recall the traffic model in slide 4 – a video frame size can vary frame by frame after compression.)
  Unused time in slots is still open for non-owners to access – not wasting bandwidth.
  Less stringent requirement on the scheduling algorithm.
Notes: Notes:
Need to count in possible retry. One slot between two groups.

## Slide 12: Details: Management of Time Slots
AP accepts non-AP MLD’s request in form of 1) direct assignment of slots; and/or 2) traffic requirement, and assign one or more contiguous/non-contiguous slots
  AP may take into account of STA’s capability to decide if performing DL/UL MU transmission and decide if grouping a few STAs/slots together
  Non-AP MLD can request slots for the communication between itself and other peer devices
AP can assign slots for traffic originated from AP itself
  However, for some application running on a device, the client device may know the traffic characteristic better afore-head.
The requesters/owners of the slots should monitor their traffic dynamics and update the reservation as needed.
AP monitors the utilization of slots, and may force release or change assignments
AP broadcasts this information in form of bitmap to share across intra-/inter-BSS STAs
  Help distribute contention among the set of STAs with latency sensitive traffic
  Allow APs of different BSS’s to coordinate
   Coordinated AP scheme (to be defined )

## Slide 13: What It Does and What It Does NOT
Prioritize: provides STAs requiring more stringent latency a higher probability of QoS delivery without hurting network performance in absence of such STAs
Distribute: distributes access among STAs of higher priority to different time slots to avoid contention among themselves
  Increase capacity for a network containing many latency sensitive traffic streams
Enables peer-to-peer traffic to gain prioritized access as well
  Can do so without much involvement of AP at packet/txop level (AP doesn’t know peer-2-peer traffic info anyways!)
Coordinate: scalable and light-weighted scheduling intra-BSS and can be extended to support multi-BSS coordination
It does NOT define a scheduling algorithm for applications
  Each device/application can characterize their traffic patterns at their best knowledge (run-time estimate e.g.) and either come up with intended slots to sign up, or provide minimum info for AP to assign. This can include their own originated traffic, the traffic to be received, or peer-to-peer communications.

## Slide 14: Summary
Propose a capability of MLO to support differentiated services over different links
Propose latency sensitive service as one such service
Propose a prioritized EDCA access over time-slotted channel to provide the latency sensitive service

## Slide 15: More Discussion
The proposed prioritized EDCA access can be supported without MLO
But MLO has more flexibility and provides more benefits
  Provide connectivity and services to both regular and latency sensitive traffic in the same BSS
The scheme can be a key component leading to a multi-AP coordination protocol in 11be.
More details to be hashed out in the protocol design
  Such as but not limited to: Interval/slot, EDCA parameter/access policy in assigned slots; admission control/link steering in this framework; multi-AP coordination of slot allocation …

## Slide 16: References
[1] 11-18-1233-07-0eht-eht-draft-proposed-csd
[2] 11-18-2009-06-0rta-rta-report-draft.docx
[3] 11-19-1924-01-00be-multilink-steps-for-using-a-link.pptx
[4] 11-19-1904-03-00be-mlo-link-management-follow-up.pptx
[5] 3GPP TR 26.928 (link): technical specification group services and system aspects; extended reality (XR) in 5G.

## Slide 17: Straw Poll 1
Do you support that the TGbe SFD shall include that
  An MLD AP may offer differentiated quality of service over different links

## Slide 18: Straw Poll 2
Do you support that the TGbe SFD shall include:
  An optional mechanism of dividing medium time into slots of duration TBD during which prioritized EDCA access operates for specifically allowed STAs
Notes: an optional mechanism of dividing medium time into slots of minimum duration TBD during which prioritized EDCA access operates for specifically allowed STAs

## Slide 19: Straw Poll 3
Do you support that the TGbe SFD shall include:
  A definition of Latency Sensitive Links in Multi-Link Operation as one or more links over which a prioritized EDCA access over time-slotted channel is defined and conducted by STAs

## Slide 20: Straw Poll 4
Do you support that the SFD shall include:
  A procedure to share and coordinate time resource allocation for prioritized EDCA access between BSSs.

## Slide 21: Appendix

## Slide 22: Feasibility of Providing Differentiated QoS over Different Links in a BSS
A lot of existing AP already have multi-band capability
It’s natural to assume most APs capable of 11be will be able to support multiple links as well (even some STAs don’t)
With MLO, it’s possible to divide links on-demand into two groups: one for latency sensitive traffic or devices carrying such traffic, and the other for rest
AP can monitor CCA over channels and choose one or more clean channels allocated as latency sensitive link(s)
  MBO/OCE certificate program in WFA
FCC opens 6GHz Band to Wi-Fi and Other Unlicensed Uses (R&O)
  “Green-field” for 11ax and 11be

## Slide 23: Example 1: Network with Latency Sensitive App/Device joining
A MLO network with two links: two regular* clients. One client operates at link 1 (client A) and the other client operates at link 2 (client B).
  A third device (client B) associates, carrying latency sensitive traffic. It is steered to link 2 and through negotiation handshake, obtained two slots for prioritized EDCA access.
  Client B can be still present but with reduced throughput as result of shared bandwidth.
  Six more devices with latency sensitive traffic joined and are allocated slots to have distributed/prioritized EDCA access. Client B can still operate in link 2 but with further reduced throughput. It can choose to stay on link 2 but AP hasn’t forced it to do so.
  When the 8-th device joining link-2 with latency sensitive traffic, AP decides the link capacity is about to saturate. It hence steers client B to link-1.
*: STAs that doesn’t register a device with any latency sensitive traffic.

## Slide 24: Example 2: Coexistence With Legacy STAs
Over latency sensitive links, it is still possible that a legacy STA can be still admitted/operating in coexistence with STAs that understand the prioritized EDCA access protocol (per AP’s policy)
  A legacy STA doesn’t have time slot view, and it operates with default (regular) EDCA parameters.
  Owners of designated slots have more aggressive EDCA parameters and hence still have higher priority to gain more immediate channel access
  Not ideal, but still an improvement compared to without this new protocol. Mitigation mechanism can be invoked by AP via, e.g. UL MU scheduling; admit or steer legacy STAs over non-latency sensitive links (MBO/OCE).

## Slide 25: Compared to TWT
TWT doesn’t provide any special medium access method
  It doesn’t have any restrictions on use of medium for non-TWT participants, either
TWT doesn’t advertise all STA’s start/end/period in the way the proposed mechanism enables
  Scalability
  Coordination
TWT involves more overhead in negotiating/settling with STA on a schedule (demand/reject/suggest/accept).
To satisfy traffic requirement, STA may have to sign up multiple TWT sessions. More challenging to track.
  In proposed mechanism, a STA can sign up multiple groups of slots in one request