## Slide 1: Multi-RU Indication in Trigger Frame
Date: 2020-03-12
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@Huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2: Background
Multi-RU
  Multi-RU means more than one RU can be assigned to a single STA [1][2].
  11ax does not support multi-RU combination and assignment
  11be shall support multi-RU for higher spectral efficiency
  Recently, several motions on multi-RU combination have been passed, including small RU combination and large RU combination [3][4]
  Small RU: RUs with size smaller than 242
  Large RU: RUs with size equal to or lager than 242
Although several signaling options on multi-RU have been discussed, these options mainly focus on the solutions for non-TB PPDU [5]. In this proposal, we focus on the trigger frame and discuss the multi-RU Indication in it.

## Slide 3: Format of Trigger Frame
Trigger Frame
  A trigger frame allocates resources for and solicits one or more TB PPDU transmissions.
  The User Info List field contains zero or more User Info fields. Each User Info field contains an RU Allocation subfield.
  The RU Allocation subfield along with the UL BW subfield in the Common Info field identifies the size and location of the RU. One STA is corresponding to one User Info field.
Trigger Frame Format

## Slide 4: RU allocation subfield for 240/320 MHz BW
Similar method is assumed to be used for an 11be trigger frame.
For 240MHz/320MHz, a 9-bit RU-Allocation subfield can be used. The mapping of B1-B0 of the RU Allocation subfield is shown in the following table, which indicates an 80MHz segment in 240Mhz/320MHz BW.
In the following, we propose several multi-RU indication options on the basis of the existing format.
BW | RU Allocation subfield (B1,B0) | Descriptions
20MHz, 40MHz and 80MHz | 00 | Only one 80MHz segment
160MHz or 80+80MHz | 00, 01 | 00: lower segment, 01: higher segment
240MHz | 00, 01, 10 | Three segment
320MHz, 160+160MHz | 00, 01, 10, 11 | Four segment

## Slide 5: Opt 1: Repeat AID
If an AP wants to allocate N RUs for one STA, we could directly use N user Info fields to indicate these N RUs. Each User Info fields contains the same AID.
Some considerations
  User Info fields with the same AID could be put together to save energy
  An end indication could be added to each user field to denote whether it belongs to a same STA
  etc.
Opt 1: Repeat AID

## Slide 6: Opt 2: Combination Indication
Although less specification impact is achieved by Opt 1, the first option needs more than one User Info field to indicate multi-RU combination.
Opt 2: A Combination Indication subfield can be added to each User Info field to denote the multi-RU combination. Different combinations can be distinguished by this subfield along with the RU Allocation subfield.
Opt 2: Combination indication

## Slide 7: Opt 2: Combination Indication
For example, to indicate the 52+26 combination case, we could let the RU Allocation subfield in User Info field point at the location of the 52-tone RU (the larger/largest one). Then by using the following table, we can get the exact 52+26 combination.
Same for 106-tone RU + 26-tone RU combination.
RU allocation | Combination Ind |  | Meaning
 | Bit 1 | Bit 0 | 
2nd 52-tone RU (e.g.) | 0 | 0 | 52-tone RU only, no multi-RU combination
 | 0 | 1 | 52 + 26 (on the left, contiguous)
 | 1 | 0 | 52 + 26 (on the right, contiguous)
 | 1 | 1 | Reserved

## Slide 8: Opt 2: Combination Indication
Another example is about large RU combination, e.g., to indicate 484+242 combination case, we could let the RU Allocation subfield in User Info field point at the location of the 484-tone RU (the larger/largest one). Then by using the following table, we can get the exact 484+242 combination.
RU allocation | Combination Ind |  | Meaning
 | Bit 1 | Bit 0 | 
1st 484-tone RU (e.g.) | 0 | 0 | 484-tone RU only, no multi-RU combination
 | 0 | 1 | 484 + 242 (contiguous)
 | 1 | 0 | 484 + 242 (non-contiguous)
 | 1 | 1 | Reserved
Other combinations of multi-RU could follow the same rules.
To indicate more flexible combination (e.g., for RU combinations across 80MHz), we could either use larger bitwidth, or this option can be combined with Opt 1, which means that more than one User Info field can be used.

## Slide 9: Opt 3: Change in RU Allocation subfield
To indicate different multi-RU combinations, new entries can be added to the RU Allocation subfield.
An example of the mapping of B8-B2 in RU Allocation subfield is shown in the following table. Some newly added entries are added in this table to show the MRU combinations related to this 80MHz segment.
B8-B2 | Description | Number of entries
0-36 | 26-tone RU in 80MHz | 37
37-52 | 52-tone RU in 80MHz | 16
53-60 | 106-tone RU in 80MHz | 8
61-64 | 242-tone RU in 80MHz | 4
65-66 | 484-tone RU in 80MHz | 2
67 | 996-tone RU in 80MHz | 1
68-70 | Two 996-tone RUs | 3
71-73 | Three 996-tone RUs | 3
74 | Four 996-tone RUs | 1
75-82 | In 80MHz, the lower/upper 106-tone RU and the middle 26-tone RU in a 20MHz | 8
83-90 | In an 80MHz, the secondary lower/upper 52-tone RU and the 26-tone RU on the same side in a 20MHz | 8
91-92 | In an 80MHz, a 484-tone RU and a contiguous 242-tone RU | 2
93-94 | In an 80MHz, a 484-tone RU and a non-contiguous 242-tone RU | 2
… | … | …

## Slide 10: RU combination indication for non-OFDMA TB PPDU
For non-OFDMA TB PPDU, the number of RU combination modes may be larger than the number for OFDMA case.
May first indicate the trigger frame is for non-OFDMA TB PPDU, and then use similar indication method as the indication in the EHT-SIG of a non-TB PPDU.
Specific signaling methods will be discussed separately.

## Slide 11: Summary
Options | Pros | Cons
Option 1 Repeat AID in the User Info field allocated to the same STA | Less specification impact Very flexible combination | 1. A multi-RU user needs more than one User Info field (high overhead)
Option 2 (Preferred) Combination Indication in each User Info field | 1. For most cases, one STA only needs one User Info field (More User Info fields are needed to support more flexible combinations) | 1. Needs to add a Combination Indication subfield in each User Info field (medium overhead)
Option 3 (Preferred) Change in the RU Allocation subfield | 1. One STA only needs one User Info field (no additional overhead) | 1. More entries in the RU allocation subfield

## Slide 12: Straw Poll #1
Do you agree to the bitwidth of the RU allocation subfield in the trigger frame is 9 bit? And B1, B0 of the RU allocation subfield are used to indicate which 80Mhz the RU allocation subfield applies to?

## Slide 13: Straw Poll #2
Which option do you prefer to be used for RU combination indication in the trigger frame?
  Non-OFDMA mode TBD
  Opt1
  Opt2
  Opt3
  None
  Abstain
Options | Descriptions
Option 1 | Repeat AID in the User Info field allocated to the same STA
Option 2 | Combination Indication in each User Info field
Option 3 | Change in the RU Allocation subfield

## Slide 14
[1] IEEE 802.11-19/1126r1 Enhanced Resource Unit Allocation Schemes for 11be
[2] IEEE 802.11-19/1914r4 Multiple RU Discussion
[3] IEEE 802.11-19/1907r2 Multiple RU Combinations for EHT
[4] IEEE 802.11-19/1908r4 Multi-RU Support
[5] IEEE 802.11-19/1968r2 Signaling Support for Multi-RU Assignment
References