## Slide 1: Coordinated AP Spatial Sharing in a TXOP
Date: 2020-03-10
Authors:

## Slide 2: Abstract
TXOP sharing has been discussed in several presentations [1-2].
Spatial multiplexing using coordinated beamforming and nulling has also been discussed [3-4].
We propose to re-use and extend the protocol in [1] for spatial TXOP sharing. We refer to this scheme as CAP-SDMA.

## Slide 3: CAP-SDMA
The following scheme was presented in [1]:
Use the same scheme and extend Data TX part with a Channel Sounding phase and a modified Data TX, where Nulling is done to reduce interference:
Channel Sounding
Data TX and Nulling

## Slide 4: Performance gains requires degrees of freedom at the APs
In the Data TX and Nulling
  Data is transmitted to STAs in the APs own BSS
  Nulls are placed to STAs in neighboring BSSs who are sharing the TXOP
  The full bandwidth may be spatially reused for the full TXOP time
Nulling STAs in neighboring BSSs requires degrees of freedom
Assume for example:
  Each AP has 8 antennas
  4 APs cooperate
  2 simultaneous DL transmissions per AP, 1 spatial stream per transmission
  For each AP: 2 degrees of freedom for DL data, 6 degrees of freedom for Nulling
  If not enough degrees of freedom to null STAs, null the ones which are interfered the most (based on e.g. CSI).

## Slide 5: Performance comparison
DL: 4 spatial streams, total 80 MHz,
  CAP-OFDMA: 20 MHz, full TXOP  X Mbit/s
  CAP-TDMA: 80 MHz, ¼ TXOP  X Mbit/s
  CAP-SDMA: 80 MHz, full TXOP  up to 4X Mbit/s (if channel sounding overhead is negligible)
Channel Sounding
Data TX and Nulling

## Slide 6: How large is the channel sounding phase?
Need to learn channels for each AP and each STA
  Explicit sounding must be sent from each AP to all STAs
    4 APs, 8 STAs  32 sounding frames
    If the APs multicast their sounding frames  4 sounding frames
  STAs must report sounding feedback to all APs
    4 APs, 8 STAs  32 sounding feedback frames
    If the STAs multicast their feedback and include multiple APs  8 sounding feedback frames
Total of 12 frames ~ 1-2 ms of time. TXOP budget ~ 6 ms. Total gain 2X – 3X
Channel sounding
Data TX and Nulling
~300 us
~2 ms
~3.7 ms
Typically 2X - 3X throughput compared to CAP-OFDMA, CAP-TDMA.

## Slide 7: Channel Sounding
AP2 obtains beamforming feedback from STAs is BSS1
AP3 obtains beamforming feedback from STAs is BSS1
AP4 obtains beamforming feedback from STAs is BSS1
AP1 obtains beamforming feedback from STAs is BSS2
AP3 obtains beamforming feedback from STAs is BSS2
AP4 obtains beamforming feedback from STAs is BSS2
AP4 obtains beamforming feedback from STAs is BSS3
AP1 obtains beamforming feedback from STAs is BSS3
AP2 obtains beamforming feedback from STAs is BSS3
AP1 obtains beamforming feedback from STAs is BSS4
AP2 obtains beamforming feedback from STAs is BSS4
AP3 obtains beamforming feedback from STAs is BSS4
STAs in BSS2 learns the channel to AP1, AP2, AP3 and AP4.
STAs in BSS1 learns the channel to AP1, AP2, AP3 and AP4.
STAs in BSS3 learns the channel to AP1, AP2, AP3 and AP4.
STAs in BSS4 learns the channel to AP1, AP2, AP3 and AP4.
Broadcast (outside BSS) NDP. Multi-AP feedback frames.
Channel Sounding
Trg.
NDP
TXOP Owner BSS1
BSS2
BSS3
NDP
NDP
NDP
Mult-AP FB
Mult-AP FB
Mult-AP FB
Mult-AP FB
Mult-AP FB
Mult-AP FB
Mult-AP FB
Mult-AP FB
BSS4
...
...
...
...
...
...
AP TX
STA TX
...
AP RX

## Slide 8: Data TX and Nulling
Trg.
TXOP Owner BSS1
BSS2
BSS3
BSS4
Data TX and Nulling
Prmbl
Prmbl
Prmbl
Prmbl
PSDU(s). One or more STAs (both OFDMA and MU-MIMO). Total BW = 80 MHz.
ACK
PSDU(s). One or more STAs (both OFDMA and MU-MIMO). Total BW = 80 MHz.
ACK
PSDU(s). One or more STAs (both OFDMA and MU-MIMO). Total BW = 80 MHz.
ACK
PSDU(s). One or more STAs (both OFDMA and MU-MIMO). Total BW = 80 MHz.
ACK

## Slide 9: Pen-and-paper throughput
Assumptions as slide 4, with 4 APs, 8 STAs in total, 8 TX antennas at the APs

## Slide 10: Pen-and-paper throughput
Scheme | Norm. Tput
EDCA (reference) | 100%
CAP-OFDMA | 84%
CAP-TDMA | 79%
CAP-SDMA | 195%
We need to sacrifice half of the time for training all channels, but gain 4 times in sum throughput during the TX phase.

## Slide 11: Straw Poll 1
Do you believe that, using the protocol in [1], we should consider TX beamforming and nulling to increase system throughput in TXOP sharing for EHT?
Y/N/A:

## Slide 12: References
[1]: Coordinated AP Time and Frequency Sharing in a Transmit Opportunity in 11be, Lochan Verma (Qualcomm), George Cherian (Qualcomm) et al.
[2]: Multi-AP coordination for spatial reuse, Dmitry Akhmetov (Intel) et al.
[3]: Performance of parameterized spatial reuse (PSR) with coordinated beamforming/null steering for 802.11be, Adrian Garcia-Rodriguez (Nokia) et al.
[4]: Downlink spatial reuse parameter framework with coordinated beamforming/null steering for 802.11be, David Lopez-Perez (Nokia) et al.