## Slide 1: Multi-Link TSF Discussion
Date: 2020-3-10
Authors:

## Slide 2: Introduction
For a multiple-link operation, TSF information of each link has to be provided from an AP MLD to a non-AP MLD to coordinate activities among multiple links
There are two cases to consider
  Case 1: an AP of an AP MLD doesn’t have TSF time information of the other AP(s)
  Case 2: an AP of an AP MLD have TSF time information of the other AP(s)

## Slide 3: Case 1: an AP of an AP MLD doesn’t have TSF time information of the other AP(s)
We assume each AP of an AP MLD has its own TSF counter independent from the other APs
Likewise, a non-AP STA MLD also maintains multiple TSF counters for multiple enabled links
Each TSF counter of an non-AP STA is updated by receiving a beacon on each link
Non-AP MLD calculates difference by comparing two TSF timers = t – t’ = delta(TSF) > 0
The other link’s TWT can be calculated as follows: TWT2’ = TWT1 + offset - delta(TSF)
For multi-link TWT setup, both TWT1 and TWT2’ are included in a setup frame
Link 1
t
AP 1
STA 1
STA1
AP1
Link 2
t’
AP 2
STA 2
STA2
AP2
AP MLD
Non-AP MLD
TSF counter1 = t
TSF counter2 =t’
TSF counter 1 = t
TSF counter 2
= t’
t1
B
Timestamp = t2’
t2’
B
Beacon (Timestamp = t1)
TWT1
TWT2
TWT1
offset
TWT2’ = TWT1 + offset - delta(TSF)
t2
Delta(TSF) = t - t’ = 10
300
290
100
90
200
10
0
50
40

## Slide 4: Discussion on clock drift for Case 1
Assuming each AP of an AP MLD has independent clock and the APs don’t adjust their clock with each other, each clock will drift and one TSF counter will run faster than the other
This will result in increased or decreased offset between TWT SPs in different links
One way to address this is to track the changes of difference between the TSF counters in a non-AP MLD and report to AP MLD so that AP MLD can adjust the clock
  Non-AP STA reports delta(TSF) to AP periodically
Otherwise, the two independent clocks will just drift without any correction
Link 1
t
AP 1
STA 1
STA1
AP1
Link 2
t’
AP 2
STA 2
STA2
AP2
AP MLD
Non-AP MLD
TSF counter1 = t
TSF counter2 =t’
TSF counter 1 = t
TSF counter 2
= t’
B
Timestamp = t2’
t2’
B
Beacon (Timestamp = t1)
TWT1
TWT2
TWT1
offset
TWT2’ = TWT1 + offset - delta(TSF)
t2
delta(TSF) = t - t’ = 11
290
101
90
200
11
0
51
40
100
89
10
t1
301
289
-1

## Slide 5: Case 2: an AP of an AP MLD have TSF time information of the other AP(s)
We assume APs of an AP MLD can exchange TSF values and calculate time difference (delta) between each other
Each AP announces its TSF value and time difference between other link(s)
A STA can receive a beacon on one link and synchronize to the clocks of other links (e.g. receiving one timestamp and delta between two APs)
AP MLD may compensate clock drift based on the calculated time difference between APs
Link 1
t
AP 1
STA 1
STA1
AP1
Link 2
t’
AP 2
STA 2
STA2
AP2
AP MLD
Non-AP MLD
TSF counter1 = t
TSF counter2 =t + delta
TSF counter 1 = t
TSF counter 2
= t + delta
t1
B
(Timestamp2 = t2, -delta)
t2’
B
Beacon (Timestamp1 = t1, +delta)
TWT1
TWT2
TWT1
offset
TWT2’ = TWT1 + offset + delta
t2
300
290
100
90
200
10
0
50
40
communication channel (TSF exchange)

## Slide 6: Discussion
Option 1 [Preferred]: AP MLD shall calculate TSF time difference between APs on different links and announce the time difference on each link
  Non-AP MLD doesn’t need to track TSF times on multiple links
  Non-AP MLD can track TSF time of one link and knows TSF times of other links
Option 2: AP MLD doesn’t support calculation of TSF time difference between APs on different links
  Non-AP MLD needs to track TSF times of multiple links for the non-AP MLD to operate on multiple links in a time coordinated fashion (e.g. coordinated TWTs among multiple links)

## Slide 7: Summary
For a multi-link operation that needs time coordinated operation between multiple links, non-AP MLD needs to know the TSF time difference between the links
The problem gets simpler when an AP MLD calculates TSF time difference between APs on different links and each AP of the AP MLD announces the time difference along with its TSF value
  Non-AP MLD obtains TSF information from one link and derives TSF info of the other links

## Slide 8: Straw Poll 1
Do you support to add the following to 802.11be SFD?
AP MLD shall calculate TSF time difference between APs on different links and each AP shall announce the time difference along with its TSF value on each link

## Slide 9: Straw Poll 2
Do you support to add the following to 802.11be SFD?
An AP MLD shall correct the clock (TSF time) drift between APs in the AP MLD, if there is a drift