## Slide 1: Synchronous multi-link operation
Date: 2020-04-06
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Introduction
For those non-AP MLDs that don’t support simultaneous Tx & Rx on different links (non STR MLD), several mechanisms were discussed:
  Synchronous mode operation.
    When a non-AP MLD is in Tx mode on one link, the non-AP MLD is not supposed to be in Rx mode on the other link.
  Reduced power operation
    When a non-AP MLD is in Tx mode on one link, the non-AP MLD reduces its transmit power such that its interference to other link is manageable.
In this contribution, we discuss transmission sequence for the synchronous mode operation, especially when a transmission error happens.

## Slide 3: Recap: Synchronous mode operation
Normal operation
  Assumption: An AP MLD is a STR MLD and a non-AP MLD is a non STR MLD.
  When the AP MLD transmits a frame (D2) on link1 to the non-AP MLD:
    The AP MLD will transmit another frame (D3) on link2 simultaneously to the non-AP MLD.
      The transmission end time of D2 and D3 will be the same.
    If D2 solicits an immediate response (BA2) on link1, D3 will also solicit an immediate response (BA3) on link2.
      The transmission end time of BA2 and BA3 will be the same.
D0
D1
BA0
BA1
D2
BA2
D4
BA4
D3
BA3
D5
BA5
Link 1
Link 2
TXOP1
TXOP2

## Slide 4: Synchronous mode operation
If an AP MLD transmits frames (D2/D3) on link1 and link2 simultaneously to a non-AP MLD, which solicit immediate response, but receives a response frame (BA2) on link1 only:
  Conventional PIFS recovery may not be possible as BA2 transmission will interfere with reception of the retransmitted D3.
    Transmission of BA2 will interfere with ED during PIFS as the non-AP MLD is a non STR MLD.
PIFS
D0
D1
BA0
BA1
D2
BA2
D4
BA4
D3
D3
Link 1
Link 2
TXOP1
TXOP2

## Slide 5: Synchronous mode operation
Option 1: Terminate the TXOP on link2
  The non-AP MLD does not initiate another TXOP on link2 during on-going TXOP on link1.
    Benefit of using multi-link operation can be significantly reduced.
D0
D1
BA0
BA1
D2
BA2
D4
BA4
D3
Link 1
Link 2
TXOP1

## Slide 6: Synchronous mode operation
Option 2: Continue transmission on the failed link
  As the transmission time for the immediate response frame for both links are the same, as long as the non-AP MLD successfully receives BA2 on link1, the non-AP MLD can continue transmission during the TXOP2.
  On link2, chance of 3rd party STA transmitting during the BA2 time is very low:
    When the 3rd party STA receives frames that elicit TXOP (D1/BA1), the Duration information will prevent the 3rd party STA from accessing the link2 during TXOP2.
    If the 3rd party STA receives D3 correctly, the Duration information will prevent the 3rd party STA from accessing the link2 during TXOP2.
    If the 3rd party STA fails to receive D3, the 3rd party STA has to wait at least EIFS duration before its own transmission.
  The non-AP MLD may need to check channel status (CCA) before transmission.
D0
D1
BA0
BA1
D2
BA2
D4
BA4
D3
D3
BA3
Link 1
Link 2
TXOP1
TXOP2

## Slide 7: Synchronous mode operation
Option 3: Dummy frame transmission on the failed link
  For synchronous mode operation, the responder knows when to send acknowledgement frame on link2 if the responder successfully receives D2 on link1.
  Even if the responder does not successfully receive D3 on link2, the responder sends back a Dummy frame whose packet duration is the same with BA2 so that the non-AP MLD can maintain the TXOP on link2.
  This gives a burden to the non-AP MLD side.
D0
D1
BA0
BA1
D2
BA2
D4
BA4
D3
Dummy
D3
BA3
Link 1
Link 2
TXOP1
TXOP2

## Slide 8: Summary
Possible options for retransmission on synchronous mode multi-link operation has been discussed.
  Terminate the TXOP
  Continue transmission on the failed link
  Dummy frame transmission on the failed link
Considering the efficiency and complexity, we prefer Option 2.

## Slide 9: SP
Do you support the following transmission sequence for the constrained multi-link operation:
  When an AP MLD obtains TXOPs on multiple links and transmits frames to a non STR non-AP MLD soliciting immediate response on the multiple links, and intends to align the ending time of DL PPDUs during the obtained TXOPs:
    If the AP MLD does not receive an immediate response successfully on a link that is not a first frame exchange within the obtained TXOP of the link, and if the AP MLD receives an immediate response on at least one another link, the AP MLD can continue its transmission on the link within the obtained TXOP TBD (e.g., SIFS or PIFS) time after the failed reception of the immediate response if the channel is idle.
    CCA mechanism on the link is TBD.