## Slide 1: Partial Bandwidth Transmission Opportunities in EHT
Date: 2020-03
Authors:

## Slide 2: Introduction
11be supports wider bandwidth, eg., 320/160+160 MHz , 240/160+80MHz, 160/80+80MHz bandwidth operation.
However, if the primary channel is overloaded or busy, no transmission (neither dynamic bandwidth nor preamble puncturing) is allowed
  The spectrum of the wideband channel is under utilized
  Hard to provide reasonable quality of service for low latency applications like cloud gaming, voice/video calls, etc.

## Slide 3: Motivation
This contribution discusses
  How to increase spectrum utilization in the wide band system by using the idling non-primary channels while the primary channel is busy
  How to improve the service for real-time applications by providing more opportunities using non-primary channels when the primary channel is idle or busy

## Slide 4: Discussions
Wide band transmission is good for
  increasing the peak throughput
  supporting narrow band non-AP devices with more flexible resource allocation and more transmission opportunities
When primary 20MHz channel is blocked, is there any opportunity to use idling part of the operating bandwidth?
  OBSS interference
    Legacy OBSSs occupy primary 80MHz channel
  Interference from other competing system (eg. LAA/NR-Unlicense)
    Multi-channel channel access rules allow the use of any combination/grouping of 20 MHz Operating Channels if channel access requirements are satisfied on each of the 20MHz operating channel [1]
    More aggressive channel contention mechanism than 802.11, and is not based on the condition of the primary channel
  Radar signals or incumbent signals

## Slide 5: Partial Bandwidth Transmission Opportunity
The benefits of partial bandwidth transmission (PBT) opportunity are:
  to allow wide bandwidth to be used more often among OBSSs or other system in dense deployment scenarios
    When an AP detects an OBSS PPDU (eg. 80MHz 11ax PPDU), the AP can take the opportunity to use the idling non-primary channels (eg. Remaining idle 80MHz/160MHz/240MHz with/without preamble puncturing) for partial bandwidth transmission
    The AP can take the opportunity to trigger partial bandwidth uplink transmission to other non-AP STAs which are parking on idling channels
  to provide service to low latency applications more opportunities
    No matter the primary channel is idle or busy, an AP can always take any opportunity to use the idling channels to provide services to low latency applications

## Slide 6: Further Analysis on Partial Bandwidth Transmission Opportunity
Case1: Assume the channel access prob. is identically 60% for PIFS as well as EDCA based access
  With PBT, the upper bound of channel access on the non-primary channel should be calculated as :
    First part: primary 80 is idle & non-primary 80 is idle, 60% x 60% =36%
    Second part: primary 80 is busy & non-primary 80 is idle, 40% x 60% = 24%
    Total prob. is 36%+24% = 60%
  So, the upper bound of channel access for PBT proposal is the same as parking on the primary channel which is 60% as well.

## Slide 7: Further Analysis on Partial Bandwidth Transmission Opportunity
Case 2: Assume that the channel access probability for PIFS is higher than 60%, say 80%, and the channel access probability for EDCA on non-primary channel is 60%.
  This assumption is reasonable because PIFS channel access is of the highest priority.
  With PBT, the upper bound of channel access for PBT proposal is dominated by the non-primary channel access:
    First part: primary 80 is idle & non-primary 80 is idle, 60% x 80% = 48%
    Second part: primary 80 is busy & non-primary 80 is idle, 40% x 60% = 24%
    Total Prob. : 48% + 24% = 72%
  So, the upper bound of channel access for PBT proposal is higher than which parking on the primary channel.

## Slide 8: Partial Bandwidth Transmission Opportunity
Based on the analysis in slide 6 and 7, we can see that :
  With PBT, fairness on channel access can be provided among non-AP STAs parking on primary 80 MHz channel and non-primary 80 MHz channels, so that load balancing performance can be achieved.
  With PBT, higher opportunities may be achieved by parking on non-primary channel than parking on the primary channel

## Slide 9: AP’s operation in PBT Operation
An AP obtains a PBT Opportunity (PBT TXOP) on a subset of non-primary channels when it detects the primary channel busy with signal strength equal to or higher than a threshold.
  The AP preconfigured bandwidth part(s) which is a subset of operating bandwidth (eg. Four 80MHz bandwidth segments for a 320 MHz operating bandwidth)
  The AP contends on the designated channel(s) for channel access on the preconfigured bandwidth segment(s)
    On multiple 20 channels if the AP is capable of doing multiple parallel preamble detection
    Otherwise, on one 20 channel
  The PBT TXOP is obtained on one or more preconfigured bandwidth segments when PBT backoff to zero, and
    The PBT TXOP occupies the non-primary channels which are PIFS idle immediately before the transmission
    The idle non-primary channels may be across multiple bandwidth segments

## Slide 10: PBT Backoff
An AP that meets the PBT conditions obtains a PBT TXOP using PBT channel access
  PBT conditions:
    Detect an OBSS PPDU on the primary channel with signal strength level equal to or larger than a threshold
    The detected energy is equal to or larger than a PBT ED threshold
  PBT backoff:
    PBT backoff can be invoked
      If meeting the PBT conditions
      A TBD delay (eg. NavSyncDelay) may be applied
    One or more PBT backoff procedure(s) can be invoked
      Parallel PBT backoffs are performed if an AP is capable of doing parallel multiple preamble detection
      Otherwise, one PBT backoff is performed on random selected bandwidth segment

## Slide 11: PBT TXOP Example 1
primary
80 MHz
OBSS PPDU
…
BA
PBT TXOP
PPDU to STA(s)
…
PIFS idle
PIFS idle
AP Backoff suspend
BA
OBSS TXOP
PBT backoff
80MHz
Bandwidth segment 1
80MHz
Bandwidth segment 2
80MHz
Bandwidth segment 3
PIFS idle
ch1
ch2
ch3
ch4
The PBT backoff is done on a 20MHz channel in one randomly selected 80MHz bandwidth segment
The PBT TXOP bandwidth can be across multiple 80MHz bandwidth segments
PIFS idle
PIFS idle
PIFS idle
PIFS idle
PIFS busy

## Slide 12: PBT TXOP Example 2
primary
80 MHz
OBSS PPDU
…
BA
PBT TXOP
PPDU to STA(s)
…
PIFS idle
PIFS idle
AP Backoff suspend
BA
OBSS TXOP
PBT backoff
80MHz
Bandwidth segment 1
80MHz
Bandwidth segment 2
80MHz
Bandwidth segment 3
PIFS idle
ch1
ch2
ch3
ch4
The PBT backoff is done on a 20MHz channel in one randomly selected 80MHz bandwidth segment
The PBT TXOP bandwidth is restricted to one 80MHz bandwidth segment

## Slide 13: PBT TXOP Example 3
primary
80 MHz
OBSS PPDU
…
BA
PBT TXOP
PPDU to STA(s)
…
PIFS idle
PIFS idle
AP Backoff suspend
BA
OBSS TXOP
PBT backoff
80MHz
Bandwidth segment 1
80MHz
Bandwidth segment 2
80MHz
Bandwidth segment 3
PIFS idle
PBT backoff
suspend
Channel busy
ch1
ch2
ch3
ch4
The PBT backoff is done on parallel 20MHz channels in each non-primary 80MHz bandwidth segment
The PBT TXOP is obtained on the 80MHz bandwidth segment which is the earliest to have PBT backoff counts down to zero

## Slide 14: Non-AP STAs’ operation in PBT Operation
Non-AP STAs park on different 80MHz band and decode EHT-SIG from the U-SIG of that 80MHz [2] to receive resource allocation information or trigger information from the AP.
  The AP knows which non-AP STAs are monitoring preamble on which 80MHz bandwidth segment
  The non-AP STAs do not need to switch channels
  The non-AP STAs will update its NAV based on the 80MHz bandwidth segment
A non-AP STA parking on the specific non-primary 80MHz can receive downlink transmission or be triggered for uplink transmission only
  No contention among the AP and its associated non-AP STAs on non-primary 80MHz channel
A non-AP STA parking on the non-primary 80MHz channel needs to switch back to the primary 80MHz channel if it wants to contend the medium for uplink transmission

## Slide 15: PBT is no harm to STAs monitoring on the primary channel
PBT does no harm to STAs monitoring on the primary channel if AP moves to transmit on a different channel after detecting the primary channel as busy
  AP can configure the threshold for it to move to idling non-primary channels so that most associated non-AP STAs parking on the primary channel may also be blocked.
  Some non-AP STAs might still transmit on the primary channel, but the transmission would have failed due to high interference on the AP side.

## Slide 16: PBT is fair to OBSS transmission
PBT provides more restrict channel access by doing backoff on non-primary channel(s) instead of just PIFS ED check
  The current wideband transmission rule only follows NAV and full backoff on the primary channel and does PIFS ED check on all non-primary channels.
  If the ongoing OBSS PPDU does not occupy all the wide bandwidth (eg. 320MHz), the PBT scheme requires an AP to backoff on non-primary channel(s) and do PIFS ED check on other non-primary channels.

## Slide 17: PBT follows Regulatory Rules
The PBT follows the regulatory rules and allows EHT to compete fairly with competing technologies!
  A competing system allows the use of any combination/grouping of 20 MHz Operating Channels if channel access requirements are satisfied on each of the 20MHz operating channel

## Slide 18: Improvement of the Utilization of Idling Radio Resources
To reduce possible collisions on the idling non-primary channels for DL and triggered based UL transmission when primary channel is busy
  AP can use RTS/CTS before downlink data transmissions.
  Non-AP STAs parking on non-primary channels for trigger-based uplink transmissions check virtual CS before responding to the trigger frame

## Slide 19: Summary
To increase spectrum utilization in a wide band system and improve quality of services for low latency applications, partial bandwidth transmission opportunities are discussed
We proposed a PBT operation to allow a partial bandwidth transmission on the non-primary subchannels to share the medium with OBSS or other system
The fairness issues among OBSS and between 802.11 and other competing technologies are discussed
The utilization efficiency of idling channels is also discussed

## Slide 20: SP1
Do you agree that partial bandwidth transmission opportunities should be considered when the primary channel is blocked?

## Slide 21: Reference
[1] “ETSI EN 301 893 V2.1.1”
[2] 11-20-0380-00-00be-u-sig-structure-and-preamble-processing, Qualcomm