## Slide 1: Block Acknowledgment for EHT
Date: 2020-03-15
Authors:

## Slide 2: Introduction
Baseline block ack sessions use 64-long BlockAck bitmaps
  These bitmaps are carried in a Compressed (C-) BlockAck frame
HE introduced BlockAcks with up to 256-long BlockAck bitmaps
  Carried in C-BlockAck and a newly defined Multi-STA (M-) BlockAck
In addition, HE introduced Multi-TID A-MPDU as well
  For which M-BlockAck frames are used as control responses

## Slide 3: Considerations for EHT
EHT is increasing significantly the achievable throughput due to
  Increase of BW to 320 MHz, SSs to 16, QAM constellation to 4K,
  Introduction of multi-link operation, etc.
In order to efficiently acknowledge A-MPDUs at these higher rates
  We propose to increase the BlockAck bitmap sizes
    Add 512, 1024, 2048 options to the existing pool of options
    Focusing on 512 and 1024 for release 1
    With remaining options to be discussed during release 2

## Slide 4: C-Block Ack frames
C-BlockAck frames are individually addressed to STAs
  Currently have the option of acknowledging 64 or 256 bitmaps
    Fragment Number subfield values in SSC indicate length of Bitmap
  Proposal is to introduce another two options 512 and 1024
    Use same signaling (Fragment Number) to indicate the new lengths
      2 reserved values available when Fragmentation is OFF
      8 reserved combinations available when B3 is set to 1
Note:
  Currently recipient STA chooses BA’s Bitmap length depending on RX’ed A-MPDU
  We propose to have explicit indication from the originating STA
    E.g., Include solicited Bitmap size in A-Control field or within C-BAR frame
    Beneficial for originating STA to correctly set the NAV, etc.

## Slide 5: M-Block Ack frames
M-BlockAck frames may be broadcasted to many STAs
  Currently have 5 options of acknowledging (A-) MPDUs
    Per AID TID Info fields and Fragment Number indicate length of Bitmap
  Proposal is to introduce another two options 512 and 1024
    Use same signaling (Fragment Number) to indicate the new lengths
      8 reserved combinations available when B3 is set to 1
  Backwards compliance for M-BA: HE STA doesn’t understand new sizes
    Option 1: Create longer bitmaps by concatenating Per AID TID Info fields
      E.g., 1 K bitmap using 4 bitmaps of 256 (with same AID value)
    Option 2: Exclude HE STAs from newly formed M-BA (e.g., use another MAC address for broadcast)
Note :
  Same considerations as C-BA apply here as well, but in addition
    Indicate explicitly Bitmap sizes for each TID in a multi-TID A-MPDU

## Slide 6: SP1
Do you agree with the following:
  In 11be spec, add 512-long BlockAck bitmap and 1024-long BlockAck bitmap

## Slide 7: SP2
Do you agree with the following:
  In 11be spec, use some of the reserved values of the Fragment Number field to indicate the added bitmap lengths (512 and 1024). This applies to both the C-BlockAck and M-BlockAck frames