## Slide 1: Block Acknowledgment for EHT
Date: 2020-03-15
Authors:

## Slide 2: Introduction
Baseline block ack sessions use 64-long BlockAck bitmaps
  These bitmaps are carried in a Compressed (C-) BlockAck frame
HE introduced BlockAcks with up to 256-long BlockAck bitmaps
  Carried in C-BlockAck and a newly defined Multi-STA (M-) BlockAck
In addition, HE introduced Multi-TID A-MPDU as well
  For which M-BlockAck frames are used as control responses

## Slide 3: Considerations for EHT
EHT is increasing significantly the achievable throughput due to
  Increase of BW to 320 MHz, SSs to 16, QAM constellation to 4K,
  Introduction of multi-link operation, etc.
In order to efficiently acknowledge A-MPDUs at these higher rates
  We propose to increase the BlockAck bitmap sizes
    Add 512, 1024, 2048 options to the existing pool of options
      Focusing on 512 and 1024 for release 1
      Other options can be discussed for release 2.

## Slide 4: C-Block Ack frames
C-BlockAck frames are individually addressed to STAs
  Currently have the option of acknowledging 64 or 256 bitmaps
    Fragment Number subfield values in SSC field indicate BA Bitmap length
  Proposal is to introduce another two lengths: 512 and 1024
    Use same signaling (based on Fragment Number) to indicate the new lengths
      There are 2 reserved combinations available when B3=0
      There are 8 reserved combinations available when B3=1
Note:
  Currently RX STA chooses the Bitmap length based on RX’ed A-MPDU
    It is beneficial for originating STA to provide an explicit indication of it
      E.g., include solicited Bitmap length in A-Control field of soliciting MPDUs
      And additionally include it in a soliciting (MU-)BAR frame [1]
    Helps originating STA to correctly set the NAV,
    Helps RX STA generate BlockAck response with correct Bitmap length, etc.

## Slide 5: M-Block Ack frames
M-BlockAck frames may additionally be broadcast to many STAs
  Currently have 5 options (32, 64, …) of acknowledging (A-)MPDUs
    The BA Bitmap length is provided in each “Per AID TID Info” fields
      Fragment Number subfield values in SSC field indicate each BA Bitmap length
  Proposal is to introduce another two lengths: 512 and 1024
    With particular attention that the solution need be backward compliant
      Since HE STA doesn’t understand new BA Bitmap lengths
  Note:
    Similar considerations regarding the RX STA choosing BA’s Bitmap length depending on RX’ed A-MPDU apply here as well,
      Hence it is beneficial to explicitly indicate solicited Bitmap length,
      However, this indication would need be for each TID in a multi-TID A-MPDU
In the next slides we discuss several options for M-BA

## Slide 6: M-Block Ack frames (Cont’d)
Option 1: Create longer bitmaps by concatenating “Per AID TID Info” fields addressed to the same EHT STA
  E.g., 1 K bitmap can be obtained by using 4 bitmaps of 256
    The AID subfield in each Per AID TID Info field is set to the same value
    A reserved value in Fragment Number can indicate there are more “Per AID TID Info” fields to follow for the same EHT STA
      Helps with parsing, however, it is not strictly necessary
  Each “Per AID TID Info” field should include the “Block Ack Starting Sequence Control” of the 256-bit bitmap block being acknowledged

## Slide 7: M-Block Ack frames (Cont’d)
Option 2: Create longer bitmaps by adding new BlockAck Bitmap lengths (same concept as C-BlockAck frame case)
  Use Fragment Number signaling to indicate new lengths (512 or 1024)
    8 reserved combinations available when B3 is set to 1
The following options would avoid parsing errors by HE STAs (i.e., preserve backward compatibility)
  Ensure that no HE STA is the intended recipient of an M-BA that would contain the new BlockAck Bitmap lengths (simplest and preferred)
    HE STA is not expected to parse M-BAs that are not responses to sent (A-) MPDUs
  Place all “Per AID TID Info” fields corresponding to EHT STAs after “Per AID TID Info” fields corresponding to HE STAs
    An HE STA should stop parsing the “Per AID TID Info” fields corresponding to the EHT STAs once it reads the Fragment Number is set to a reserved value
    Requires pre-ordering for SIFS-generated frames, which is not preferred

## Slide 8: Conclusion
For R1, should add 512 and 1024 as new bitmap lengths
For C-BA, use some reserved values in the FN fields to indicate 512 and 1024 bitmaps
For M-BA, there are two options as follows:
  Option 1: Concatenate the “Per AID TID Info” fields to create 512 and 1024
    Some risks of Option 1 for pre-11be STAs
    Higher overhead due to repetition of identical info
    Really not needed for unicast M-BA
  Option 2: will be backward compatible and lower overhead
    Preferred option for the M-BA case

## Slide 9: SP1
Do you agree to add to the TGbe SFD:
  The spec shall define 512-long BlockAck bitmap and 1024-long BlockAck bitmap

## Slide 10: SP2
Do you agree to add to the TGbe SFD:
  For a Compressed BlockAck frame, use some of the reserved values of the Fragment Number field of the BlockAck frame to indicate the added bitmap lengths (512 and 1024).

## Slide 11: SP3
Do you agree to add to the TGbe SFD:
  For a M-BlockAck frame, add support for 512/1024 bitmap lengths by:
    Including new BA Bitmap lengths (of 512 and 1024 bits), where the length of the BA Bitmap field is signaled in the Per AID TID Info field addressed to an EHT STA
    The M-BA frame containing these Per AID TID Info fields is not sent as a response to an HE TB PPDU generated by at least one HE STA.

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/16/11-16-1028-01-00ax-cids-for-section-25-4-ba-variants.docx