## Slide 1: MLA: Non-STR STA Behaviors
Date: 2020-03-14
Authors:

## Slide 2: Terminology
STR (simultaneous Tx and Rx)
  An MLD that is capable of simultaneous Tx/Rx on multiple links for the given set of links
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on all links)

## Slide 3: Background and Problem Statement
In case of STR AP + non-STR STA
  When the STA is transmitting UL on the first link
    The STA will not be able to receive DL transmission on the second link
    The STA will not be able to continue count down on the second link either (we call this CCA blocked)
    We describe the STA is “deaf” on the second link during the period of transmission on the first link
Problem statement:
  When the transmission is finished on the first link, what should the STA do on the second link given that the STA has been deaf on that second link?
    Continue the count down immediately? Wait for a while to observe NAV first, etc.

## Slide 4: Option 1: Count Down Procedure after Link Gone Deaf
Reuse the existing Nav Sync procedure
  At the end of Link 1 Tx, start a countdown_prohibit timer (set to aPPDUMaxTime)
  If STA Tx on Link 1 while the countdown_prohibit timer is running, the timer is reset
  The countdown_prohibit timer is expired if STA2 successfully decode a preamble and/or NAV

## Slide 5: Option 2: Lowered ED Level
After the transmission ends on the first link, the ED Level of STA2 is reduced to -82dBm
  If STA2 misses some preamble transmission (by other STAs) that was within the PPDU1 transmission, STA2 would still detect a transmission on link 2 and NOT resume its count down

## Slide 6: Option 3: Cross-Link NAV Setting
After the PPDU transmission on link 1, AP1 send a BA
In the same BA, AP1 can include the NAV setting of AP2 and send it to STA1
STA1 can then indicate the NAV setting to STA2
STA2 will then update its NAV based on the received info

## Slide 7: Conclusion
We discussed the issue of the Non-STR STA
  When one of the links has finished transmission, what should the other link do when the it comes out of that state
We presented three options to solve the issue