## Slide 1: Multi-Link BA Bitmap Parsing Rule
Date: 2020-03-10
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Through multi-link aggregation, MPDUs that belong to the same TID can be transmitted on multiple links
In this case, the Block Ack (BA) frame transmitted on one link as a response to an A-MPDU may carry a bitmap that covers the acknowledgement status of the MPDUs that are transmitted on other links
It is also mentioned by many contributions that the BA frame transmitted on one link can carry the ACK information of the MPDUs that are transmitted on other links [1-4].
Based on this concept, we propose an acknowledgement scheme in this contribution.

## Slide 3: Motivation
Assuming MLD1 is using link1 and link2 to transmit MPDUs to MLD2, a BA frame is transmitted on link 1, and also carries the acknowledgement of the MPDUs transmitted on link 2.
By the time the BA is transmitted, some MPDUs may still be under processing, how does the MLD1 decide which MPDUs’ ACK status are carried in the BA?
E.g., the TX time of MPDU B5 is very close to the TX time of BA1, probably BA1 does not carry the ACK status of MPDU B5 due to the processing delay (especially in non-collocated multi-link case), but how does MLD1 know it?
MPDU A1
MPDU A2
MPDU A3
MPDU A4
MPDU A5
MPDU Ai
……
MPDU B1
MPDU B2
MPDU B3
MPDU B4
MPDU B5
MPDU Bj
……
BA1
MLD1
STA1
MLD1
STA2
MLD2
STA3
MLD2
STA4
Link 1
Link 2
ACK status not carried
Not sure ACK status carried or not
AMPDU 1
AMPDU 2

## Slide 4: Motivation
A simple way is: only trust the bit with value “1” for MPDUs transmitted on other links
When the data transmitter receives the BA, it can parse the BA bitmap according to the following rules:
  For a given bit in the bitmap
    If the corresponding MPDU is transmitted on the same link of the BA frame, then the bit is trusted
    If the corresponding MPDU is transmitted on a different link of the BA frame, then:
      If the bit is 1, then the bit is trusted
      If the bit is 0, then the bit is not trusted, and shall be ignored
The reason for ignoring the “0”-valued bits is, the data transmitter can not distinguish the following two cases:
  The corresponding MPDU is not decoded correctly
  The corresponding MPDU is still under processing (but may be decoded correctly later)
Due to the above mentioned limitation, we propose a further optimized rule to handle all the bits in the BA bitmap in this contribution, .

## Slide 5: Option 1
Option 1: PPDU based decision with fixed threshold
Rule: if an MPDU is carried in a PPDU which is transmitted on a different link of the BA frame, and the duration from the ending of the PPDU to the transmission time of the BA has exceeded MLIFS (multi-link inter frame space), then the ACK status of that MPDU is carried in the BA frame
BA1
MLD1
STA1
MLD1
STA2
MLD2
STA4
MLD2
STA5
Link 1
PPDU 1
PPDU 2
MLD1
STA3
MLD2
STA6
PPDU 3
Link 2
Link 3
MLIFS
ACK status carried in BA1
ACK status not carried in BA1
Note 1: the exact value of MLIFS is TBD
Note 2: the name of MLIFS can be changed

## Slide 6: Option 2
Option 2: MPDU based decision with fixed threshold
Rule: if an MPDU is carried in one or more OFDM symbols of a PPDU which is transmitted on a different link of the BA frame, and the duration from the ending of the last OFDM symbol that carries the MPDU to the transmission time of the BA has exceeded MLIFS (multi-link inter frame space), then the ACK status of that MPDU is carried in the BA frame
BA1
MLD1
STA1
MLD1
STA2
MLD2
STA3
MLD2
STA4
Link 1
PPDU 1
Symbol 2
Link 2
MLIFS
Symbol 3
Symbol 1
MPDU 1, 2
MPDU 3, 4
MPDU 5, 6
ACK Status not carried in BA1
ACK Status carried in BA1

## Slide 7: Option 3
Option 3: PPDU based decision with flexible threshold
Rule: if an MPDU is carried in a PPDU which is transmitted on a different link of the BA frame, and the duration from the ending of the PPDU to the transmission time of the BA has exceeded a time threshold T, then the ACK status of that MPDU is carried in the BA frame
The time threshold T can be announced by MLD2, during the BA setup procedure, in the ADDBA response frame.
Threshold T
BA1
MLD1
STA1
MLD1
STA2
MLD2
STA4
MLD2
STA5
Link 1
PPDU 1
PPDU 2
MLD1
STA3
MLD2
STA6
PPDU 3
Link 2
Link 3
ACK status carried in BA1
ACK status not carried in BA1

## Slide 8: Option 4
Option 4: MPDU based decision with flexible threshold
Rule: if an MPDU is carried in one or more OFDM symbols of a PPDU which is transmitted on a different link of the BA frame, and the duration from the ending of the last OFDM symbol that carries the MPDU to the transmission time of the BA has exceeded a time threshold T, then the ACK status of that MPDU is carried in the BA frame
The time threshold can be announced by MLD2, during the BA setup procedure, in the ADDBA response frame.
BA1
MLD1
STA1
MLD1
STA2
MLD2
STA3
MLD2
STA4
Link 1
PPDU 1
Symbol 2
Link 2
Threshold T
Symbol 3
Symbol 1
MPDU 1, 2
MPDU 3, 4
MPDU 5, 6
ACK Status not carried in BA1
ACK Status carried in BA1

## Slide 9: Comparison
It is easy to see that different option has different complexity
STA need to announce its capability of transmitting multi-link BA
There can be 3 different levels of capability:
Level 0: STA supports transmitting multi-link BA with no side information on the “0”-valued bits (the simple way in slide 4)
  In this level, the BA carries the ACK status of the MPDUs transmitted on the same link, and may additionally carry the ACK status of the MPDUs transmitted on other links
Level 1: STA supports transmitting multi-link BA based on PPDU (Opt1 & Opt3)
  In this level, the BA carries the ACK status of the MPDUs transmitted on the same link, additionally, it carries the ACK status of the MPDUs which are carried in the PPDU, and the duration from the ending of the PPDU to the transmission time of the BA has exceeded a given threshold.
Level 2: STA supports transmitting multi-link BA based on MPDU(Opt2 & Opt4)
  In this level, the BA carries the ACK status of the MPDUs transmitted on the same link, additionally, it carries the ACK status of the MPDUs which are carried in in one or more OFDM symbols of a PPDU, and the duration from the ending of the last OFDM symbol that carries the MPDU to the transmission time of the BA has exceeded a given threshold.

## Slide 10: Comparison
Regarding the given threshold,
  it can be a fixed value, e.g., MLIFS (multi-link inter frame space), which can be SIFS, PIFS, DIFS, or MLIFS can be announced by the AP, e.g., in the Beacon frame;
  it can also be a STA-specific value, it can be announced by MLD2, during the BA setup procedure, in the ADDBA response frame, or in the EHT capabilities element in the (re)association / authentication / probe frames.
Regarding different levels, STA can announce its supported level during the BA setup procedure, in the ADDBA frames, or in EHT capabilities element in the (re)association / authentication / probe frames.

## Slide 11: Conclusion
  We propose a multi-link BA bitmap parsing rule, under which the data transmitter can determine each bit in the BA bitmap as trustable or not.
  We propose 3 different ways of parsing the BA bitmap, which correspond to 3 different levels of capabilities.
  STAs can announce the capability of transmitting multi-link BA during the BA setup procedure.

## Slide 12: Straw Poll 1
  Do you support to define a multi-link BA bitmap parsing rule where each bit is treated as trustable or not according to the transmission time of the MPDU and the transmission time of the multi-link BA, if the bit corresponds to an MPDU which is transmitted on a different link than the link that is used to transmit the BA?

## Slide 13: Straw Poll 2
  Which option do you support to determine the transmission time of the MPDU?
  Opt1: the ending time of the PPDU that carries the MPDU
  Opt2: the ending time of the last OFDM symbol that carries the MPDU

## Slide 14: Straw Poll 3
  Do you support that an MLD can announce its processing delay to include in a BA frame the ACK status of an MPDU that is received on a different link than the link used to transmit the BA?

## Slide 15: References
  [1] 11-19-1856-00-00be-a-mpdu-and-ba
  [2] 11-19-1887-00-00be-multi-link-acknowledgement
  [3] 11-19-1532-01-00be-discussion-on-multi-link-acknowledgement
  [4] 11-20-0024-00-00be-mlo-acknowledgement-procedure