## Slide 1: NGV SIG CRC
Date: 2020-03-13
Authors:

## Slide 2: Introduction
NGV-SIG content bits are decided in Jan. meeting [1]
The 4-bit CRC generation is not specified.
Propose the method similar to 11ax for the 4-bit CRC generation.

## Slide 3: NGV SIG CRC
11ax SIG-A uses 4 bit defined in 27.3.11.7.3 (CRC computation).
  The same CRC generation method can be adopted for NGV-SIG with L=13.

## Slide 4: NGV SIG Table
Bit | Field | Number of bits | Description
B0-B1 | PHY version | 2 | Set 0 for 11bd, other three options are reserved for future generations.
B2 | Bandwidth | 1 | Set 0 for 10MHz, set 1 for 20MHz.
B3-B6 | MCS | 4 | MCS table
B7 | Nss | 1 | Set 0 for 1 ss, and set 1 for 2ss.
B8-B9 | Midamble Periodicity | 2 | Set 0 for 4 symbols, set 1 for 8 symbols, set 2 for 16 symbol. Value 3 is reserved.
B10 | LTF format | 1 | Set 0 for uncompressed LTF; set 1 for compressed LTF.
B11 | LDPC Extra OFDM Symbol | 1 | Set to 1 if the LDPC PPDU encoding process results in an extra OFDM symbol as described in 21.3.10.5.4 (LDPC coding). Set to 0 otherwise.
B12-B13 | Reserved | 2 | Reserved and set to 1.
B14-B17 | CRC | 4 | CRC calculated as in 19.3.9.4.4 (CRC calculation for HTSIG). 27.3.11.7.3 (CRC computation) by setting L = 13.
B18-B23 | Tail | 6 | Used to terminate the trellis of the convolutional decoder. Set to 0.

## Slide 5: Reference
[1] Rui Cao and etc., “NGV SIG content followup”, 11-20/0044r2.

## Slide 6: Straw Poll 1
Do you agree to incorporate the spec changes in 11-20/0452r0 into 11bd spec D0.3?
Y:
N:
A: