## Slide 1: NGV GI and LTF
Date: 2020-03-15
Authors:

## Slide 2: Introduction
NGV LTF_1x guard interval (GI) value is not specified yet.
Repeated NGV LTF_1x is not a useful format.

## Slide 3: GI for NGV LTF_1x
LTF_1x GI option is not specified.
  0.8us or 1.6us?
  To combat long delay spread, NGV-LTF-1x is evaluated with 1.6us GI in all compressed LTF/Midamble contributions [1, 2].
  In addition, the GI for data symbol is fixed to 1.6us.
We propose to use 1.6us GI for NGV LTF_1x.

## Slide 4: Repeated LTF_1x
LTF_1x is designed to improve preamble/midamble efficiency for high throughput case.
Repeated LTF is designed to improved channel estimation SNR for extended range case.
Repeated LTF_1x can not achieve either purpose.
Propose to remove Repeated LTF_1x format.
NGV LTF formats:
  LTF_2x: default format.
  LTF_1x: high-efficient format (Nss=1 only).
  Repeated LTF_2x: range extension format

## Slide 5: Reference
[1] Prashant Sharma and etc., “Midamble Compression”, 11-19/0685r2
[2] Yujin Noh and etc, “Compressed Midamble in NGV”, 11-19/1152r1

## Slide 6: Straw Poll 1
Do you agree that NGV LTF_1x uses 1.6us GI?
Y:
N:
A:

## Slide 7: Straw Poll 2
Do you agree that NGV does not support repeated LTF_1x?
Y:
N:
A:

## Slide 8: Straw Poll 3
Do you agree to incorporate the spec changes in 11-20/0454r0 into 11bd spec D0.3?
Y:
N:
A: