## Slide 1: Asynchronous multi-link operation for non-STR STA
Authors:
Name | Affiliations | Address | Phone | Email
Dmitry Akhmetov | Intel |  |  | 
Laurent Cariou |  |  |  | 
Das Dibakar |  |  |  | 
Notes: September 2012

## Slide 2: Recap [1, 2]:
In [1] we proposed classification of multi-link device operations based on channel access capabilities
  SPC – single primary channel operation; ~1.27x gain over single link
  MPC – multiple primary channel operation; ~2.09x gain over single link; preferable as it reuse existing channel access mechanism
  JMPC – join multiple primary channel operation; ~ 2.2x gain over single link
In [2] we discussed limitations raising from radio coexistence issues of co-located radios
  isolated (R)estricted MPC operation; ~1.9x gain over single link for DL case
  non-isolated (R)estricted MPC operation; ~1.6x gain over single link DL case
  MPC/Async mode still provide decent performance in terms of throughput for DL case while keeping ETE benefits for UL case
Based on [1] and [2] we conclude that in terms of Channel Access (or TXOP initiation) an asynchronous mode of operation a.k.a. Multiple Primary Channels mode (MPC) is preferable

## Slide 3: Recap [3, 4, 5]:
We focus on non-STR STA / STR AP case
We presented simulation results on Async performance in DL-only direction with the analysis of impact of non-STR STA response (BA on link1 ) to the RX process on link 2
  Corner case: 1 MLD AP + 1 MLD STA
    of ~1.5x – 1.8x vs single link
  Generic case: 1 AP + multiple STAs
    ~1.9x gain in case of partial AMPDU losses
    ~1.5x – 1.8x gain in case of lost the end of AMPDU
A several ideas on PPDU end alignment were discussed to solve/improve beforementioned problem
In [5] stated that DL-only is a rare use case and mix DL/UL mode need to be considered
  In mix mode for isolated 1 AP and 1 STA best performance achieved with sync (JMPC) access
  Synchronization is required to avoid staggering; otherwise UL throughput is destroyed
  PPDU alignment is claimed as a possible solution to the staggering problem

## Slide 4: Lowlight/downsides/bright sides of Sync/JMPC access
What is it:
  Sync, one primary channel and a secondary channel
    80+80 type of operation – already exist in a spec
    Contend on a dedicated primary channel/link, access to the medium on a “secondary\other\second” link by doing ED for PIFS time
  JMPC, multiple primary channels with join contention
    New mode that has to be defined in a spec
    All links contend for medium, access to the medium on another link a by doing ED for PIFS time
Why it is attractive
  Allow easy link aggregation in both DL and UL
  Seems to be a solution for non-STR operation – synchronous access which naturally align TX/TX and RX/RX operations
Why it is not attractive
  Regulatory restriction\prohibition on access to a medium with PIFS access
  Limited applicability
    Synchronous access only works in clean environment (no OBSS/legacy/hidden nodes around)
    JMPC is independent of environment but chances of join medium access are not high
  JMPC has fairness issues
  If implemented for Multi-Link operations may provide a door for channel access abuse

## Slide 5: Notes on DL and UL traffic coexistence
DL traffic :
  DL traffic prevail in a network, so addressing DL aggregation would be logically the first thing to do
  we assume AP MLD side does not suffer from leakages so DL might be easier to handle
  Simulation results shows that in DL only case w/o applying any special techniques we get decent performance
UL traffic
  is important, but much smaller comparing to DL traffic
  non-STR device is self aware about constraints and in most cases will be self-synchronized between links
  TX on one link stop/pause the other link – so device is naturally should does not hurt much self RX operations
So, separately DL and UL traffic are not a concern to each other in a communication between STR AP and non-STR STA

## Slide 6: Device capabilities are important to consider
There were a lot of contributions and discussions mentioning “device quality/integration”
Level of integration matters
  an MDL STA may or may not have capability to exchange information between instances in a timely manner
  Amount of shared information may vary greatly
    can signal only CCA status of a link
    Or can provide full MAC/PHY state (i.e. transmit address, current TX duration, TX data or expect response, etc)
    Or cannot share anything
Four possible corner cases considered in a following simulations
  iAP or iSTA – integrated AP/STA. An AP/STA that can share full internal MAC/PHY state within MLD device
    For example: a non-STR STA want to start a TXOP on link1, it may request link 2 status and transmit if link 2 PHY status is IDLE and MAC status is “Backoff” OR may not transmit if link 2 PHY status is IDLE but MAC status is “Expecting Ack”
    For example: an STR AP may to transmit on link 1 to non-STR STA1 if link 2 is receiving from STR STA2; OR it may not to transmit if MAC status on link2 is “sending CTS to non-STR STA1”; OR transmit to non-STR STA1 if MAC status of link 2“Sending data to non-STR 1”
  nAP or nSTA – non-integrated AP/STA. An AP/STA that has no sharing/communication capabilities
    Note: in case of non-STR device (i.e. device with leakage) we assume “involuntary” information sharing through CCA signals raised due to interference
    Note: an AP in such case cannot verify if it is talking to a non-STR device on another link

## Slide 7: Simulation assumptions
“Simplest” case, 1 MLD AP, 1 MLD STA
Two links, 1x1x80 @ MCS11
RTS/CTS on
Symmetrical saturated DL and UL traffic on each link of 600mbps in both directions
Results averaged over 10 simulation runs, 10 seconds each
iSTA/iAP behavior:
  Before starting TXOP on link 1 integrated device will check status of link 2
  AP/STA plan their TXOP with respect to PHY and MAC status of another link
nSTA/nAP behavior
  Devices are not aware about presence of link/status of the other link

## Slide 8: JMPC vs Async
JMPC (sync) obviously perform well for isolated 1 Ap 1 STA use case
  If both STA and AP are single-chip/tightly integrated/coordinated
Does not work if one side cannot do PIFS access to sync channel results
  IF AP has bad integration there in NO possibility for UL traffic aggregation
Async access “as is”, i.e. the “do nothing” provide some UL, i.e. see no staggering problem

## Slide 9: Do something (PPDU alignment)
In [3, 4, 5] we mentioned few way to achieve PPDU end alignment to avoid self interference (for DL aggregation), fight staggering and enable synchronization (for DL and UL aggregation)
  Option 1: Within device signaling assuming this signaling is possible
  Option 2: Over the air signaling in CTS frame
  Option 3: Artificial PPDU alignment to some slot boundaries known to AP MLD instances
  Option 4: Clever use of delayed BA
We consider Option 1 for iAP/nSTA and iAP/iSTA cases and Option 2 for nAP/iSTA case
Preferred\simple

## Slide 10: DL/UL mix with PPDU alignment
  improve UL traffic for completely integrated case, a more balanced traffic pattern
  “enable” nAP/iSTA case
  Can we do better and enable all cases?

## Slide 11: What seems more important for constrained devices:
Is to have a separation of DL and UL traffic in time
  To avoid uncontrolled DL/UL but to have only UL or DL over a period of time,
    As we have shown before DL case perform well for SRT AP – non-STR STA communication
    In turn, UL is “self-controlled” at non-STR STA (one link block the other preventing a mix of ops)
      It is a general understanding that STA, unlike AP, will have better/tighter link integration/interaction, so quick state signaling or operation management is possible
  A separation of DL and UL traffic would highly likely solve UL/DL mix use case where TX operation from a non-STR STA may interfere with TX operations of STR AP and vice versa
  Traffic separation is a natural solution to enable all/most possible combinations of AP/STA levels of integration

## Slide 12: Per link DL \ UL traffic separation
Few possible options to organize that:
  TWT negotiation to say only DL/Triggered UL or only EDCA based UL during the SP
  Or a signaling so that STA controls when DL can start or not , e.g.,
    STA stays in “DL Rx unavailable” state in both links during EDCA based UL transmission so that AP does not transmit DL frames during that state
    STA comes out of that state to be able to receive DL packets on both links
    May require changes to existing PSM signaling to cover some cases (e.g., U-APSD).
  Or may be have special rules to disallow certain operation on links per TXOP basis
    For instance, mandate RTS/CTS exchange when talk to/from non-STR device and have special rules for CTS response to indicate STA unavailability for operation on a certain link during TXOP
Simulation parameters for traffic separation
  DL duration period : 0.1s
  UL duration period : 0.1s
  Consider in MPDU/BA signaling

## Slide 13: DL-Rx unavailable state
The STA can signal when it is unable to receive DL frames by a one bit signaling in UL frames (incl. Data or BA frames).
On reception of this frame and after Acking, the AP does not transmit any DL Data frames to this STA regardless of the power state and modes of that STA starting the end of current TXOP
By default the signaling is done independently on all links.
Link 1
AP MLD
AP 1
AP 2
Non-AP MLD
STA 1
STA 2
Link 2
time
: U-APSD SP
: STA in Doze
: UL Data
: Ack
Suspend DL Data frames
: DL Data
DL-Rx Available = 0
DL-Rx Available = 1
Notes: Alternatively, a softer AP behavior will be that the STA is requesting the AP to do RTS-CTS prior to every DL Data frame transmission.

## Slide 14: Traffic separation vs PPDU alignment vs Do nothing
  Traffic separation naturally enable traffic in all 4 possible cases

## Slide 15: Conclusion
Traffic separation enable traffic in both directions in case of DL/UL mix for all observed configurations
PPDU end alignment enable nAP/iSTA case and improve UL throughput in iAP/iSTA case
Amount of shared information/level of AP/STA integration greatly affect results and need to be explicitly considered/mentioned in behavior analysis
  Having asymmetrical setup, like iAP/nSTA or nAP/iSTA, harm overall system behavior
JMPC work only in one case – when devices have full information and able to grab medium at the same time
  Both parties shall be able to synchronize their start of PPDU not always possible
  Synchronization is an issue in congested environment

## Slide 16: Straw poll 1
Do you agree as a part of R1 spec to
  Define a way to enable end of PPDU alignment in DL to a non-STR non-AP MLD
  Define a way for the for non-AP STA to indicate its unavailability (doze state or unavailable) at any time, including in BA
    Note: Following that indication, the AP will not transmit to the STA data frames in DL, while the STA will be able to transmit data frames in UL
  Define a service periods where data frames are sent only in DL or only in UL direction

## Slide 17: Straw poll 2
Do you agree as a part of R2 spec to develop a mechanisms for non-AP MLD with constraints to enable simultaneous transmission of PPDUs overlapping in time on multiple links

## Slide 18: References
[1] 11-19-1291-03-00be-some-aspects-of-multi-link-op-performance, Intel
[2] 11-19-1541-01-00be-performance-aspects-of-multi-link-op-with constraints, Intel
[3] 11-20-0081-00-00be-mlo-synch-transmission, Broadcomm
[4] 11-19-0106-02-00be-discussion on multi-link operation with leakage on non-AP MLD, Intel
[5] 11-20-0275-00-00be-need-for-sync-ppdu, Qualcomm
[6] 11-20-0026-01-00be-MLA Support for Constrained Devices, Qualcomm
[7] 11-19-1928-01-00be-multi-link-operation-performance-evaluation, Mediatek

## Slide 19: Backup

## Slide 20: Risks with a sync mode
We don't want to break backoff rules and allow an AP that is in synch on a channel with other contending STAs to be able to ignore backoff and just follow NAV + CCA
  This is different from secondary channel access, as the STA accessing secondary channel is not in synch with the other contending STAs (does not know when the CP occurs). The “other” link is an independent link with independent channel access aligned with other devices operating on that link
  There are regulatory restrictions to do PIFS access on independent channel/link
Risks of unfairness if we go full-sync direction:
  A sync AP MLD with an AP1 alone on link 1 and with an AP2 sharing medium with other AP(s) on link2.
  If that AP1 carefully chooses TxOP duration on link 1 to always end (Backoff time) before TxOP on link2, so that AP1 ends backoff right at the start of the CP on link 2: this way, link2 is always gained by the AP2.
  Basically if we allow this mode, there is a clear potential abuse.