## Slide 1: Tx EVM Requirement for 4k QAM
Date: 03/12/2020
Authors:
Name | Affiliation | Address | Phone | Email
Yaron Yoffe | Intel |  |  | Yaron.Yoffe@intel.com
Shlomi Vituri |  |  |  | Shlomi.Vituri@intel.com
Qinghua Li |  |  |  | Qinghua.Li@intel.com
Feng Jiang |  |  |  | 
Xiaogang Chen |  |  |  | 
Assaf Gurevitz |  |  |  | 
Uri Perlmutter |  |  |  | 
Gadi Shor |  |  |  | 
Laurent Cariou |  |  |  | 

## Slide 2
4k QAM boosts the peak data rate but requires high EVMs
However, there is a tradeoff between EVM and transmission power
In this contribution, we show the EVM requirements for 4k QAM
Problem Statement
Mar 2020
Y. Yoffe, et. al, Intel

## Slide 3
80 MHz channel, fading Channel D
4x2 SU MIMO with 4 Tx antennas, 2 Rx antennas, 2 streams
Beamforming applied
Common Usage Scenario
Mar 2020
AP
STA
Beamforming
Y. Yoffe, et. al, Intel

## Slide 4
It includes channel estimation errors and is 3 dB worse than the actual distortion at the transmitter
It is modeled as AWGN, which is the worst case
EVM due to phase noise can be mostly cancelled by pilot tracking
Tx EVM
Mar 2020
MCS Parameters
Highest MCS with 4k QAM and LDPC 5/6
4k bytes per packet, 20 packets per PPDU
Y. Yoffe, et. al, Intel

## Slide 5
With ideal channel estimation
Mar 2020
Y. Yoffe, et. al, Intel
Curve spacing gets smaller
and smaller

## Slide 6
With LTF based channel estimation
Mar 2020
Y. Yoffe, et. al, Intel
Curve spacing gets smaller
and smaller

## Slide 7
Degradation is with respect to no EVM case
It gets harder and harder to reduce the degradation as the EVM approaches zero. Namely, each dB of EVM drop produces less and less degradation drop e.g. 0.1-0.2 dB per EVM dB drop.
Degradation vs. EVM
Mar 2020
Y. Yoffe, et. al, Intel
Tx EVM (dBc) | Degradation with ideal channel (dB) | Degradation with estimated channel (dB)
-36 | 1.1 | 1.1
-37 | 0.9 | 0.8
-38 | 0.7 | 0.6
-39 | 0.5 | 0.5
-38 EVM is a good choice balancing Tx power and distortion

## Slide 8
Phase noise effect with ideal channel estimation
Mar 2020
Y. Yoffe, et. al, Intel
Low frequency phase noises are cancelled by removing
the common phase rotation
Phase noise power is calculated from 10k – 200 MHz and normalized with respect to the total power of the other distortions

## Slide 9
-38 dB Tx EVM is a reasonable choice
Degradation is small i.e. about 0.6 dB from the ideal
Further EVM reduction may require additional Tx power reduction that shortens the 4k QAM usable range
Conclusion
Mar 2020
Y. Yoffe, et. al, Intel

## Slide 10
Do you support -38 dB as the Tx EVM requirement for 11be 4k QAM?
  Y: N: A:
Straw Poll
Mar 2020
Y. Yoffe, et. al, Intel

## Slide 11
Backup
Mar 2020
Y. Yoffe, et. al, Intel