## Slide 1: Priority Access Support Option for NS/EP Services
Date: 2020-03-15
Authors:

## Slide 2: Outline
This presentation covers the following:
  Overview of NS/EP Priority Services
  Assumptions
  An approach for indicating the priority access need for NS/EP Priority Service non-AP STA(s) to AP STA using OFDMA-based Triggered Uplink Access framework

## Slide 3: Overview
Priority access support for National Security and Emergency Preparedness (NS/EP) priority services was approved as a work item in IEEE 802.11be during January 2020 meeting [1]
Objective Summary
  A standardized mechanism to support the NS/EP priority services in WLANs without requiring additional infrastructure
  Priority Access in IEEE 802.11be would also be beneficial to other services ( e.g., Public-Safety Mission-Critical Services, Critical medical applications)

## Slide 4: NS/EP Priority Services
Service Objective: Provide priority access to system resources for a limited set of authorized users during network congestion
  Priority Access: Allow preferred access to the wireless medium during network congestion and/or failures to establish a data session
  Limited Set: Number of users is generally a small fraction of the overall user base
  Authorized Users: Only available to some designated individuals who are identified to receive such service
Existing NS/EP Priority Services in the US provide priority voice calls over public networks
  Government Emergency Telecommunications Service (GETS): Landline phone networks
  Wireless Priority Service (WPS): Wireless phone networks
  Next Generation Network Priority Services (NGN-PS): Providers’ IP-based communications networks
Many countries have similar priority telecommunications services, e.g.,
  Belgium: Blue Light Mobile, Canada: WPS, Czech Republic: Mobile Crisis Communications service, Great Britain: MTPAS
  GSM for Railway Communications deployed in multiple countries
NS/EP Priority Services are NOT Emergency Services (e.g., E911 in US; 112, 999, etc. in Europe)

## Slide 5: Assumptions
NS/EP Priority Service user’s non-AP STA is associated with BSS prior to invocation of priority capabilities
  Authentication/Association and authorization occur via standard procedures
After association, AP STA has the knowledge of which non-AP STAs are authorized to use NS/EP priority services
NS/EP Priority Service non-AP STA will inform the AP STA regarding the need for Priority Service
  Mechanism for communicating the need for priority access to the AP STA is the focus of this presentation.
    The method of identifying the need for priority access is out of the scope of TGbe
  The priority remains in effect until terminated by either party
NS/EP Priority Service non-AP STA supports UL MU-MIMO operation

## Slide 6: Realizing NS/EP Priority Service Concept
NS/EP non-AP STA associates with AP STA
  Managed AP/AP Controller retrieves user’s NS/EP priority attributes (e.g., user priority level, credentials, etc.) during association
  Managed AP/AP Controller verifies authorization to use NS/EP priority service via access/service provider
  Managed AP/AP Controller caches the non-AP STA’s NS/EP priority service profile
Non-AP STA user indicates* priority for a NS/EP session on-demand (e.g., when experiencing poor network performance) by signaling the need for priority access
  Mechanism for determining the need for invoking this service is out of scope
  Goal of NS/EP priority is to support existing access-category QoS even under congestion (e.g., serve NS/EP non-AP STAs first)
Non-AP STA user deactivates NS/EP priority service when priority is no longer needed
  e.g., session is over, network conditions return to normal
* Note: This is low-frequency event due to limited use for NS/EP purposes (Ref[1])

## Slide 7: Network Architecture (Simplified)
Regular STA
AP
AP
Access Controller/
Gateway
NS/EP Authorized STA
Wi-Fi Access Provider
Core Network
The service provider and/or the access provider are(is) responsible for identifying, authenticating and authorizing a NS/EP STA for priority access
  The capabilities are exchanged during authentication/association
  The additional element in ‘Capability IE’ is TBD
STA- Wi-Fi Device
AP- Wi-Fi Access Point
AAA

## Slide 8: Proposed Approach
Use existing BSRP Trigger Frame and extend QoS Control Field format to indicate the NS/EP Priority Service non-AP STA’s Priority Access need in buffer status report

## Slide 9: Use of OFDMA .11ax Triggered Uplink Access for NS/EP Priority Services
Enabling priority in OFDMA scheduling (in presence of network congestion)
  AP STA polls non-AP STAs using BSRP Trigger Frame to determine data to be sent upstream
    Subsequent messages may not require a Trigger Frame
  NS/EP Priority Service non-AP STA reports access class and buffer status with priority indication
    Proposed enhancement enables STA to provide priority indication
  AP STA verifies authorization for NS/EP Priority Service
  AP STA incorporates priority into scheduling and RU-allocation decisions for NS/EP Priority Service non-AP STA

## Slide 10: QoS Control Field Format for IEEE 802.11ax
QoS Control field
  QoS Control field enables non-AP STA to report the buffer status after receiving the Trigger Frame (e.g., BSRP) poll from an AP STA
    Non-AP STA can send multiple QoS Control fields to indicate requirements for multiple TCs
  Non-AP STA sends QoS Control field with TID and Queue Size in QoS Data or QoS Null frame
    TID (4 bits) maps to User Priority (UP) value
    UP Values 0-7 are assigned
      Values from 8 to 15 are not used in buffer status report in .11ax
QoS Control Field Format
1
A-MSDU Present
Queue Size
Ack Policy
TID

## Slide 11: Proposed Approach: Use QoS Control Field
Encode priority in QoS Control field TID
  Rationale: Only values 0-7 (3 bits) are used to indicate UP (mapped to AC)
  Proposal: Use one value >7 of 4-bit TID to indicate the need for NS/EP Priority Services
    Use TID= 1101 (13) to indicate that the Priority Service is required
      NS/EP Priority Service non-AP STA sets TID=1101 in QoS control field while sending the buffer status report in response to a BSRP trigger poll frame.
    In case non-NS/EP Priority Service STAs set TID= 1101 in buffer status report, AP will be able to deny the Priority Access based on the authorization information.
    If one QoS Data or Null frame within an A-MSDU has as TID of 1101, all other queues are treated as priority.
  Impact:
    Legacy STAs will not be able to decode this information but this should not be an issue since MIB can be updated to address the backward compatibility.
QoS Control field Format
1
A-MSDU Present
Queue Size
Ack Policy
TID=1101
(Priority Service Indicator )
bits 0-3
bit 4
bit 7
bits 5-6
bits 8-15

## Slide 12: NS/EP Priority Access Procedures
AP polls the STAs using BSRP Trigger Frame to determine data to be sent upstream.
At time t₁, the NS/EP STA determines the need for priority and sets the TID value to 1101 of QoS control field while sending the subsequent buffer status report in response to a BSRP trigger frame as an indication to the AP (with which it is associated) that the Priority Access is required
After receiving the Priority Access indication, AP verifies the STA’s authorization information (AP has this knowledge during authentication/association)
NS/EP STA Capability Information
AP
NS/EP STA (EHT)
Frame carrying BSRP Trigger
Ack
Frame Carrying Trigger with RUs allocated to NS/EP STA
EHT TB PPDU with UL Data
Ack
Capability exchanged during Association
Time = t₁
Frame carrying BSR in QoS data and/or null frame with TID value set to 1101

## Slide 13: NS/EP Priority Access Procedures Contd..
If the STA is authorized to obtain the service, AP prioritizes the RU allocation to the NS/EP STAs for UL/DL transmissions similar to .11ax procedures. RUs can be assigned to one or more NS/EP STAs based on buffer status
The NS/EP STAs access these resources (slots) to gain the prioritized access
As long as the STA identifies the need for priority, it continues to include a QoS control field with the TID value set to 1101 in QoS data and/or null frames. If it determines that the priority treatment is no longer needed, it stops including this TID value in the QoS control field

## Slide 14: Additional Clarifications
BSR containing QoS frame with TID > 7 is proposed to signal that NS/EP non-AP STA requires Priority Access (i.e., to turn the service on)
  Presence of such frame indicates that data in NS/EP STA buffers should receive priority over other non-AP STAs
  Absence of such frame indicates that data in NS/EP STA buffers should receive same treatment as other non-AP STAs
A single TID value signals the need for Priority Access
  In particular, it is not mapped to any specific access class
  Mapping of the TID value to an access class at the AP STA is an implementation issue
  Other QoS data frames reported in BSR use existing TIDs (<7) to indicate the AC
  NS/EP Priority Service is not a low latency service
Specific TID value > 7 is TBD
  Value of 13 is proposed since it is the next highest unused value available
  May be possible to reuse TID=15 (currently used in .11ax m-BA) by defining appropriate procedures

## Slide 15: Summary
Described a simple approach by which NS/EP Priority Service non-AP STAs can signal the AP STA that priority access is required during network congestion
  Leverages existing BSRP Trigger Frame
  Use of one TID value in buffer status report
  No other existing mechanisms need to be modified
  Backward compatible
Feedback and comments ??

## Slide 16: Straw Poll 1
Do you support the addition of following text to TGbe SFD?
  The NS/EP Priority Service if supported by a non-AP STA, shall use a TID value >7 to indicate the need for priority access to AP STA
    Note: The identification of the need is outside the scope of this specification.
    Note: The container of the TID is TBD.
Y:
  N:
  A:

## Slide 17: References
[1] 11-19-1901-04-00be-priority-access-support-in-ieee-802-11be-what-and-why.pptx
[2] 11-20-0021-01-00be-Priority-Access-support_for_NS_EP_Services.pptx,
[2] IEEE P802.11ax™/D6.0, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 1: Enhancements for High Efficiency WLAN”, November 2019
[3] IEEE Std 802.11™-2016, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 7 December 2016