## Slide 1
Authors:
Multi-Link Channel Access Discussion
Date: 2020-03-16
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the carrier sensing and channel access mechanism in Multi-Link communication to support high priority/low latency services.

## Slide 3: Background
Re-cap of support low latency requirements (1)
  802.11be PAR and CSD [1][2] indicate that
    This amendment defines at least one mode of operation capable of improved worst case latency and jitter.
    This amendment aims to build on the current and emerging WLAN technologies by providing further improvement of aggregate throughput and latency to ensure competitiveness of IEEE Std. 802.11 in coming years.
    This project will improve the latency and jitter of WLAN.

## Slide 4: Background
  Re-cap of support low latency requirements (2)
  In the SFD of 802.11be [3], it indicates that
    802.11be amendment shall define mechanism(s) in support of priority access to a non-AP STA for national security (NS)/emergency preparedness (EP) priority service
    802.11be shall allow the following asynchronous multi-link channel access:
      Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.
      Downlink and uplink frames can be transmitted simultaneously over the multiple links
    802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links.

## Slide 5: Background
Support low latency application with ML
  [4] describes the requirement for 802.11be to support low latency application.
    A non-AP MLD should perform the channel access on multiple channels to find and acquire the earliest available link(s) to transmit the low latency data packet over this link.
  This indicates that the CCA should be performed on each link independently to find the earliest available channel.
  In this contribution, we will follow-up this and discuss the ML channel access for the MLD cable of STR (simultaneous transmission and reception)
Link 2 (CH2)
Link 1 (CH1)
Link 3 (CH3)
The earliest available channel (in the idle)
CH Busy
CH Busy
CH Busy
Transmits a PPDU over CH3
Pending data to be sent
T0
Time
T1
T2

## Slide 6: Channel Access for STR
  Independent ML EDCA Backoff
  A STR capable MLD has multiple individual CCA sensors and backoff counters.
    Each STA of MLD has its own backoff counters for counting idle slots. When a STA of MLD performs CCA and detects the channel idle, its backoff counters associated to this STA are reduced by “1”, till reaching to “0”.
  When a backoff counter of the STA reaches to “0”, and NAV is not set, the STA of MLD performs channel access on this link.
  The approach will allow each STA of MLD to sense the channel and perform the channel access independently.
Link 2 (CH2)
Link 1 (CH1)
Link 3 (CH3)
The earliest available channel (in the idle)
CH Busy (OBSS)
CH Busy (OBSS)
CH Busy (OBSS)
Transmits a PPDU over CH3
Pending data to be sent
T0
Time
T1
T2
BFC 1
BFC 2
Transmits a PPDU over CH2

## Slide 7: Channel Access for STR
  Joint ML EDCA Backoff
  A STR capable MLD has multiple individual CCA sensors, but shares the same set of backoff counters, i.e.
    A STA of MLD performs CCA on its operating channel independently from other STAs.
    All STAs of MLD uses the same set backoff counters to count an idle slot in CCA. If any STA detects the channel idle, the backoff counters are reduced by “1”, till reaching to “0”.
  When the backoff counter reaches to “0”, and NAV is not set, the MLD can perform a channel access on this link.
  The joint ML EDCA backoff will reduce waiting time significantly and expedite a MLD to access to the earliest available channel(s) when multiple channels are available.
Link 2 (CH2)
Link 1 (CH1)
Link 3 (CH3)
The earliest available channel (in the idle)
CH Busy
CH Busy
CH Busy (occupied by another MLD)
Transmits a PPDU over CH3
Pending data to be sent
T0
Time
T1
T2
BFC
Transmits a PPDU over CH2

## Slide 8: Straw Poll
Do you support to include the following in SFD ?
  STAs of MLD may use the joint backoff counters during EDCA process on multi-links for HP/LL transmissions.
YES/NO/ABS

## Slide 9: References
[1] 11-18-1231-06-0eht-eht-draft-proposed-par
[2] 11-18-1233-07-0eht-eht-draft-proposed-csd
[2] 11-19-1262-07-00be-specification-framework-for-tgbe
[3] 11-19-1095-01-0eht_multi-link_requirement_discussion

## Slide 10
Thank you!