## Slide 1: HCFA Example
Date: 2020-03-17
Authors:

## Slide 2: Abstract
This presentation is a supplemental information for HCFA (11-20/0040r3).

## Slide 3: Feedback for 11-20/0040r3
HCFA is faster but it is not clear if it would be able to handle stream with high number of frames going out continuously. In addition, the concept of using hash value from a frame that will be transmitted at a later time can be a problem. In most implementations, all high throughput encryption is performed in hardware which works in-line with the actual transmission of a frame. Such implementations won't work if they have to rely on receiving a future frame. In addition, it will add a significant burden on the memory requirement (esp. true for high thruput cases).
It would be good to have a presentation that estimates how high a throughput (number of frames/second) this scheme is expected to handle. This will help the group determine how realistic it would be to implement the part that generates eBCS Data frames in hardware.

## Slide 4: HCFA Procedure
Transmitter
With Instant Authentication
  Transmitter requires to buffers the frames in 2 * TK
Without Instant Authentication
  Transmitter does not require to buffer frames
Receiver
Receiver requires to buffer the frames in 2 * TK
Hash
TK
TK
TK
TK
TESLA Authentication
Instant Authentication
TESLA key for

## Slide 5: Buffer Size Estimation
Assumptions
  Payload size: 1,400B
  Frame size: Payload (1,400) + .11 header (24) + HCFA overhead (128) + IP/UDP header (28) = 1,580B
  TK: 100ms
Full HD Video (1920 * 1080 30fps)
  12Mbps (AV1 level 4.0) = 1.5MB/s = 1,072frames/s
  Required buffer size: 1,580B * 1,072 * 0.2 = 339kB
4K Video (3840 * 2160 30fps)
  30Mbps (AV1 level 5.0) = 3.75MB/s = 2,679frames/s
  Required buffer size: 1,580B * 2,679 * 0.2 = 847kB
TK * 2 = 200ms