## Slide 1: Coordinated TXOP sharing in UL
Date: 2020-03-14
Authors:

## Slide 2: Abstract
TXOP sharing among APs could reduce worst-case latency
A protocol for coordination and sharing of frequency/time resources for DL transmission has been proposed [1]
In this contribution we discuss extensions to this protocol in order to support sharing of resources for UL transmission

## Slide 3: Recap
Coordinated AP sharing was proposed in [1]. There are two variants
  Frequency resource sharing (OFDMA)
  Time resource sharing (TDMA)
Gains are expected in terms of worst-case latency improvement
The sharing scheme in [1] seems to apply only to sharing of frequency/time resources for DL transmissions

## Slide 4: Coordinated TXOP sharing in UL
TXOP sharing in UL could also improve the worst case latency
A protocol similar to that described in [1] is not enough to enable TXOP sharing in UL
In order to support TXOP sharing in UL it is necessary to update the HE rules for setting of the NAV. The problem is illustrated in the next slide

## Slide 5: Illustration of TXOP sharing in UL with HE NAV rules
Suppose AP1 attempts to share (TDMA) a TXOP with AP2, following a protocol similar to [1]

## Slide 6: Summary
It is desirable to extend the benefits of coordinated AP sharing to UL transmissions
This can be achieved by slightly modifying the protocol described in [1]
There are some issues with NAV setting that would need to be resolved though

## Slide 7: References
[1] Lochan Verma et al. “IEEE 802.11 19/1582r1 Coordinated AP Time and Frequency Sharing in a Transmit Opportunity in 11be”, Nov 2019

## Slide 8: Straw poll
Do you believe that TGbe should extend the coordinated AP time/frequency resource sharing protocol described in [1] in order to support resource sharing for UL transmissions?
Y:
N:
A: