## Slide 1: Remark on PPDUs with midambles
Date: 2020-03-14
Authors:

## Slide 2: Abstract
This contribution discusses the design of the midambles in 11bd PDDUs
Specifically, to avoid discrete components in the spectrum which may limit the maximum output power, it is suggested to randomize the midambles

## Slide 3: Recap - Midambles in 802.11bd
TGbd has agreed [1]:
That the 11bd PPDU design shall support midambles with periodicity 4, 8
That a midamble comprises a Long Training Field (LTF)
To support up to two spatial streams

## Slide 4: Repeated deterministic signal components
In general, randomization or scrambling of repeated deterministic signal components is a good practice in wireless communications
Reoccurring deterministic signals are often randomized in 802.11 OFDM PHYs:
  Pilots are randomized
  The LTFs in MIMO PPDUs are randomized by means of the P matrix. For example the 6x6 VHT P matrix is not a DFT matrix but a modification in order to eliminate the row consisting of ones only.
  Padding bits are scrambled
  HE midambles seem to be the exception
Repetition of deterministic signal components leads to spectral lines  repetition of midambles leads to spectral lines

## Slide 5: Spectrum Requirements
The spectrum requirements for 802.11bd devices are uncertain at the time of writing this contribution, due to upcoming decisions by the FCC [2]
The FCC and other regulatory bodies typically impose limits on the PSD, in terms of the maximum power in a given band, requiring that the power spectral density conducted to the antenna shall not exceed X dBm / Y Hz
  For example in Section 15.247 of [3], X = 8 (dBm) and Y = 3000 (Hz)
The smaller the resolution bandwidth (i.e. the term “Y” in the previous bullet), the more expensive and time consuming become the tests
  This fact is recognized by regulators
Spectral lines may make it more difficult to fulfill PSD limits

## Slide 6: Randomization of the midambles in 802.11bd
It is suggested to randomize the midambles
Without randomization there can be a non-negligible concentration of the PSD in narrow bands
  Example: 10 MHz PPDU with 2 SS and midamble periodicity = 4: power in 3 kHz band increases up to 5.5 dB with respect to PPDU without midambles
  Example: 10 MHz PPDU with 1 SS and midamble periodicity = 4 : power in 3 kHz band increases up to 3.0 dB with respect to PPDU without midambles
  Example: 10 MHz PPDU with 2 SS and midamble periodicity = 4: power in 100 kHz band increases up to 0.8 dB with respect to PPDU without midambles

## Slide 7: Summary
It is desirable to enable the testing of PSD limits with wide resolution bandwidths
OFDM signal designs without spectral lines make a compelling case to argue in favour of spectrum tests with wide resolution bandwidths
It is suggested to randomize the midambles in order to suppress spectral lines
  It is good engineering practice
  In view of the possibility of new regulations for DSRC

## Slide 8: Straw poll
Do you agree that the midamble design should include a procedure to suppress spectral lines?
Y: 12
N: 1
A: 9

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0497-06-00bd-802-11bd-specification-framework-document.docx
[2] “In the Matter of: Use of the 5.850-5.925 GHz Band, ET Docket No. 19-138, NOTICE OF PROPOSED RULEMAKING”, Released: December 17, 2019, FCC 19-129
[3] “FEDERAL COMMUNICATIONS COMMISSION, 47 CFR Part 15”