## Slide 1: 240 MHz channelization
Date: 2020-03-16
Authors:

## Slide 2: 240 MHz agreements
A number of agreements have been reached on 240 MHz [1]:
  802.11be supports 240 MHz and 160+80 MHz transmission
    Whether 240/160+80 MHz is formed by 80 MHz channel puncturing of 320/160+160 MHz is TBD
  240/160+80 MHz bandwidth is constructed from three 80 MHz channels which include primary 80 MHz
    the tone plan of each 80 MHz segment is the same as HE80 in 802.11ax
  Various puncturing modes for 240 MHz

## Slide 3: 240 MHz channelization
Agreements on 240 MHz do not indicate where to 240 MHz channels can be located
  Allowed channel numbers for a given BW are typically listed in Annex E
Specifically:
  Can any three consecutive 80 MHz channels be combined into a 240 MHz channel?
  Should 160 + 80 MHz allow any combination of 160 MHz and 80 MHz channels?

## Slide 4: 240 MHz channelization
Three options for 240 MHz channelization
  Option 1: Contiguous but non-overlapping channels
  Option 2: Any combination of three consecutive 80 MHz channels
  Option 3: puncturing of 320 MHz channel

## Slide 5: Option 1: non-overlapping
Similar to allocation for other BW channels
Note: a 160 MHz channel may overlap with two 240 MHz channels

## Slide 6: Option 2: any three contiguous 80 MHz
Higher probability of having OBSS with different primary channel
Not allowed for any other BW

## Slide 7: Option 3: punctured 320 MHz channel
Overlap possible within 320 MHz channel

## Slide 8: 160+80 MHz channelization
Note that contiguous 160+80 MHz is essentially identical to 240 MHz
Even if going with “Option 1”, this mode could be used as a “backdoor” to creating overlapping 240 MHz channels
  NOTE: this is generally true for other BW as well

## Slide 9: Summary
240 MHz channelization options
  Only non-overlapping 240 MHz channels
  Any three consecutive 80 MHz channels
  Any three consecutive 80 MHz channels within 320 MHz channel
    i.e. 240 MHz channel equals punctured 320 MHz channel
In case of non-overlapping allocation, do we need additional restrictions on (contiguous) 160+80 MHz channel allocations?

## Slide 10: Straw Poll 1
Which channel allocation for 240 MHz do you support?
Option 1: Non-overlapping 240 MHz channels
Option 2: Allow any three consecutive 80 MHz to form a 240 MHz channel
Option 3: Punctured 320 MHz allocation
Option 1:
Option 2:
Option 3:

## Slide 11: Straw Poll 2
Should 160+80 MHz be disallowed if the 160 and 80 MHz are adjacent?
Y/N/A:

## Slide 12: References
[1] Specification Framework for TGbe, IEEE 802.11-19/1262R8