## Slide 1: Discussion on HARQ Unit
Date: 2020-03-03
Authors:
Name | Affiliation | Address | Phone | Email
Shimi Shilo | Huawei |  |  | 
Nadav Basson |  |  |  | 
Ezer Melzer |  |  |  | 
Avi Weitzman |  |  |  | 
Yaron Ben Arie |  |  |  | 

## Slide 2: Background
Various contributions on Hybrid Automatic Repeat Request (HARQ) have been presented in previous meetings [1-8]
The issue of the basic HARQ unit – which is signaled and retransmitted – is still under debate
The two HARQ units being considered are:
  MPDU
  Codeword
Several recent contributions [9, 10] have raised concerns that an MPDU cannot be considered as an HARQ unit, due to two issues:
  Different payload between retransmissions (e.g. due to changes in MPDU header)
  Misalignment between MPDUs and codewords
In this contribution, we recap the existing procedures/frame format and potential problems, address the concerns and present the pros and cons of each HARQ unit

## Slide 3: Tx Frame Format in 802.11
The figure below depicts the frame format used in .11 (similar to [9]):
MPDU #1
MAC Header
IV
Encrypted Data
MIC/CRC
SDU(s)
MPDU #2
MPDU #3
EOF Padding
Zero-Length Delimiter
PSDU
Service Field
Pre-FEC Padding
Post-FEC Padding
CW #1
CW #2
CW #3
CW #4
CW #5
CW #6
CW #7
MAC
PHY
CW Info Bits
Delimiter

## Slide 4: Different MPDU Contents within ReTx
Today, between retransmissions, the following can change:
  Number of Zero-Length Delimiters (ZLDs) between MPDUs
  Entire MAC header can change
    Due to changing conditions and QoS
    Retry bit changes upon retransmission
    Duration will be modified based on transmission parameters
  Encryption parameters
  CRC (due to any of the above)
  EOF/Pre-FEC/Post-FEC padding, depending on the transmission parameters
Any change in the MPDU contents (or delimiters/padding) will result in different coded bits and hence cannot be combined at the receiver side

## Slide 5: Misalignment between MPDUs and CWs
The 802.11 specs (and hence respective implementations) so far assume the following:
    The PHY receives a PSDU from the MAC layer and is not aware of the MPDU boundaries, their length, delimiters, etc.
    The FEC (LDPC) operates on blocks of information bits, regardless of MPDU boundaries
    A Block ACK (BA) indicates which MPDUs (within the A-MPDU) were decoded correctly, so retransmission occurs only for incorrectly decoded MPDUs

## Slide 6: Misalignment between MPDUs and CWs
Assuming an A-MPDU was transmitted and some of the MPDUs were incorrectly decoded, the transmitter will have to retransmit only those MPDUs that failed
For example, in the figure, an A-MPDU containing 5 MPDUs (2000 bits each) is transmitted using coding rate 1/2, where the 2nd and 3rd MPDUs failed and need to be retransmitted
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
MPDU Boundary
FEC Boundary
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822

## Slide 7: Misalignment between MPDUs and CWs
A retransmission of the failed MPDUs will include different coded bits due to a different setting of the FEC, as shown here, so the LLRs cannot be combined
This is a major problem – reusing the existing (retransmission) mechanism, the LLRs respective to retransmitted coded bits cannot simply be combined with old LLRs, as there is no alignment between old and new codewords
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Retransmitted
Retransmitted
MPDU of size 2000 bits
FEC block
Different info bits at input to FEC, hence different coded bits at output
Padding 20 bits
FEC #1
Info: 804
Coded: 1612
FEC #2
Info: 804
Coded: 1613
FEC #3
Info: 804
Coded: 1613
FEC #4
Info: 804
Coded: 1613
FEC #5
Info: 804
Coded: 1613

## Slide 8: Codeword Retransmission
Based on the description in the previous slides, a straight-forward approach to solving both the MPDU/CW alignment and the different payload issues would be to retransmit failed codewords
Reusing the same scenario from before, if CWs #4 and #6 fail, the retransmission can be composed of only the failed CWs
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
MPDU Boundary
FEC Boundary
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822
1st Tx
failed
failed
FEC #4
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
2nd Tx

## Slide 9: Codeword Retransmission
How does the transmitter re-generate the same CWs upon a retransmission?
  One approach would be to save the CWs in memory, and based on the (codeword) ACK determine which CWs should be read from memory and transmitted
  An alternative (complicated) approach would be to incorporate a new PHY-MAC interface which indicates to the MAC which bits to read, and then – based on previously saved parameters (e.g. length of CWs, number of punctured/repeated bits) – regenerate the same CWs

## Slide 10: Codeword Retransmission
The advantages of this approach are clear:
  Solves both content and MPDU/CW misalignment issues
  Keeps HARQ mostly within the PHY layer
  Assuming not all CWs of a failed MPDU do fail, it is more efficient than retransmitting the entire MPDU
However, there are some serious disadvantages that need to be considered:
  Need a new (Codeword) Block-ACK design, which means more overhead and also more time needed for spec design
  Need memory to save the codewords for future retransmission (alternatively need new PHY/MAC interface to indicate which bits correspond to which CW)
  Not clear it actually yields better performance (e.g. throughput increase) than MPDU retransmission

## Slide 11: MPDU Retransmission
As described in detail in previous slides, in order for an MPDU to be considered as a potential HARQ unit, we would need to address the following two issues:
  Difference in payload (e.g. padding, delimiters, MAC header contents) between retransmissions
  Misalignment of MPDUs and CWs
We first address these two issues, show how MPDU can in fact be used as an HARQ unit, and then turn to discussing the pros and cons associated with MPDU being an HARQ unit

## Slide 12: MPDU Retransmission
In order to address the different payload problem, we note the following important observations:
  When an MPDU is correctly decoded, the preceding delimiter is correctly decoded
  ZLDs immediately following the MPDU are not necessarily decoded correctly
  A retransmission indication should be contained within the PHY header (not indicated via MAC)
An MPDU retransmission should follow the following rules:
  A retransmission of an MPDU should contain its respective preceding delimiter and (any existing subsequent) ZLDs
  The contents of the MPDUs and delimiters should not be changed
  The retransmitted MPDUs should be transmitted in order, preferably at the beginning of the PPDU

## Slide 13: MPDU Retransmission
As an example, let us consider the following scenario, assuming a single MPDU retransmission with new aggregated MPDUs:
  Numbers indicate the index of each field
Zero-Length Delimiter
Delimiter
1st Tx
2nd Tx (retransmission)
MPDU #1
MPDU #2
1
2
3
MPDU #3
4
EOF Padding
PSDU
Service Field
Pre-FEC Padding
Post-FEC Padding
failed
Retransmitted without modifications
MPDU #4
5
MPDU #5
6
EOF Padding
5
4
New PSDU
New data
MPDU #2
1
2
3
2
1
2
3

## Slide 14: MPDU Retransmission
Let us now consider the following scenario, assuming the last MPDU fails (it is aggregated with new MPDUs within the reTx):
  Numbers indicate the index of each field
Zero-Length Delimiter
Delimiter
MPDU #1
MPDU #2
1
2
3
MPDU #3
4
EOF Padding #1
PSDU
1
2
3
Service Field
Pre-FEC Padding
Post-FEC Padding
failed
Retransmitted without content changes
MPDU #4
5
MPDU #5
6
EOF Padding #2
5
4
New PSDU
New data
MPDU #3
4
EOF Padding #1
3
1st Tx
2nd Tx (retransmission)

## Slide 15: MPDU Retransmission
How does the transmitter re-generate the same MPDUs and delimiters?
  One approach would be to save the MPDUs and delimiters in a (Low-MAC) memory, and choose which MPDUs and delimiters to retransmit based on the received Block-ACK
    This memory would be smaller than the one required for codeword retransmission, since only uncoded bits are saved
  An alternative (more complicated) approach would be to re-generate the same MPDUs and delimiters based on parameters saved in the first transmission

## Slide 16: MPDU Retransmission
As proposed in [8], retransmission of the info bits only – corresponding to failed MPDUs – solves the misalignment between MPDUs and CWs
The receiver indicates to the transmitter which MPDUs were successfully decoded using the existing Block-ACK bitmap
The transmitter can then retransmit the (uncoded) info bits corresponding to the failed MPDUs
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
Info 910
Padding 20 bits
parity910
Codeword #1
Info 911
parity911
Codeword #2
Info 911
parity911
Codeword #3
Info 911
parity911
Codeword #4
Info 911
parity911
Codeword #5
Info 911
parity911
Codeword #6
Info 911
parity911
Codeword #7
Info 911
parity911
Codeword #8
Info 911
parity911
Codeword #9
Info 911
parity911
Codeword #10
Info 911
parity911
Codeword #11
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Info
4000

## Slide 17: MPDU Retransmission
The receiver combines LLRs respective to info bits only, and decodes the codeword using all LLRs (including saved LLRs respective to parity bits)
This enables simple processing at receiver side (combine LLRs respective to info bits only), and significantly improves the efficiency since the reTx is much shorter, as shown in [8]

## Slide 18: MPDU Retransmission
The advantages of MPDU retransmission are clear:
  Maintains existing Block-ACK mechanism and bitmap (no need to develop new ACK, this solution reuses the same bitmap)
  Hence, time spent on spec should be shorter
In terms of disadvantages, the following should be taken into consideration:
  Need memory to save the MPDUs/delimiters for future retransmission (alternatively need complicated state machine to re-generate the same MPDUs and delimiters)
  HARQ is managed in both PHY & MAC

## Slide 19: Conclusions
In this contribution, we discussed two main issues related to using MPDUs as HARQ units
We showed that MPDUs can serve as HARQ units
We discussed the pros and cons of using either CWs or MPDUs as HARQ units
Though we are open to both options, our preference is MPDU retransmission since it is simpler and requires less time spent on spec design

## Slide 20: References
11-18-1587: HARQ for EHT, Sep. 2018
11-18-1955: HARQ for EHT – Further Information, Nov. 2018
11-18-1963: Discussion on HARQ for EHT, Nov. 2018
11-19-1992: HARQ Feasibility, Jan. 2019
11-19-2029: HARQ in EHT, Jan. 2019
11-19-1979: HARQ performance analysis, Jan. 2019
11-19-780: Consideration on HARQ, May 2019
11-19-1578: An HARQ Transmission Scheme for 11be, Nov. 2019
11-19-1589: What should be the HARQ unit and why?, Sep. 2019
11-20-101: 11be HARQ Discussions, Jan. 2020