## Slide 1: Decoupling Channel Training from NSTS
Date: 2020-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Abhishek Agrawal | Quantenna (ON Semiconductor Inc.) | 1704 Automation Pkwy San Jose, CA |  | Abhishek.Agrawal@onsemi.com
Sigurd Schelstraete |  |  |  | Sigurd.Schelstraete@onsemi.com
Huizhao Wang |  |  |  | Huizhao.Wang@onsemi.com

## Slide 2: Introduction
MIMO channel training is based on dedicated training sequence (HT-LTF, VHT-LTF, HE-LTF)
Length of training sequence for a given NSTS,tot is fixed to minimum needed to estimate up to NSTS,tot channels for each Rx antenna.
Below is the table of nominal NLTF as used by HT, VHT and HE training field generation:
In this contribution we evaluate decoupling channel training length from number of streams for EHT.

## Slide 3: Impact of Noise in Channel Estimation
Error in detection of data symbols depends on quality of channel estimates.
Assuming same noise level during channel estimation and data reception, post-equalizer SNR is worse by 3dB compared to noise-free channel estimate.
Channel estimation noise from received training signal: ( is Gaussian with variance s2)
( is Gaussian with variance s2)
Received data signal and Equalization:
This can be rewritten as:
3 dB SNR Loss

## Slide 4: CE Noise Improvement Techniques
Channel Smoothing
  Not effective for precoded transmissions
Data Driven Equalizer adaptation
  Not effective for early symbols
Averaging:
  Requires increased training sequences
  N-averaging can improve Post-Equalizer noise to (1+1/N) instead of
N | Theoratical SNR improvement (dB)
2 | 1.25
4 | 2.04
8 | 2.5

## Slide 5: 11ax Training Sequence
SU PPDU: NHE-LTF is not communicated as part of packet and receiver assumes NHE-LTF based on NSTS,tot information.
MU PPDU: NHE-LTF in specified in HE-SIG-A.
TB-PPDU: AP can request specific NHE-LTF in common info field of trigger frame.
  But use of NHE-LTF greater than nominal value is restricted to more than 1 RU transmissions.
  [Reference] 802.11ax draft: section 27.3.11.10

## Slide 6: Simulation Parameters
We evaluate the impact of using higher NLTF through PER simulations for 3 cases:
  DL SU without beamforming and channel smoothing on receiver
  DL SU with beamforming
  DL MU-MIMO
For each case, we compare default NLTF vs maximum NLTF(8) performance.
Other Simulation parameters:
  Transmitter: N_Tx = 8, BF sounding NSS = 8
  Receiver: N_Rx = 4, MMSE detection
  Channel model = TGnD

## Slide 7: Simulation Results (1/2)
SU result for non-beamformed and beamformed cases are shown below.
For non-beamformed case, channel smoothing is performed at receiver. LTF averaging improves CS noise further and provides up to ~1 dB gain in PER.
For beamformed case, up to 2.5 dB gains in performance can be achieved with improved CE.

## Slide 8: Simulation Results (2/2)
DL MU results for MCS 2 and MCS 11 are shown below.
Up to 2.5 dB gains are seen as increased training help with CE errors on receiver.

## Slide 9: Conclusions
Based on these results, we propose decoupling NEHT-LTF from NSTS,tot for all packet formats in EHT.
For SU format, current 11be SFD agrees on adding below subfields in U-SIG or EHT-SIG of an EHT PPDU sent to a single User:
  MCS
  NSTS
  GI+EHT-LTF Size
  Coding
  We propose to add indication of NEHT-LTF in U-SIG.
For MU and TB formats, we propose to remove multi-RU requirement for using higher number of LTF while keeping the indication of NEHT-LTF in EHT-SIG fields or trigger frame (similar to 11ax).

## Slide 10: Straw Polls
SP1: Do you support to include NEHT-LTF in U-sig for SU packets in EHT
Y:
N:
A:
Note: There is an ongoing discussion to use same packet format for SU and MU.

## Slide 11: Straw Polls
SP2: Do you support removing multi-RU restriction on using higher NEHT-LTF for MU packets in EHT
Y:
N:
A:

## Slide 12: Backup slides

## Slide 13: 802.11ax draft: section 27.3.11.10
  …In an HE MU PPDU with more than one RU and in an HE TB PPDU, NHE-LTF may take a value 1, 2, 4, 6 or 8 that is greater than or equal to the maximum value of the initial number of HE-LTF symbols for each RU…
  …For an OFDMA HE TB PPDU NHE-LTF may be 1, 2, 4, 6 or 8, which is greater than or equal to the maximum value of the initial number of HE-LTF symbols for each RU …