## Slide 1: BSS parameter update for Multi-link Operation
Date: 2020-04-01
Authors:

## Slide 2: Background
We agreed that a non-AP MLD monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s) [1].
BSS parameter update notification for Multi-link Operation was first mentioned in [2] and [3]
  BSS parameter update notification could be done in one link for another link such that to avoid monitor every link’s parameter update info
In this contribution, we provide a possible mechanism for it.

## Slide 3: Recap: BSS parameter Update
BSS parameter update notification is not new thing for a STA
  For TIM broadcast STA, BSS parameter update notification is carried in TIM broadcast frame
  TIM Broadcast allows a non-AP STA to receive a TIM element without receiving a Beacon frame that may reduce the required wake time in a power save mode.
  The shorter receive time reduces the power consumption for non-AP STAs in a power save mode.
  For SIG STA, BSS parameter update notification is carried in Change sequence element
Moreover, we have BSS parameter update notification for wake up radio
  It is similar to multilink device, which has more than one link
  One link is Wake up receiver, the other is Primary Connective Radio (PCR)
  Provide the BSS parameter update notification for PCR through wake up receiver

## Slide 4: Why we need BSS parameter updates info for multi-link
doze
doze
In most cases, the non-AP MLD will not enable all the STAs because of the following reasons
  Power consumption is a big issue if enabling all the STAs all the time
  No big traffic requirement all the time
In this case, the non-AP MLD will miss the important information, such as BSS parameter updates for the link on which the STA in doze state work
BSS parameter update information is needed for the STA in doze state when it transforms to be awake state
Link 1
Link 2
Beacon
Beacon
Link 1
Link 2
AP MLD
Non AP MLD
PM =1 for Link 1&2
awake
doze
Beacon
Beacon
awake

## Slide 5: Why we need BSS parameter updates info for multi-link
For non-STR non-AP MLD, it is impossible to monitor BSS parameter updates for every link simultaneously
  The non-AP MLD may miss the new BSS parameters broadcast while it transmits a packet in another link
  BSS parameter update information is needed for the STA in a MLD which can not receive the packet because of non-STR capability
Link 1
Link 2
Beacon
Link 1
Link 2
AP MLD
Non-AP
MLD
Packet

## Slide 6: BSS Parameters Update notification
Generally speaking, the STA in a MLD knows all the necessary info for its corresponding link after association
When there are changes in some BSS parameters, it is not possible to broadcast the detail info through one link for another link, otherwise it will bloat that management frame, such as beacon
We propose the reporting AP just carries a simple indication to alert the STA in a MLD to sync with new info for a reported AP in the same MLD
  Propose to use a counter field in beacon or reuse check beacon field in the broadcast TIM frame for the reported AP
  Meanwhile it requires an identifier of the reported AP, such as Link ID
  After being informed the changed BSS parameters, the STA in a MLD can either wake up to receive the beacon of the corresponding link or retrieve updated information by using probe request in any link
  Frequent Probe Request may lead to congestion

## Slide 7: BSS Parameters Update notification
  Initialize check beacon filed for a link to 0 at the beginning, and increase by one when a critical update occurs to any BSS parameters of that link
  a) Inclusion of Channel Switch announce element
  b)Inclusion of Extended Channel Switch announce element
  b) Modification of the EDCA parameters
  c) Inclusion of a Quiet element
  e) Modification of the HT Operation element
  f) Inclusion of an Operating Mode Notification element
  g) Inclusion of a Quiet Channel element
  h) Modification of the VHT Operation element …
  When the STA in a MLD receives a check beacon/Change Sequence Number field that is different from the local stored number, it shall
  receive the next beacon frame
  and update the local stored number
doze
doze
Link 1
Link 2
Beacon
Beacon
Link 1
Link 2
AP MLD
Non AP MLD
Check beacon for link 2 is 3
awake
doze
Beacon
Beacon
awake
Local #=2
awake
doze
Local #=3

## Slide 8: Summary
To avoid monitor every link’s parameter update, BSS parameter update notification could be done in one link for another link
We propose to use a counter field in beacon or reuse check beacon field in the broadcast TIM frame to provide BSS parameter update notification for MLD

## Slide 9: References
[1] IEEE 802.11-19/1262r8 Specification Framework for TGbe
[2] IEEE 802.11-19/1988r1 Power save for multi-link
[3] IEEE 802.11-20/337r0 Multi-link BSS Parameter Update

## Slide 10: SP 1
Do you agree that an AP in an AP MLD shall provide BSS specific parameters update indication for one or more other APs in the same AP MLD?
  BSS specific parameters update indication includes Link ID and Change Sequence Number for each reported AP, where Link ID is an identifier of the reported AP
  Reusing the existing Check beacon field as Change Sequence Number field is TBD

## Slide 11: SP 2
Do you agree that a non-AP MLD shall maintain a record of the most recently received sequence counter for each reported APs with which a STA in the non-AP MLD is associated

## Slide 12: SP 3
Do you agree that when a STA in a non-AP MLD receives a Change Sequence Number field that is different from the previously received Change Sequence Number field for a reported AP in an AP MLD, the corresponding STA in the non-AP MLD shall attempt to receive the next beacon frame sent by reported AP to retrieve the update?

## Slide 13: SP 4
Do you agree that when a STA in a non-AP MLD receives a Change Sequence Number field that is different from the previously received Change Sequence Number field for a reported AP in an AP MLD, any STA in the non-AP MLD may send the Probe Request frame to retrieve the update for the reported AP?