## Slide 1: Signaling of preamble puncturing in SU transmission
Date: 2020-03-23
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
March 2020

## Slide 2: Introduction
The preamble puncturing in SU transmission and various puncturing patterns were agreed in the past F2F meeting.
In order to support the preamble puncturing efficiently in SU transmission, we should consider the following issues.
  Transmission of EHT-SIG field in SU PPDU
  Signaling of puncturing patterns
In this contribution, we introduce how to indicate the preamble puncturing pattern and how to configure the EHT-SIG in SU transmission.

## Slide 3: Preamble puncturing patterns
Based on the passed motion[1], following puncturing patterns are defined in SU transmission.
BW | Aggregated BW | RU Size | Cases
80MHz | 60MHz | 484 + 242 | 4
160MHz | 120MHz | 484+996 | 4
160MHz | 140MHz | 484 + 242 + 996 | 8
240MHz | 160MHz | 996+ 996 | 3
240MHz | 200MHz | 484 + 996+ 996 | 6
320MHz | 240MHz | 996+ 996+996 | 4
320MHz | 280MHz | 484 + 996+ 996+996 | 8

## Slide 4: Transmission of EHT-SIG (1/2)
The SU PPDU format was not yet defined but we have been discussing the following options.
  The unified PPDU format for SU and MU[2]
  Individual PPDU format for SU/MU[3]
The details are different, but basically, both options are considering the inclusion of EHT-SIG field in SU PPDU.
However, in SU transmission, since we don’t need to indicate the RU allocation used for OFDMA transmission, we can consider the duplicated transmission of EHT-SIG per 20MHz.

## Slide 5: Transmission of EHT-SIG (2/2)
EHT-SIG configuration in SU PPDU
  For example, in 80MHz
    The EHT-SIG configured with 20MHz is duplicated per 20MHz in 80MHz.
    And, EHT-SIG contains all contents regarding the entire transmission bandwidth.
Duplicated per 20MHz

## Slide 6: Signaling of puncturing patterns
As described in previous slides, the SU PPDU may contain the two SIG fields, i.e., U-SIG and EHT-SIG.
  The details for EHT-SIG is TBD
So, to indicate the puncturing patterns, we can consider using of both fields or using of each field.
  Various signaling methods have already been introduced in [4].
For the indication of preamble puncturing, we can consider the following 3 options.
  Opt. 1 : only using BW field
  Opt. 2 : using the combination of BW field and puncturing pattern information
  Opt. 3 : only using puncturing pattern information

## Slide 7: Opt. 1 : BW field
The all preamble puncturing patterns can be indicated by using the BW subfield in the U-SIG field.
In order to support the various puncturing patterns in each BW, we can consider the large size bits of the BW subfield.
  Considering both continuous BW and non-continuous BW (i.e., preamble punctured), we can take into account the following cases to indicate the puncturing pattern where the puncturing of primary 20MHz is excluded.
    Continuous BW : 20,40,80,160/80+80,240/160+80,320/160+160
    BW w/ puncturing : 60MHz (3), 120MHz(3), 140MHz(7), 160MHz(2), 200MHz(5), 240MHz(3), 280MHz(7)
  In order to support a total of 36 cases (or a total of 43 cases including the primary 20MHz), we need to define the large size of BW bits such as 6bits.
    See the appendix for configuration of BW field
However, since the BW field is defined as version-independent information in the U-SIG field, it should be set to the same regardless of EHT PPUD type.
But, we do not decide yet whether the same puncturing patterns are applied to SU and MU transmission or not.
Thus, we need to consider the use of the BW field for the indication of puncturing patterns more carefully.

## Slide 8: Opt. 2 : combination of BW and puncturing pattern information
Similar to 11ax, we can consider that the preamble puncturing pattern can be indicated by the BW field and pattern information.
  for example, we can consider the 4bits BW field and 5bits puncturing information.
    The 4bit BW field can be configured like as following to indicate whether the Secondary 20MHz is punctured or not and primary 40/80 is present or not.
      80MHz for preamble puncturing
        [ 1 x 1 1 ]
        [ 1 1 ? ? ] – 2 puncturing case
      160MHz/80+80MHz for preamble puncturing
        [ 1 x 1 1 1 1 1 1 ]
        [ 1 1 ? ? ? ? ? ? ] – 9 puncturing case
      240MHz/160+80MHz for preamble puncturing
        [ 1 1 x x 1 1 1 1 1 1 1 1 ]
        [ 1 1 1 1 ? ? ? ? ? ? ? ? ] – 6 cases
      320MHz contains the preamble puncturing can be composed with following.
        [ 1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1 ]
        [ 1 1 1 1 ? ? ? ? ? ? ? ? ? ? ? ? ] – 9 cases
    To indicated the pattern of puncturing which is included in the second case of the above BW field, 5bit of pattern information can be used.
      This information can be included in U-SIG or EHT-SIG.
      See the appendix for the detail configuration of pattern bits
  Also, to minimize the signaling overhead, we can consider the following composition of the BW field and pattern bits.
    4bits BW field and 4 bits puncturing information.
      Where the fixed size of pattern information regardless of BW is used.
      See the appendix for the detail configuration of the BW field and pattern bits
1 means non punctured 20MHz
x means punctured 20MHz

## Slide 9: Opt. 3 : Puncturing pattern information
To support the various puncturing patterns, we can simply consider the indication of puncturing per each 20MHz.
  In consideration of 320 MHz, the pattern information may be composed of up to 16 bits.
  And, to reduce the overhead, the pattern information consists of 4 bits per 80MHz and according to BW, bit size can be extended as followings
    Pattern information bit = N * 4bit , where N = 1,2,3,4 when BW = 80/160/240/320MHz .
Similar to the above signaling, we can also consider the pattern information that contains the puncturing information per 80MHz.
  Within 80MHz of BW, because we can consider the 20/40/80MHz puncturing cases, for example, pattern information can consist like of as follows.
  With this pattern bits per 80MHz, we can consist the patter information like as following
    Fixed information case - pattern information consist of 12 bit
    None fixed case - pattern information bit = N* 3bit where N is 1,2,3,4 according to BW
Index | Puncturing pattern | content | Index | Puncturing pattern | content
1 | [1 x 1 1] | Second 20MHz is punctured | 5 | [ 1 1 x x] | Second 40MHz is punctured
2 | [1 1 x 1] | Third 20MHz is punctured | 6 | [x x 1 1] | First 40MHz is punctured
3 | [1 1 1 x] | Fourth 20MHz is punctured | 7 | [x x x x ] | 80MHz is punctured
4 | [x 1 1 1] | First 20MHz is punctured | 8 | [ 1 1 1 1 ] | No puncturing
In the table, 1 means non punctured 20MHz , x means punctured 20MHz

## Slide 10: Summary
We introduce the transmission of the EHT-SIG field in SU-PPDU.
  Since it does not need the RU allocation subfield for each 20MHz channel and PPDU bandwidth, the EHT-SIG field in SU-PPDU can be transmitted with duplication per 20MHz.
For the signaling of preamble puncturing in SU transmission, the three options are considered in this contribution.
  Opt.1 : only BW field
  Opt.2 : BW field(4bits) and puncturing pattern bits(4/5bits)
  Opt.3 : puncturing pattern bits
Considering the limited space of U-SIG and the next version of the Wi-Fi design, it may be more efficient to use such methods as options 2 and 3 to signal the puncturing pattern rather than using the version independent field only.

## Slide 11: Straw poll 1
Do you agree that EHT-SIG field included in EHT-PPDU sent to a single user is duplicated per 20MHz in BW?

## Slide 12: Straw poll 2
Do you agree that a subfield which is not the BW field for preamble puncturing pattern information is included in U-SIG/EHT-SIG for the 11be PPDU transmitted to a single user?

## Slide 13: Straw poll3
Which option do you prefer to configure the preamble puncturing information?
  Approach. 1 : BW field + puncturing pattern bits
  Approach. 2 : only puncturing pattern bits
  Abs

## Slide 14: Reference
[1] 11-19-1262-08-00be-specification-framework-for-tgbe
[2] 11-20-0049-02-00be-PPDU Types and U-SIG Content
[3] 11-20-0019-01-00be-11be PPDU format
[4] 11-20-0285-01-00be-SU PPDU SIG Contents Considerations

## Slide 15: Appendix: Opt.1
6bit BW field.
Index | BW | Allocated BW | Allocation
1 | 20MHz | 20MHz | 242
2 | 40MHz | 40MHz | 484
3 | 80MHz | 80MHz | 996
4 | 80MHz | 60MHz | 242+0+484
5 | 80MHz | 60MHz | 484+242+0
6 | 80MHz | 60MHz | 484+0+242
7 | 160MHz | 160MHz | 996+996
8 | 160MHz | 120MHz | 484+0+996
9 | 160MHz | 120MHz | 996+484+0
10 | 160MHz | 120MHz | 996+0+484
11 | 160MHz | 140MHz | 242+0+484+996
12 | 160MHz | 140MHz | 484+242+0+996
13 | 160MHz | 140MHz | 484+0+242+996
14 | 160MHz | 140MHz | 996+0+242+484
15 | 160MHz | 140MHz | 996+242+0+484
16 | 160MHz | 140MHz | 996+484+242+0
17 | 160MHz | 140MHz | 996+484+0+242
18 | 240MHz | 240MHz | 996+996+996
19 | 240MHz | 160MHz | 996+0+996
20 | 240MHz | 160MHz | 996+996+0
21 | 240MHz | 200MHz | 484+0+996+996
22 | 240MHz | 200MHz | 996+484+0+996
23 | 240MHz | 200MHz | 996+0+484+996
24 | 240MHz | 200MHz | 996+996+484+0
25 | 240MHz | 200MHz | 996+996+0+484
26 | 320MHz | 320MHz | 996+996+996+996
27 | 320MHz | 240MHz | 996+996+996+0
28 | 320MHz | 240MHz | 996+0+996+996
29 | 320MHz | 240MHz | 996+996+0+996
30 | 320MHz | 280MHz | 484+0+996+996+996
31 | 320MHz | 280MHz | 996+484+0+996+996
32 | 320MHz | 280MHz | 996+0+484+996+996
33 | 320MHz | 280MHz | 996+996+484+0+996
34 | 320MHz | 280MHz | 996+996+0+484+996
35 | 320MHz | 280MHz | 996+996+996+484+0
36 | 320MHz | 280MHz | 996+996+996+0+484
37~64 | Reserved |  | 

## Slide 16: Appendix : Opt.2
BW field
Index | BW | Contents | Index | BW | Contents
1 | 20MHz | 20 MHz non-preamble puncturing | 9 | 160MHz/80+80MHz | 160 MHz/80+80MHz preamble puncturing , Only secondary 20MHz is punctured
2 | 40MHz | 40 MHz non-preamble puncturing | 10 | 160MHz/80+80MHz | 160 MHz/80+80MHz MHz preamble puncturing , P40 is present and at least one 20 MHz subchannel that is not in the primary 40 MHz is punctured
3 | 80MHz | 80 MHz non-preamble puncturing | 11 | 240MHz/160+80MHz | 240MHz/160+80MHz preamble puncturing , Only secondary 40MHz is punctured
4 | 160MHz/80+80MHz | 160 Mhz and 80+80MHz non-preamble puncturing | 12 | 240MHz/160+80MHz | 240MHz/160+80MHz preamble puncturing , P80 is present and at least one 40 MHz subchannel that is not in the primary 80 MHz is punctured
5 | 240MHz/160+80MHz | 240 MHz and 160+ 80MHz non-preamble puncturing | 13 | 320MHz/160+160MHz | 320MHz/160+160MHz preamble puncturing , Only secondary 40MHz is punctured
6 | 320MHz/160+160MHz | 320 MHz and 160+160MHz non-preamble puncturing | 14 | 320MHz/160+160MHz | 320MHz/160+160MHz preamble puncturing , P80 is present and at least one 40 MHz subchannel that is not in the primary 80 MHz is punctured
7 | 80MHz | 80 MHz preamble puncturing , Only secondary 20MHz is punctured | 15-16 | Reserved | 
8 | 80MHz | 80 MHz preamble puncturing , P40 is present and one of 20MHz in S40 is punctured |  |  | 

## Slide 17: Appendix : Opt.2
Configuration of pattern information
Index | BW index | Allocation information | Index | BW index | Allocation information
1 | 8 | [ 1 1 1 0 ] | 15 | 12 | [1 1 1 1 1 1 1 1 1 1 0 0]
2 | 8 | [ 1 1 0 1 ] | 16 | 12 | [1 1 1 1 0 0 0 0 1 1 1 1]
3 | 10 | [1 1 1 0 1 1 1 1] | 17 | 12 | [1 1 1 1 1 1 1 1 0 0 0 0]
4 | 10 | [1 1 0 1 1 1 1 1] | 18 | 14 | [1111 0011 1111 1111]
5 | 10 | [1 1 0 0 1 1 1 1 ] | 19 | 14 | [1111 1100 1111 1111]
6 | 10 | [1 1 1 1 0 1 1 1] | 20 | 14 | [1111 1111 0011 1111]
7 | 10 | [1 1 1 1 1 0 1 1] | 21 | 14 | [1111 1111 1100 1111]
8 | 10 | [1 1 1 1 1 1 0 1] | 22 | 14 | [1111 1111 1111 0011]
9 | 10 | [1 1 1 1 1 1 1 0] | 23 | 14 | [1111 1111 1111 1100]
10 | 10 | [1 1 1 1 1 1 0 0] | 24 | 14 | [1111 0000 1111 1111]
11 | 10 | [1 1 1 1 0 0 1 1] | 25 | 14 | [1111 1111 0000 1111]
12 | 12 | [1 1 1 1 0 0 1 1 1 1 1 1] | 26 | 14 | [1111 1111 1111 0000]
13 | 12 | [1 1 1 1 1 1 0 0 1 1 1 1] | 27~32 |  | Reserved
14 | 12 | [1 1 1 1 1 1 1 1 0 0 1 1] |  |  | 

## Slide 18: Appendix : Opt.2
4bits BW field and 4 bits of pattern information
  The BW field can be configured as shown in slide 16.
  As shown in slide 3, the number of pattern for preamble puncturing in each BW is different and the maximum number including the none punctured case is 13.
  So, we can indicate the all cases of puncturing pattern in each BW by using the 4 bits like as following.
    According to BW, the indices indicated the different puncturing pattern.
80MHz |  | 160MHz |  | 240MHz |  | 320MHz | 
Index | Content | Index | Content | Index | Content | Index | Content
1 | [1 1 1 1 ] | 1 | [1 1 1 1 1 1 1 1 ] | 1 | [1 1 1 1 1 1 1 1 1 1 1 1 ] | 1 | [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1]
2 | [1 x 1 1 ] | 2 | [1 x 1 1 1 1 1 1 ] | 2 | [1 1 x x 1 1 1 1 1 1 1 1 ] | 2 | [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1]
3 | [ 1 1 x 1 ] | 3 | [1 1 x 1 1 1 1 1 ] | 3 | [x x 1 1 1 1 1 1 1 1 1 1 ] | 3 | [x x 1 1 1 1 1 1 1 1 1 1 1 1 1 1]
4 | [1 1 1 x ] | 4 | [1 1 1 x 1 1 1 1 ] | 4 | [1 1 1 1 x x 1 1 1 1 1 1 ] | 4 | [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1]
5 | [x 1 1 1 ] | 5 | [x 1 1 1 1 1 1 1 ] | 5 | [1 1 1 1 1 1 x x 1 1 1 1 ] | 5 | [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1]
6~16 | Reserved | 6 | [1 1 1 1 x 1 1 1 ] | 6 | [1 1 1 1 1 1 1 1 x x 1 1 ] | 6 | [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1]
 |  | 7 | [1 1 1 1 1 x 1 1 ] | 7 | [1 1 1 1 1 1 1 1 1 1 x x ] | 7 | [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1]
 |  | 8 | [1 1 1 1 1 1 x 1 ] | 8 | [1 1 1 1 x x x x 1 1 1 1 ] | 8 | [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1]
 |  | 9 | [1 1 1 1 1 1 1 x ] | 9 | [1 1 1 1 1 1 1 1 x x x x ] | 9 | [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x]
 |  | 10 | [1 1 x x 1 1 1 1 ] | 10 | [x x x x 1 1 1 1 1 1 1 1 ] | 10 | [1 1 1 1 x x x x 1 1 1 1 1 1 1 1]
 |  | 11 | [ x x 1 1 1 1 1 1 ] | 11~16 | Reserved | 11 | [1 1 1 1 1 1 1 1 x x x x 1 1 1 1]
 |  | 12 | [1 1 1 1 x x 1 1 ] |  |  | 12 | [1 1 1 1 1 1 1 1 1 1 1 1 x x x x]
 |  | 13 | [1 1 1 1 1 1 x x ] |  |  | 13 | [x x x x 1 1 1 1 1 1 1 1 1 1 1 1]
 |  | 14-16 | Reserved |  |  | 14-16 | Reserved