## Slide 1: Multi-Segment EHT-SIG Design Discussion
Date: 2020-03-23
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
Several contributions propose an efficient multi-segment (per-80Mhz) EHT-SIG design.
This contribution shows our views on the multi-segment EHT-SIG design regarding:
  Overhead analysis
  Applicable scenarios
  Some suggestions on signaling

## Slide 3: Overhead Analysis
If following 11ax, with 320Mhz and 2CCs, there will be 8 RU allocation subfields with the user specific fields of the same content channels.
With the multi-segment EHT-SIG method, there can be 2 CCs per 80Mhz, hence it is like 8 CCs. So there can be only 2 RU allocation subfields with the user specific fields of the same content channels.
The overhead of the multi-segment EHT-SIG is around ¼ of the 11ax-like EHT-SIG.
For U-SIG, the overhead doesn’t save much even one U-SIG covers puncture info for all the bandwidth.

## Slide 4: Applicable Scenario
Subchannel selective transmission within a TWT service period is proposed to be a good scenario where different STAs park in different channels.
The TWT request/response will indicate one secondary channel for a 20Mhz operating STA, and indicate whether primary 80MHz or secondary 80MHz channel for a 80MHz operating STA.
Some restrictions for the SST within TWT SP because the STAs are staying on non-primary channels:
  Shall not do DCF or EDCAF
  The TWT SP shall not overlap TBTTs at which DTIM Beacon frames are sent
Outside this scheduling only period, the STAs shall not park on non-primary channels.
We propose to add this restriction as for now, and let the MAC guys further discuss other applicable scenarios.

## Slide 5: Some suggestions on signaling
Some suggestions should be considered regarding the signaling. The following indication should be the same considering symbol alignment within each segment from PHY point of view:
  Number of EHT-SIG symbols should be the same
  GI+EHT-LTF Size should be the same
  Number of EHT-LTF symbols should be the same
  PE related parameters should be the same
SST in 11ax doesn’t consider preamble puncture. Instead, 11be will consider preamble puncture for each segment.
  Need more discussion

## Slide 6: Some suggestions on signaling
RUs smaller or equal to 996-tone RUs should be prioritized to schedule within the same segment to save the overhead for EHT-SIG signaling.
  Increase BW from 80Mhz to 160Mhz will increase the overhead (Number of RU allocation subfields and per user field)
  Large RUs can cross different segments, indicated through the enhanced RU allocation table.

## Slide 7: Summary
Several aspects on multi-segment EHT-SIG design have been discussed regarding:
  Overhead analysis
  Applicable scenarios
  Some suggestions on signaling

## Slide 8: Straw Poll #1
Do you agree to limit the applicable scenario of multi-segment EHT-SIG to SST in a TWT SP as for now?
  Other scenarios TBD

## Slide 9: Straw Poll #2 (after update during the CC)
Do you agree that the following indication shall be the same considering symbol alignment within each segment from PHY point of view, if the fields are present in U-SIG:
  Number of EHT-SIG symbols
  GI+EHT-LTF Size
  Number of EHT-LTF symbols
  PE related parameters

## Slide 10
[1] 11-20-0380-00-00be-u-sig-structure-and-preamble-processing
[2] 11-20-0439-00-00be-efficient-eht-preamble-design
References

## Slide 11: Appendix
The TWT Channel field includes a bitmap that provides the channel that is being negotiated by a STA as a temporary channel during a TWT SP. Each bit in the bitmap corresponds to one minimum width channel for the band in which the TWT responding STA's associated BSS is currently operating, with the least significant bit corresponding to the lowest numbered channel of the operating channels of the BSS.