## Slide 1: Discussion On Coordinated UL MU-MIMO
Date: 05-07-2020
Authors:
Name | Affiliation | Address | Phone | Email
Genadiy Tsodik | Huawei Technologies |  |  | 
Shimi Shilo |  |  |  | 
Arik Klein |  |  |  | 
Yunbo Li |  |  |  | 
Jason Yuchen Guo |  |  |  | 

## Slide 2: Introduction
802.11be introduces Multi-AP as a set of features that is expected to bring additional efficiency gain when multiple networks share resources and efforts
The are several methods to achieve different level of coordination, where each method has its own advantages and constraints
In [1] we introduced a Coordinated UL MU-MIMO transmission scheme and studied its properties and performance
In this contribution we want to review the scenarios where the proposed scheme has advantages, and suggest it as a candidate scheme for UL Coordination

## Slide 3: Short Recap
UL Coordination Negotiation Procedure
Coordinated UL Trigger
Sharing AP
Shared AP
STA1
STA2
UL MU-MIMO Transmission
Time
In [1] we introduced an idea to allow STAs from different BSSs to transmit in parallel using an UL MU-MIMO format
We showed that when STAs from different BSSs transmit in parallel, using UL MU-MIMO format, it may significantly improve the overall performance (see Appendix for a corresponding PER figure)
We suggested to use UL MU-MIMO format with the total number of SSs that can be supported by each AP (AP with least capabilities will limit the N_SS) where each AP will use different N_SS according to its requirements
Suggested scheme requires time alignment and a coordinated trigger frame – see illustrative diagram below
Block ACK

## Slide 4: Main Motivation of UL Coordination
We see Multi-AP operation as an effort to improve system efficiency by sharing/coordinating resources among different APs from different BSSs
The currently discussed coordination techniques share frequency (Co-OFDMA), time (Co-TDMA) and Power (Co-SR)
There is an additional resource - spatial streams - which is already shared today between STAs in UL and DL MU-MIMO transmissions
More sophisticated Multi-AP schemes - JT and Co-BF - were discussed and deferred to Release 2
Assuming the majority of 11be APs and STAs will support UL MU-MIMO, UL Coordination by sharing spatial streams may be considered as well
This can yield an additional level of flexibility and higher efficiency
Hence we believe that Coordinated UL MU-MIMO should be considered and discussed as part of Multi-AP operation topic

## Slide 5: Procedure
We assume that APs (Sharing and Shared) have already exchanged their status/capabilities; the coordinated UL MU-MIMO procedure will be made up of:
  M-AP TF transmitted by Sharing AP (may also participate, not necessarily) with all the relevant coordination parameters for all the BSSs
  Each Shared AP will then transmit a TF to its associated STAs
    All TFs should be transmitted simultaneously (can be done by any solution developed in scope of Multi-AP)
  STAs transmit a TB PPDUs (each STA using its allocated N_SS)
  Procedure is completed by a simultaneous Block Ack transmission from each of the APs (can also use one of several solutions)
M-AP TF
Coordinated UL Trigger
Data Frame
Sharing AP
Shared AP2
STA1 (associated with AP1)
STA2 (associated with AP2)
Data Frame
MU-MIMO HE-LTF
MU-MIMO HE-LTF
Full Alignment
Time
Coordinated UL Trigger
Shared AP1
B-ACK
B-ACK

## Slide 6: When to apply Co-UL MU-MIMO
We compared the goodput of Co-OFDMA and Co-UL MU-MIMO, by simulating the following scenarios:
  2 APs, equipped with 8 Rx antennas
  2 STAs, transmitting 2 spatial streams each (total Nss = 4)
  Co-OFDMA – every AP operates on its own 20MHz channel
  Co UL MU-MIMO – two APs operate on same 40MHz (with UL MU-MIMO)
  MCS 0-7, MMSE detector
In the figure we can see the performance for a single AP where we ignore the overhead of preamble and control frames
It is clear that at higher SNRs UL MU-MIMO outperforms Co-OFDMA and achieves higher goodput (which makes sense because it is similar to operating with higher-order spatial multiplexing at high SNR)

## Slide 7: Standardization Aspects
802.11be agreed on two releases, where only low-complexity AP Coordination schemes will be developed for Rel. 1
The main aspect to be addressed for Coordinated UL MU-MIMO is triggering STAs from different BSSs
As this issue is not unique to our scheme, Co-UL MU-MIMO will reuse any solution that will be developed within the scope of Multi-AP in R1
Thus we suggest the following:
  Consider Coordinated UL MU-MIMO with a trigger frame based on R1-compatible coordination schemes

## Slide 8: Conclusion
Multi-AP operation is a wide topic with multiple TX Coordination schemes and techniques
We showed that Co-UL MU-MIMO outperforms Co-OFDMA in specific scenarios
Preferred scheme may be selected by network to maximize throughput depending on a specific scenario
Coordinated UL MU-MIMO should be considered as a candidate for UL Tx coordination

## Slide 9: References
[1] 11-19-1979-01-00be-ul-coordination-for-throughput-improvement-and-interference-reduction

## Slide 10: SP1
Do you support that 802.11be will adopt Coordinated UL MU-MIMO as an Multi-AP Coordination scheme for UL transmissions?

## Slide 11: Appendix
PER with synchronized and non-synchronized interference