## Slide 1: Power Efficient Broadcasting
Date: 2020-03-15
Authors:

## Slide 2
Abstract
In this contribution, we discuss proposals to address the power efficiency requirements for TGbc.

## Slide 3: Introduction
802.11bc has a requirement for power efficiency [1]
  TGbc R3.4.2: 802.11bc amendment shall have a mechanism to facilitate power-efficient broadcasting.
Potential source of wasted energy in E-BCS:
  APs keep on broadcasting when there are no longer consumers of the broadcast information
Broadcasting APs need to have the capabilities to ensure that there are consumers
  AP should stop broadcasting when it has detected that there is no STAs consuming the broadcast service

## Slide 4: Ways to Prevent Energy Waste (1/2)
There may be a number of ways to determine when to end broadcasting service in order to prevent energy waste
  Option 1: Negotiate broadcast service for a reasonable duration
  Option 2: Termination notice for broadcast services
  Broadcast service should be terminated once it is detected that there is no STA consuming the broadcast data
Option 1: Negotiate broadcast service for a reasonable duration
  Unassociated and associated STAs may negotiate with an AP for particular broadcast services
    May be conducted through ANQP or e-BCS request/response exchanges
  An optional duration indication may be added to the negotiation to indicate the broadcast service may be provided for a reasonable amount of time
    In terms of time units, or for the entire duration of the broadcast service (e.g., a football match video)
  STAs needs to re-negotiate if they still desire the service at the end of the duration
  However, this option alone may not be sufficient:
    STAs are mobile and may move away before duration expires
    STAs that cannot transmit may also request e-BCS services

## Slide 5: Ways to Prevent Energy Waste (2/2)
Option 2 may be needed to address these cases
Option 2: AP sends Termination Notice before ending a e-BCS service
  Termination Notice should be sent out well before the termination of e-BCS service to ensure that STAs consuming the service have time to act
  Termination Notice likely needs to include the following information:
    E-BCS service identifier
    Time to termination
    Negotiation method: e-BCS request/response frame, ANQP, IP
  Need to ensure that there won’t be a response storm by many of the STAs that are consuming a certain e-BCS service
    GAS already has some mechanisms to avoid signaling storms
    May need to design other mechanisms in a similar fashion

## Slide 6: Conclusions
We proposed two ideas to address the power efficiency requirement for e-BCS; both can help determine whether there are STAs consuming one or more eBCS service
Option 1: Negotiate broadcast service for a reasonable duration
Option 2: AP sends Termination Notice for broadcast services

## Slide 7
References
[1] IEEE 11-19/151r5, 802.11bc Functional Requirements Document, September 2019
[2] IEEE 11-19/1001r1, Functional Requirements Document Proposed Update, July 2019

## Slide 8: Straw Poll 1
Do you agree to add to the TGbc SFD:
  TGbc shall define a mechanism for STAs to negotiate durations of services when negotiating for one or more eBCS services.

## Slide 9: Straw Poll 2
Do you agree to add to the TGbc SFD:
  TGbc shall define a mechanism for APs to transmit Termination Notices before terminating one or more eBCS services.