## Slide 1: C-TDMA definition
Date: 2020-4-03
Authors:

## Slide 2: Content
Although everybody is using the term C-TDMA, we don’t have such definition in the SFD yet.

## Slide 3: C-TDMA
C-OFDMA is based on the transmission from the shared APs of multiple PPDUs that are orthogonalized thanks to a trigger frame sent by the sharing AP
  Each PPDU carrying data is triggered by the shared AP
  Need for a protocol for DL, and if we want to, a specific protocol for UL, and a specific protocol for a mix of DL and UL
We think C-TDMA should be designed with a simpler assumption as there is no need for orthogonality:
  Sharing AP just gives a time allocation to a shared AP, and during that time allocation the shared AP is free to do what it wants (transmits or solicits the PPDUs it wants, …)
  That means in this C-TDMA mode, the PPDUs carrying data are not triggered by the sharing AP, which only determines the start and end of the time allocation.

## Slide 4: C-TDMA
We then propose to define C-TDMA as the mode where:
  A part of the TxOP gained by a sharing AP is partitioned into Time Periods
  Each Time Period is given to one shared AP
Within the Time Period allocated to one shared AP, one or multiple of the following items are possible:
  The shared AP can send one or multiple DL PPDU to its associated STA(s)
  It can send one or multiple trigger frame to solicit UL PPDUs from its associated STA(s)
  It can apply reverse direction protocol to allow for UL PPDU transmissions from its associated STA(s)

## Slide 5: Straw polls
Do you agree to add the following to the 802.11be SFD:
The procedure for a sharing AP to share its TxOP time of an obtained TxOP with a shared AP, is called C-TDMA if each time period is only allocated to a single shared AP.
During the time period allocated to a shared AP, the shared AP can do any PPDU transmissions, including sending DL PPDUs or soliciting UL PPDUs
NOTE: a time period is a subset of the total TxOP time