## Slide 1: Coordinated Spatial Reuse: Focus on Downlink
Date: 2020-05-07
Authors:

## Slide 2: Recap: Coordinated SR (C-SR)
C-SR is a simple Multi-AP coordination scheme that can increase spectrum efficiency by reusing the same time/frequency resources among multiple BSSs
C-SR procedure
  C-SR procedure with unsolicited method [1]
  General C-SR procedure [2]
C-SR performance gain
  Compared to OBSS-PD and TDD [3]
  Compared to EDCA and complete control [4]
  Compared to C-OFDMA and OBSS-PD [5]
In this contribution, we divide the downlink (DL) C-SR procedure into 3 phases and investigate several issues of C-SR operation

## Slide 3: Issue 1: C-SR Coordination Policy
C-SR gain comes from appropriate Tx power management
Option 1: bi-directional coordination
  Sharing AP and shared AP negotiate the appropriate Tx power combination
  Could be better in terms of sum throughput
  Additional signaling overhead
Option 2: one-way coordination (Preferred)
  Sharing AP determines Tx power without a coordination process and limits the Tx power of shared AP to protect transmissions of sharing AP
  Sharing AP does not need to sacrifice its performance
  Less overhead
Shared AP
Sharing AP
Negotiated power
Negotiated power
Shared AP
Sharing AP
Enough power
Less power
AP
STA
DL TX
[Option 1]
[Option 2]

## Slide 4: C-SR Procedure into 3 Phases
Preparation phase: before AP obtains TXOP
  AP’s action list
    Decide a AP candidate set
      Collect capability (of AP2 in AP1’s point of view)
      Collect Rx RSSI information of neighboring C-SR capable APs and calculates path loss ( in AP1’s point of view)
    Collect Rx RSSI information from associated STAs
      Collect associated STA’s Rx RSSI from the associated AP and calculates path losses ( in AP1’s point of view)
      Collect associated STA’s Rx RSSI from neighboring C-SR capable APs and caculates path losses ( in AP1’s point of view)
  AP’s role in C-SR transmission is not determined yet
AP2
3
AP1
2
4
1
AP
STA
Signal

## Slide 5: C-SR Procedure into 3 Phases
Announcement phase: after AP obtains TXOP
  If the AP is willing to share the obtained TXOP, it becomes a sharing AP
  Sharing AP’s action list
    Select the shared AP from the AP candidate set
      Considering DL STA’s SINR of sharing AP
    Trigger the shared AP’s transmission using announcement frame
      Essential information: AP ID, Tx power limit
Transmission phase: after the potential shared AP obtains the shared TXOP
  If an AP receives the announcement frame successfully and is willing to participate in the C-SR transmission, the AP becomes a shared AP
  Shared AP’s action list
    Set Tx power based on the guide obtained from the announcement frame
  C-SR transmissions (including block acknowledgement) of the sharing/shared APs occur simultaneously in the shared TXOP
  Assumption: start/end time of C-SR transmissions are aligned

## Slide 6: Issue 2: Obtaining/Delivering Path Loss
AP who is willing to share its TXOP requires …
  Path loss with neighboring C-SR capable AP
    Can obtain from a measurement
  Path loss with associated STA
    Can obtain from a report
  Path loss between associated STA and neighboring C-SR capable AP
    Can obtain from a report
How to calculate path loss?
  STA can use beacon as a reference of path loss estimation
  (Beacon Tx power) – (Beacon Rx signal strength)
We need an element or a field which indicates beacon Tx power information. C-SR capable AP can include the element or the field in the beacon frame.

## Slide 7: Issue 2: Obtaining/Delivering Path Loss
Path loss report from STA
  AP can solicit path loss reports of its associated STA
    Path loss with the associated AP
    Path loss with the neighboring C-SR capable AP
  STA can estimate the path loss from the received beacon signal and is able to report path loss according to the request from the AP
We need a signaling procedure for the path loss report from STA. We can reuse Measurement Request/Report
Path loss obtained by AP1
  From request/report: and
  From measurement:
AP2
2
AP1
1

## Slide 8: Issue 2: Obtaining/Delivering Path Loss
TPC report element format defined in baseline specification
TPC report procedure
  Solicited
    TPC request frame and TPC response frame (action frames)
  Unsolicited
    A TPC report element is included in Beacon or Probe response frame without a corresponding request
C-SR supporting AP will use this element to indicate its beacon transmission power

## Slide 9: C-SR Procedure Example: 2-BSS DL/DL
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
DL MU
BA
Announcement Phase
Transmission Phase
AP1 obtains TXOP  sharing AP
AP2 obtains the shared TXOP  shared AP
STA1-2
STA2-2
BA
DL MU
BA
BA
* C-SR-A: C-SR announcement frame
Collecting
Capability/Path loss
Measuring and
Collecting
Path loss
Report
Measurement
Report

## Slide 10: Issue 3: Block Acknowledgement (BA) Separation
Problem
  BA transmissions of STAs simultaneously occur in the shared TXOP
  Tx power limit applies to shared AP’s transmission
Solution
  Separation of BA transmissions of the STAs associated with sharing/shared AP
Options for BA separation
  [Option 1] Non-overlapping resources for BA (preferred)
    Allocate non-overlapping frequency resources for BAs of sharing/shared AP
    Non-overlapping frequency resource allocation for BA is determined by the sharing AP and included in the announcement frame
  [Option 2] Implicit BA for sharing AP side, and delayed BA for shared AP side
    Pros: simple
    Cons: overhead

## Slide 11: Issue 3: Block Acknowledgement (BA) Separation
[Option 1] Non-overlapping resources for BA in detail
  Two-level BA separation
    Level 1: BA separation among sharing/shared APs
      E.g. upper 40MHz for sharing AP, lower 40MHz for shared AP
    Level 2: BA separation between DL STAs in each BSS (DL MU PPDU case)
      STAs send the immediate response according to the resource allocation information that is carried in the TRS control subfield
frequency
time
C-SR Transmission of sharing AP (DL MU PPDU)
BA of STA1
BA of STA2
frequency
time
C-SR Transmission of shared AP (DL MU PPDU)
BA of STA3
BA of STA4
SIFS
Shared AP
3
Sharing AP
2
4
1
40MHz
40MHz
same 40MHz

## Slide 12: Summary
We divide C-SR procedure into 3 phases according to TXOP acquisition status of sharing/shared AP
We believe that one-way coordination is an appropriate policy to manage the Tx power of sharing/shared AP in C-SR operation
To determine the maximum Tx power of shared AP, sharing AP collects path loss information from the associated STAs and neighboring C-SR capable APs by soliciting reports
We propose two options for BA separation

## Slide 13: Straw Poll #1
Do you agree that in 11be sharing AP limits the shared AP(s)’ transmission power during the shared TXOP in C-SR procedure?
  Sharing AP may reduce its transmission power in the shared TXOP
  Shared AP(s) shall follow the transmission power limit indicated by sharing AP in the shared TXOP
  Shared AP’s transmission power limit is included in the announcement frame
  Shared AP’s transmission power is limited by the information provided by the sharing AP and the information is included in the announcement frame
  NOTE: the term, shared TXOP, can be changed
  NOTE: the field indicating transmission power limit and its encoding are TBD
  Note: the exact format of the information in the announcement frame is TBD

## Slide 14: Straw Poll #2
Do you agree that in 11be C-SR capable AP indicates its beacon transmission power in beacon frame?
  The beacon transmission power can be included in either one of element or field
  The element or field indicating the beacon transmission power and its encoding are TBD
  Note: C-SR capable AP may utilize TPC request/report element defined in the baseline spec
Notes:   TPC Report element can be included in a Beacon frame or Probe Response frame

## Slide 15: Straw Poll #3
Do you agree that in 11be the signaling for reporting path loss values is required?
  Signaling details are TBD
  NOTE: We may reuse Measurement request/response procedure defined in the baseline spec

## Slide 16: Straw Poll #4
Do you agree that in 11be sharing AP allocates non-overlapping frequency resources of block acknowledgements for each sharing AP and shared AP(s) for C-SR operation?
  Allocating non-overlapping frequency resource shall be determined by sharing AP
  Minimum unit of frequency resource allocation is 20MHz
  The way of indicating non-overlapping frequency resources for block acknowledgement is TBD

## Slide 17: Reference
[1] 802.11-20/0410r4 “Coordinated Spatial Reuse Procedure”, Sungjin Park
[2] 802.11-20/0576r1 “Coordinated Spatial Reuse Protocol”, Yongho Seok
[3] 802.11-20/0457r1 “Discussion on Coordinated Spatial Reuse Operation”, Kosuke Aio
[4] 802.11-20/0107r1 “Multi-AP coordination for spatial reuse”, Dmitry Akhmetov
[5] 802.11-20/0073r0 “On Coordinated Spatial Reuse in 11be”, Jianhan Liu

## Slide 18: APPENDIX

## Slide 19: Calculation of Shared AP’s Tx Power Limit
Goal
  AP1 (sharing AP) wants to protect DL transmission for STA1
  SIR of STA1, , should be larger than
Procedure
  STA1 calculates from and
  STA1 calculates from and
  STA1 reports and to AP1
  AP1 obtains
AP2
3
AP1
2
4
1
AP
STA
Signal

## Slide 20: Comment RESOLUTION

## Slide 21: Parameterized Spatial Reuse
Objective
  AP uses a trigger frame to allow spatial reuse of OBSS STA(s)
Operation
  AP indicates “Acceptable Rx Interference Level” in the trigger frame
  PSR-capable STA transmits with reduced power guided by the ARIL
Notes: OBSS-PD: relaxing the CCA threshold

## Slide 22: Major Difference Between PSR and C-SR
EDCA or Trigger-based Access?
  In PSR, TXOP owner “allows” EDCA-based access of “random” OBSS STA(s)
  In C-SR, TXOP owner (sharing AP) “shares” its TXOP with a “designated” shared AP. The shared AP is able to access the medium without EDCA.
Sharing AP’s shared TXOP Usage
  In PSR, TXOP owner always uses its TXOP for UL transmission. But in C-SR sharing AP is allowed to use DL transmission in the shared TXOP
  Allowing DL transmission of sharing AP requires additional path loss signaling compared to TXOP owner of PSR
    Sharing AP needs to consider DL STA’s SIR.
Path loss estimation/collection procedure
  In PSR, OBSS STA doesn’t need additional signaling in terms of path loss
    STA utilizes Trigger frame for path loss estimation
    AP doesn’t need to collect path loss
  C-SR requires additional signaling in terms of path loss
    STA utilizes Beacon frame for path loss estimation
    AP needs to collect path loss information to calculate the limitation of shared AP
Notes: OBSS-PD: relaxing the CCA threshold

## Slide 23: Non-overlapping BA
Necessity of non-overlapping BA
  Since we don’t know the simultaneous reception of overlapping BA(s) at sharing/shared AP are successful or not, we should take a safe/conservative approach
  In a protocol design point of view, allowing multiple overlapping transmission without power/freq. management is not a desirable solution
Preamble overlapping issue
  [Case1] BAs of sharing/shared STA are assigned to the RUs in the different 20MHz
    No preamble overlap between BAs of sharing/shared STA
  [Case2] BAs of sharing/shared STA are assigned to the RUs in the same 20MHz
    Sharing AP should assign different 20MHz BW for BAs of sharing/shared STAs

## Slide 24: Etc.
Transmission power indication in Beacon frame
  TPC report element is defined in the specification and can be used to indicate beacon transmission power (slide 8 added)
Path loss signaling overhead
  Since path loss values are semi-static, once path loss collection is done, then AP can use collected path loss information for a while.
  Path loss collection is AP-side implementation issue
C-SR considering UL
  I will cover it in the another contribution DCN 11-20/1040