## Slide 1: EHT BSS Operation: EHT BW Nss MCS and HE BW Nss MCS
Date: 2020-05-12
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Basic Rule 1
Max supported Rx HE Nss vs max supported Rx EHT Nss of an EHT STA
  Option 1 (preferred): at any BW+MCS allowed by HE, the max supported HE Nss capability indicated in HE capabilities element (Nss for receiving HE PPDU) by an EHT STA/AP is no more than the max supported EHT Nss capability indicated in EHT capabilities element (Nss for receiving EHT PPDU) by the EHT STA.
    When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is no more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT Nss capability indicated in EHT capabilities element at the BW+MCS.
    When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA at the BW is 8 at the BW+MCS.
  Option 2: The max supported Rx HE Nss and the max supported Rx EHT Nss by an EHT STA/AP at a BW are independent.

## Slide 3: Basic Rule 2
Max supported HE BW vs max supported EHT BW of an EHT STA:
  Option 1(preferred): the max supported HE BW capability indicated in HE capabilities element by an EHT STA is no more than the max supported EHT BW capability indicated in EHT capabilities element by the EHT STA
    When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is no more than 160MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT BW capability indicated in EHT capabilities element.
    When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is 80+80MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT BW capability indicated in EHT capabilities element.
    When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is 320 or 160+160MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is 160MHz or 160/80+80MHz
  Option 2: The max supported HE BW and the max supported EHT BW by an EHT STA/AP are independent.

## Slide 4: Basic Rule 3
Max supported HE Nss vs max supported HET Nss of an EHT STA
  Option 1 (preferred): at any BW+MCS allowed by HE, the max supported HE Nss capability indicated in HE capabilities element (Nss for transmitting HE PPDU) by an EHT STA/AP is no more than the max supported EHT Nss capability indicated in EHT capabilities element (Nss for transmitting EHT PPDU) by the EHT STA.
    When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is no more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT Nss capability indicated in EHT capabilities element at the BW+MCS.
    When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA at the BW is 8 at the BW+MCS.
  Option 2: The max supported HE Nsts and the max supported EHT Nss by an EHT STA/AP at a BW+MCS are independent.

## Slide 5: Basic Rule 4
The max Nss capability of an EHT STA at BW1 is no smaller than the max Nss capability of the EHT STA at BW2 if BW1 is smaller than BW2.
the max EHT-MCS for n SS of an EHT STA is not smaller than the max EHT-MCS of n+1 SS of the EHT STA.

## Slide 6: Announcement of EHT-Nss MCS, Basic EHT-MCS Nss Support Set
Option 1 (with the assumption of maximal mandatory MCS 9):
  For BW<=160/80+80MHz, EHT-Nss MCS for 1 SS to 8 SS in EHT-Nss MCS capabilities and basic EHT-MCS Nss Support are defined per HE-Nss MCS capabilities and basic HE-MCS Nss Support respectively,
    The other BW, MCS, Nss are defined as follows:
      The Max EHT-MCS For n SS subfield (where n = 1, ..., 8) is encoded to as follows:
        1 indicates support for EHT-MCS 12-13 for n spatial streams
        0 indicates that HE-MCS more than 11 for n spatial streams is not supported for EHT PPDUs
          The EHT-MCS for n spatial streams follows the HE-MCS announcement of n spatial streams in Max HE –MCS for n SS.
      The Max EHT-MCS For n SS subfield (where n = 7, ..., 16) is encoded to indicates the maximal MCS for n SS, e.g.
        0 indicates support for EHT-MCS 0-9 for n spatial streams
        1 indicates support for EHT-MCS 0-11 for n spatial streams
        2 indicates support for EHT-MCS 0-13 for n spatial streams
        3 indicates that n spatial streams is not supported for EHT PPDUs
Max EHT-MCS for 1 SS | Max EHT-MCS for 2 SS | Max EHT-MCS for 3 SS | Max EHT-MCS for 4 SS | Max EHT-MCS for 5 SS | Max EHT-MCS for 6 SS | Max EHT-MCS for 7 SS | Max EHT-MCS for 8 SS | Max EHT-MCS for 9 SS | Max EHT-MCS for 10 SS | Max EHT-MCS for 11 SS | Max EHT-MCS for 12 SS | Max EHT-MCS for 13 SS | Max EHT-MCS for 14 SS | Max EHT-MCS for 15 SS | Max EHT-MCS for 16 SS
B0
B1
B2
B3
B4
B5
B6
B7
B8
9
B10
B11
B12
B13
B14
B15
B16
B17
B18
B19
B20
B21
B22
B23
Rx EHT-MCS Map subfield, Tx EHT-MCS Map subfield for BW <=160/80+80MHz

## Slide 7: Announcement of EHT-Nss MCS, Basic EHT-MCS Nss Support Set
Option 1(with the assumption of maximal mandatory MCS 9) (Cont’d):
  For BW<=320/160+160MHz, EHT-Nss MCS and basic EHT-MCS Nss Support are defined independently from HE’s definition
    The Max EHT-MCS For n SS subfield (where n = 1, ..., 16) is encoded to indicates the maximal MCS for n SS, e.g.
      0 indicates support for EHT-MCS 0-9 for n spatial streams
      1 indicates support for EHT-MCS 0-11 for n spatial streams
      2 indicates support for EHT-MCS 0-13 for n spatial streams
      3 indicates that n spatial streams is not supported for EHT PPDUs
Max EHT-MCS for 1 SS | Max EHT-MCS for 2 SS | Max EHT-MCS for 3 SS | Max EHT-MCS for 4 SS | Max EHT-MCS for 5 SS | Max EHT-MCS for 6 SS | Max EHT-MCS for 7 SS | Max EHT-MCS for 8 SS | Max EHT-MCS for 9 SS | Max EHT-MCS for 10 SS | Max EHT-MCS for 11 SS | Max EHT-MCS for 12 SS | Max EHT-MCS for 13 SS | Max EHT-MCS for 14 SS | Max EHT-MCS for 15 SS | Max EHT-MCS for 16 SS
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
B16
B17
B18
B19
B20
B21
B22
B23
B24
B25
B26
B27
B28
294
B30
B31
Rx EHT-MCS Map subfield, Tx EHT-MCS Map subfield for BW >160/80+80MHz and Basic EHT-MCS And NSS Set field format

## Slide 8: Announcement of EHT-Nss MCS, Basic EHT-MCS Nss Support Set
Option 1(with the assumption of maximal mandatory MCS 9) (Cont’d):
3
3
3
3
3
3
4
4
4
4
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
EHT
EHT
EHT
EHT Capabilities element
Supported EHT-MCS And NSS Set
EHT
EHT-MCS
EHT Operating element
320 MHz
320 MHz
160+160
MHz
160+160
MHz

## Slide 9: Announcement of EHT-Nss MCS, Basic EHT-MCS Nss Support Set
Option 2 (with the assumption of maximal mandatory MCS 9):
  EHT-Nss MCS and basic EHT-MCS Nss Support are defined independently from HE’s definition
    The Max EHT-MCS For n SS subfield (where n = 1, ..., 16) is encoded to indicates the maximal MCS for n SS, e.g.
      0 indicates support for EHT-MCS 0-9 for n spatial streams
      1 indicates support for EHT-MCS 0-11 for n spatial streams
      2 indicates support for EHT-MCS 0-13 for n spatial streams
      3 indicates that n spatial streams is not supported for EHT PPDUs
Rx EHT-MCS Map subfield, Tx EHT-MCS Map subfield and Basic EHT-MCS And NSS Set field format
Max EHT-MCS for 1 SS | Max EHT-MCS for 2 SS | Max EHT-MCS for 3 SS | Max EHT-MCS for 4 SS | Max EHT-MCS for 5 SS | Max EHT-MCS for 6 SS | Max EHT-MCS for 7 SS | Max EHT-MCS for 8 SS | Max EHT-MCS for 9 SS | Max EHT-MCS for 10 SS | Max EHT-MCS for 11 SS | Max EHT-MCS for 12 SS | Max EHT-MCS for 13 SS | Max EHT-MCS for 14 SS | Max EHT-MCS for 15 SS | Max EHT-MCS for 16 SS
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
B16
B17
B18
B19
B20
B21
B22
B23
B24
B25
B26
B27
B28
294
B30
B31
4
4
4
4
4
4
4
4
4
4
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Rx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
Tx EHT-MCS
EHT
EHT
EHT
EHT Capabilities element
Supported EHT-MCS And NSS Set
EHT
EHT-MCS
EHT Operating element
320 MHz
320 MHz
160+160
MHz
160+160
MHz

## Slide 10: SP 1
Do you support that the max supported HE BW capability indicated in HE capabilities element by an EHT STA is no more than the max supported EHT BW capability indicated in EHT capabilities element by the EHT STA
  When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is no more than 160MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT BW capability indicated in EHT capabilities element.
  When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is 80+80MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT BW capability indicated in EHT capabilities element.
  When the max supported EHT BW capability indicated in EHT capabilities element by an EHT STA is 320 or 160+160MHz, the max supported HE BW capability indicated in HE capabilities element by the EHT STA is 160MHz or 160/80+80MHz

## Slide 11: SP 2
Do you support that at any BW+MCS allowed by HE, the max supported HE Nss capability indicated in HE capabilities element (Nss for transmitting HE PPDU) by an EHT STA/AP is no more than the max supported EHT Nss capability indicated in EHT capabilities element (Nss for transmitting EHT PPDU) by the EHT STA.
  When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is no more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA is same as the max supported EHT Nss capability indicated in EHT capabilities element at the BW+MCS.
  When the max supported EHT Nss capability indicated in EHT capabilities element by an EHT STA at a BW+MCS is more than 8, the max supported HE Nss capability indicated in HE capabilities element by the EHT STA at the BW is 8 at the BW+MCS

## Slide 12: SP 3
Do you support that:
  The max Nss capability of an EHT STA at BW1 is no smaller than the max Nss capability of the EHT STA at BW2 if BW1 is smaller than BW2.
  the max EHT-MCS for n SS of an EHT STA is not smaller than the max EHT-MCS of n+1 SS of the EHT STA.