## Slide 1: AP candidate set follow up
Date: 2020-04-10
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Po-kai Huang |  |  |  | po-kai.huang@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Notes: September 2012

## Slide 2: Motivation
We have the following concept of AP candidate set introduced in 11be SFD [1]:
  11be shall define a mechanism to determine whether an AP is part of an AP candidate set and can participate as a shared AP in coordinated AP transmission initiated by a sharing AP.
Some SPs are also referring to AP candidate set, for example [2]
  In all modes of operation wherein an AP shares its frequency/time resource of an obtained TXOP with a set of APs,
    Define a mechanism for the sharing AP to optionally solicit feedback from one or more APs from the AP candidate set to learn the resource needs and the intend to participate in a coordinated AP transmission.
Some members indicated there is confusion in the definition of AP candidate set.
This contribution clarifies the concept of AP candidate set and proposes a clear definition for it.

## Slide 3: AP candidate set
The primary motivation to introduce an “AP candidate” set is to clearly define the trusted boundary of coordinated AP operations in the management domain [3][4].
  To create a trusted region: Only APs in the same “AP candidate” set can initiate or participate in coordinated Multi-AP transmissions.
    For example, the APs in my own house are in a same AP candidate set, but the APs in my neighbor’s house may not be in the same AP candidate set.
    Prevent the scenarios where any arbitrary AP (which might be an illegitimate rogue AP) can trigger another AP whenever and however it wants.
    Similar to the SRG defined in 11ax, i.e., only members of the same SRG can perform OBSS PD-based spatial reuse operations.
  Each AP is aware of which “AP candidate set” it belongs to, and all other APs in the same “AP candidate set”. However, the formation of an “AP candidate set” can be outside of IEEE and be implementation specific.
    Again, similar to SRG, where we did not define how to form a SRG in 11ax.
    Define a hook in the spec, which gives implementations enough flexibility to decide how to form such a set in real practice.
  Therefore, it is not a per-AP “AP candidate set”.
    Since the term “AP candidate set” seems to cause confusion, suggest to change it to “Coordinated AP Set”, which we will use in the rest of this presentation.

## Slide 4: Coordinated AP set & sharing/shared AP
Coordinated AP set is a long-term management domain function which should not change dynamically. In contrast, sharing AP and shared AP are defined in reference to a particular TXOP and may change from TXOP to TXOP.
  Coordinated AP set defines the boundary or superset of coordinated Multi-AP transmissions happened between a sharing AP and shared AP(s).
  An EHT AP which obtains a TXOP and initiates the Multi-AP coordination is the Sharing AP. An EHT AP which is coordinated for the Multi-AP transmission by the Sharing AP is the Shared AP [1].
Depending on the capabilities and implementation specific configurations, within a Coordinated AP set, multiple APs may be capable of acting as a sharing AP [4].
  Once an AP capable of being a sharing AP obtains a TXOP, it can initiate some form of Multi-AP transmission with other APs in the same Coordinated AP Set.
  In order to do this, an AP capable of being a sharing AP has to figure out which APs in the same Coordinated AP Set: 1) are within its transmission range and 2) have the corresponding capabilities of Multi-AP modes. This basically involves capabilities learning.
    This can be achieved by some information exchange between APs, either through implementation specific methods (for example, pre-configuration, backhaul information exchange etc.) or over-the-air information sharing.
  We already agreed in 11be that there will be such form of capabilities advertisement.
    An EHT AP supporting the Multi-AP coordination can send a frame (e.g., Beacon or other management frame) including capabilities of Multi-AP transmission schemes [1].

## Slide 5: Example of Coordinated AP Set vs. sharing/shared AP
AP1
AP2
AP3
AP4
STA
STA
STA
STA
STA
STA
STA
STA
TXOP 1, obtained by AP1
AP1 is the sharing AP
AP2, 3 are the shared APs
DL OFDMA
UL Ack/BA
DL OFDMA
UL Ack/BA
Multi-AP Trigger
Multi-AP Trigger
Time
Time
Frequency
Frequency
Coordinated AP Set
TXOP 2, obtained by AP3
AP3 is the sharing AP
AP1, 4 are the shared APs

## Slide 6: Conclusions
We clarified the definition of “AP candidate set” and the relationship between it and sharing/shared APs.
We suggest to change the term from “AP candidate set” to “Coordinated AP Set” to avoid confusion, and propose a clear definition of the “Coordinated AP Set”.
  The term can always be changed.

## Slide 7: SP1
Do you agree to use the following text to replace Motion 55 text for better clarification?
  11be shall define a Coordinated AP Set* as follows:
    A Coordinated AP Set is a set of APs that can initiate or participate in coordinated AP transmissions.
    An AP in a Coordinated AP Set can participate as a shared AP in coordinated AP transmission initiated by a sharing AP in the same Coordinated AP Set.
    At least one AP in a Coordinated AP Set shall be capable of being a sharing AP.
    *Note: The name of Coordinated AP Set can be changed.

## Slide 8: SP2
Do you agree to modify the following text in 11be SFD:
  Define a procedure for an AP to share its frequency/time resources of an obtained TXOP with a set of shared APs in the same Coordinated AP set
    Set of APs is TBD.

## Slide 9: References
[1] 11be SFD
[2] 11-19/1582r3 Coordinated-ap-time-and-frequency-sharing
[3] 11-19/1616r1 Multi-AP group formation
[4] 11-19/1931r1 Multi-AP group framework follow up