## Slide 1: Operating Class China Table Numbering
Date: 2020-03-03
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com

## Slide 2: Abstract
Annex E includes operating class tables
  Frequencies, channel numbers, op widths, op limits, class numbers
REVmd inserted the S1G table as E-5
  And moved China from E-5 to E-6
Table numbers are actually encoded into elements
  See 9.4.2.8 Country element
The change in China table number creates a backwards compatibility problem

## Slide 3: Where Is The Table Encoded?
9.4.2.8 Country element
  Contains country string dot11CountryString
  Defined in Annex C

## Slide 4: dot11CountryString
    If it is a country, the first two octets of this string is the two character country code as described in document ISO 3166-1. The third octet is one of the following:
      1. an ASCII space character, if the regulations under which the station is operating encompass all environments for the current frequency band in the country,
      2. an ASCII 'O' character, if the regulations under which the station is operating are for an outdoor environment only, or
      3. an ASCII 'I' character, if the regulations under which the station is operating are for an indoor environment only.
      4. an ASCII 'X' character, if the station is operating under a noncountry entity. The first two octets of the noncountry entity is two ASCII 'XX‘ characters.
      5. the hexadecimal representation of the Operating Class table number currently in use, from the set of tables defined in Annex E, e.g., Table E-1 (Operating classes in the United States) is represented as x'01'."

## Slide 5: Example From Annex E
NOTE 1—The following example Country element (see Figure 9-162 (Country element format)) describes U.S. operation (55, 53) using both Table E-1 (Operating classes in the United States) class 12 (nonglobal) and Table E-4 (Global operating classes) class 81 (global) for the 2.4 GHz band, 11 channels at 20 dBm limit (in hexadecimal): 07, 0F, 55, 53, 04, C9, 0C, 0, 01, 0B, 14, C9, 51, 0, 01, 0B, 14.
  Element ID 07
  Element Length 0F
  2-letter Country Code 55, 53 = U S
  Table 04 = Global

## Slide 6: Is The Example Correct?
There’s only one country string value
  It can name only one Table
  What if there are two tables in use?
    E.g. an old table for backwards compatibility, plus the newer global table
    The example states that both E1 and E4 tables are in use, but only E4 (the new global table) is explicitly called out, because there’s only room for one table to be called out in the Country String
      And that is used for E4 == Global
      This means that because the country is US, E1 is implied, per the example
    But what if the country is not US, CN, JP or in the EU?
      What is the implied table in use? Or is there none?
      E.g. does CA use the US E1 table? Is there a mapping? Should we define a mapping? Can CA only specify the global table?

## Slide 7: Is Information Missing?
Maybe the correct interpretation is:
  If there is no table listed for a country or region in Annex E, then a table must be named in the Country String:
    Any one of the tables for: US, JP, CN, EU or Global
  If there is a table for a country (US, JP, CN, EU member) then that table is implicitly included if another table is listed
    If the table index is the matching E1, E2, etc, then there is only one table in use
      I.e. The Global table is not in use
    If the table index is E4, then the global table is in use, plus the implicit matching country (or region) table
  Countries not US, JP, CN, EU cannot use two tables
    E.g. CA can use either E1 or E4, but not both

## Slide 8: Make E4 Implicit?
Is there some other way to determine that a STA or BSS supports the global table?
  E.g. inferred through the observation of some other element or parameter value?
If so, then
  Wouldn’t it be better to leave E4 as implicit and explicitly name the non-global table in use?
  Would that be backwards incompatible?
What about EU membership changes?

## Slide 9: Support For The Example
  10.22.3 Operation with operating classes
  When dot11OperatingClassesRequired is true and the STA supports one or more global operating classes, or where global operating classes domain information is present in a STA, the STA shall indicate current operating class information in the Country element and Supported Operating Classes element using the country string for the global operating classes, except that a VHT STA may omit from the Country element any Operating Triplet field for an Operating Class for which the Channel spacing (MHz) column indicates 80 MHz or wider and for which the Behavior limits set column in the applicable table in Annex E contains only a blank entry or either or both of “80+” and “UseEirpForVHTTxPowEnv.”

## Slide 10: Oh Yes, How About A CID: 4765
CID 4765
CID | Commenter | Page | Clause | Comment | Proposed Change | Proposed Resolution
4765 | Peter Ecclesine | 4379.00 | E | Global classes 115, 116, 118, 119, 125, 126 nonglobal operating classes reference should be to Table E.6 China, not Table E.5 Sub1GHz | Correct last nonglobal operating classes references to E.6.1, E.6.4, E.6.2, E.6.5, E.6.3 and E.6.6 respectively. | Revise – TGmd editor to make changes shown in 11-20-xxxxry which address Annex E table numbering problems.

## Slide 11: Proposed Changes
TGmd editor to change
Table E-5—S1G operating classes
To become:
Table E-6—S1G operating classes
And change
Table E-6—Operating classes in China
To become:
Table E-5—Operating classes in China

## Slide 12: Straw poll #1
Do you support the proposed changes to the numbering in Draft P802.11REVmd_D3.1 Annex E of Table E-5—S1G operating classes and Table E-6—Operating classes in China as described in 11-19-0599-00-000m-Operating-Class-China-Table-Number Proposed Changes?
  YES
  NO
  ABS

## Slide 13: References
[1] Draft P802.11REVmd_D3.1