## Slide 1: Further Discussion on Bandwidth and Puncturing Information
Date: 2020-04-10
Authors:

## Slide 2: Introduction (1/2)
During the 04/09/2020 PHY conference call, following SPs were run [1]
  Do you support that U-SIG in each 80MHz shall carry puncturing channel info for at-least the specific 80MHz where it is transmitted?
    Whether BW/Puncturing info can be different for different 80MHz is TBD
    Whether BW and puncturing info bits in U-SIG are carried as a combined or a separate field is TBD
    Y/N/A: 42/9/6
  Do you agree that a subfield for preamble puncturing pattern information separate from the BW field is included in U-SIG and/or EHT-SIG for the 11be PPDU transmitted to a single user?
    Y/N/A: 36/4/14
  Which option do you prefer to configure the preamble puncturing information for transmission to a single user?
    Approach. 1 : BW field includes some puncturing information
    Approach. 2 : BW field doesn’t include puncturing information. Puncturing information is a separate field.
    Approach. 1/Approach. 2/Abs: 17/30/10

## Slide 3: Introduction (2/2)
From those SPs, below seems got most support
  Separate BW and puncturing information
  Inform puncturing information of at-least the specific 80MHz where it is transmitted in the U-SIG
In this contribution, we listed potential options for bandwidth and puncturing information based on above assumptions
All options assume 3 bit BW field in U-SIG to inform BW only
  6 cases: 20/40/80/160 or 80+80/240 or 160+80/320 or 160+160 MHz
  2 cases are reserved for future extension
  Note: 320MHz is already quite wide. If it is wider, then we need to follow UWB regulation.

## Slide 4: Potential Options
Option 1: 3 bit Puncturing Information in U-SIG to inform puncturing pattern for the 80MHz
  Total 7 cases
  Further puncturing information in EHT-SIG is needed for full bandwidth single user or multi user transmission
  In case of OFDMA, resource allocation information should be enough (by not allocating resources in punctured subchannels)
Option2: 4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth
  Maximum 13 case
See appendix for detail information

## Slide 5: Option 1 Examples
Puncturing Pattern of [1 1 x x 1 1 1 1]
U-SIG to inform each
80MHz puncturing
information
EHT-SIG to further
inform other 80MHz
segments puncturing
information in case of
full bandwidth
transmission
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 x x]
PuncInfo=[1 1 x x]
Further PuncInfo
=[1 1 1 1]
Further PuncInfo
=[1 1 1 1]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
U-SIG
EHT-SIG
Punctured
subchannels
Upper 80MHz
Lower 80MHz

## Slide 6: Option 2 Examples
Puncturing Pattern of [1 1 x x 1 1 1 1]
U-SIG to inform entire
BW puncturing information,
e.g. first four is for current
80MHz, and remaining is for
other 80MHz
No further information in
EHT-SIG
PuncInfo=[1 1 1 1
1 1 x x]
U-SIG
Punctured
subchannels
Upper 80MHz
Lower 80MHz
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 x x
1 1 1 1]
PuncInfo=[1 1 x x
1 1 1 1]

## Slide 7: Summary
We presented two options for puncturing information
  Option 1: 3 bit Puncturing Information in U-SIG to inform puncturing pattern for the 80MHz
  Option 2: 4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth

## Slide 8: Straw Poll #1
Which option do you prefer?
  Option 1: 3 bit Puncturing Information in U-SIG to inform puncturing pattern for the specific 80MHz where it is transmitted
  Option 2: 4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth

## Slide 9: Reference
[1] 11-20/0587r1, “Minutes 802.11 be PHY ad hoc Telephone Conferences, April 2020”

## Slide 10: Appendix
3 bit Puncturing Information in U-SIG to inform puncturing pattern for the 80MHz
  7 cases: [1 1 1 1], [x 1 1 1], [1 x 1 1], [1 1 x 1], [1 1 1 x], [x x 1 1], [1 1 x x]
4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth
  80MHz 1: No puncturing, 2: Agg 60MHz [x 1 1 1], 3: Agg 60MHz [1 x 1 1], 4: Agg 60MHz [1 1 x 1], 5: Agg 60MHz [1 1 1 x],
  160MHz 1: No puncturing, 2: Agg 120MHz [x x 1 1 1 1 1 1], 3: Agg 120MHz [1 1 x x 1 1 1 1], 4: Agg 120MHz [1 1 1 1 x x 1 1], 5: Agg 120MHz [1 1 1 1 1 1 x x], 6: Agg 140MHz [x 1 1 1 1 1 1 1], 7: Agg 140MHz [1 x 1 1 1 1 1 1], 8: Agg 140MHz [1 1 x 1 1 1 1 1], 9: Agg 140MHz [1 1 1 x 1 1 1 1], 10: Agg 140MHz [1 1 1 1 x 1 1 1], 11: Agg 140MHz [1 1 1 1 1 x 1 1], 12: Agg 140MHz [1 1 1 1 1 1 x 1], 13: Agg 140MHz [1 1 1 1 1 1 1 x],
  240MHz 1: No puncturing, 2: Agg 160MHz [1 1 1 1 x x x x 1 1 1 1], 3: Agg 160MHz [1 1 1 1 1 1 1 1 x x x x], 4: Agg 200MHz [x x 1 1 1 1 1 1 1 1 1 1], 5: Agg 200MHz [1 1 x x 1 1 1 1 1 1 1 1], 6: Agg 200MHz [1 1 1 1 x x 1 1 1 1 1 1], 7: Agg 200MHz [1 1 1 1 1 1 x x 1 1 1 1], 8: Agg 200MHz [1 1 1 1 1 1 1 1 x x 1 1], 9: Agg 200MHz [1 1 1 1 1 1 1 1 1 1 x x],
  360MHz 1: No puncturing, 2: Agg 240MHz [1 1 1 1 x x x x 1 1 1 1 1 1 1 1], 3: Agg 240MHz [1 1 1 1 1 1 1 1 x x x x 1 1 1 1], 4: Agg 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x x x], 5: Agg 280MHz [x x 1 1 1 1 1 1 1 1 1 1 1 1 1 1], 6: Agg 280MHz [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1], 7: Agg 280MHz [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1], 8: Agg 280MHz [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1], 9: Agg 280MHz [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1], 10: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1], 11: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1], 12: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x]