## Slide 1: Discovery mechanism for MLD
Date: 2020-05-10
Authors:

## Slide 2: Background
To discover a particular BSS/AP, a STA can do either passive scanning or active scanning
  To passive scan, the STA shall listen to each channel scanned for no longer than a maximum duration
  To actively scan, the STA shall transmit Probe Request frames containing a wildcard SSID, the desired SSID or one or more SSID List elements
To speed up discovery , an AP could provide info for another AP in the same co-located set
  Info carried in reduce neighbor report element is an example
  A STA could find the info of more than one AP by just scanning one AP
In this contribution, we focus on the discover mechanism for AP multi-link device (MLD).

## Slide 3: Recap
802.11ax extended the operating frequency band to 6GHz, and the AP operating on 6GHz is expected to be multi-band collocated device
To avoid probe storm and make 6GHz green, a few 6GHz AP discovery mechanisms were proposed
Finally, the group converged to use reduce neighbor report element to help speed up the discovery for 6GHz AP
  The reduce neighbor report (RNR) just carries minimum info of collocated 6GHz AP such that the beacon could not be bloated
  The AP operating on 2.4/5GHz shall advertise its co-located 6GHz AP through the RNR element

## Slide 4: Multi-link device
The APs in a multi-link device can be regarded as co-located, but a little bit different from the excising co-located device
  An STA could do association with one AP to achieve multi-link association with more than one AP in its AP MLD
Since Multi-link association is done just with one AP in an AP MLD, so the discovery for the AP MLD is needed
Here we propose to reuse RNR carry the minimum info of the other APs in the same AP MLD as the reporting AP

## Slide 5: Multi-link device with multiple BSSID
Multiple BSSID is a mandatory feature in 802.11ax, it is straight forward to implement it at EHT AP
We agreed that each AP of an AP MLD is independently configured to operate as transmitted or nontransmitted BSSID of a multiple BSSID set, or not a multiple BSSID set [1]
An example is shown as below, and the BSSID with x is transmitted BSSID in a multiple BSSID set
We call the following structure a collocated AP MLD set
  A single STA could also be contained

## Slide 6: Discovery for co-located AP MLD set
We propose to reuse RNR to carry the minimum info of all the other APs in the same co-located AP MLD set as the reporting AP
Like Co-located subfield for 6GHz AP, we propose “co-located AP MLD set ” in RNR element to indicate the relationship between the reported AP and the reporting AP
Besides “co-located AP MLD set ”, the relationship among the APs in the co-located AP MLD set also needs to be specified
  Transmitted BSSID field and Multiple BSSID field are already in the RNR element
  MLD-index is needed to indicate in which MLD the reported AP is
  Multiple BSSID set-index is needed to indicate in which Multiple BSSID set the reported AP is
  Moreover, the simple index, like Link ID, for the reported AP in a MLD is needed
  This Link ID corresponding to the reported AP could be used for the follow up multi-link operation

## Slide 7: Discovery for co-located AP MLD set
Besides the relationship among the APs in the co-located AP MLD set, it is important to avoid the repeated info with the existing advertisement, e.g., Multiple BSSID element
For multiple BSSID set, the transmitted AP will broadcast Multiple BSSID element through the Beacon and Probe Response frames
  Multiple BSSID element carries the info of the nontransmitted BSSID
  If the reporting AP is transmitted BSSID, we propose that RNR element does not carry the info of any nontransmitted BSSID in the same Multiple BSSID set
  The corresponding MLD related info could be carried in nontransmitted BSSID profile, such as MLD-index, Link ID
2y
RNR
3
2x
1y
MBSSID
2z
Sent by BSSID—1x

## Slide 8: Summary
In this contribution, we propose to reuse RNR element to advertise the minimum info of the AP in the same co-located AP MLD set as the reporting AP
  This minimum info could help speed up the discovery for AP MLD
  The proposed minimum info could contain co-located AP MLD set, MLD-index, Multiple BSSID set-index and Link ID
  To avoid the redundant info, we propose RNR element shall not carry the info of any non-transmitted BSSID in the same Multiple BSSID set as the reporting AP

## Slide 9: References
[1] 11-20-0358-03-00be-multi-bssid-operation-with-mlo

## Slide 10: SP 1
Do you agree that RNR element shall not carry the info of any non-transmitted BSSID in the same Multiple BSSID set as the reporting AP

## Slide 11: SP 2
Do you agree to add MLD-index to the TBTT Information field of the RNR element, which is used to indicate the ID of the AP MLD in which the reported AP is?

## Slide 12: SP 3
Do you agree to add Multiple BSSID set-index to the TBTT Information field of the RNR element, which is used to indicate the ID of the Multiple BSSID set in which the reported AP is?

## Slide 13: SP 4
Do you agree to add Link ID to the TBTT Information field of the RNR element, which is used to indicate the identifier of the reported AP for the following multilink operation?

## Slide 14: SP 5
Do you agree that a nontransmitted BSSID profile in the Multiple BSSID element shall carry the MLD related parameters, such as MLD-index, Link ID if the nontransmitted BSSID is in an AP MLD?