## Slide 1: BW indication of 320MHz for non-HT and non-HT duplicate frames
Date: 2020-04-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yiqing Li |  |  |  | 
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yifan Zhou |  |  |  | 
Notes: September 2012

## Slide 2: Motivation
How to indicate BW information in non-HT or non-HT duplicate frame to support 320MHz or preamble puncture is a problem need to be solved;
Two types of solution is mentioned in [1, 2]
  Type 1: update RTS/CTS frame
  Type 2: define a new control frame or redefine Trigger/A-control. For simplicity, we call it new RTS frame for this type of solution.
Current RTS/CTS uses scrambler sequence to carry BW information, it has very limit bits can be used, so can not support preamble puncture
  Remain up to 4 bits of scrambler sequence can be used.
The new RTS frame will lose the NAV setting rule of RTS frame
  “A STA that used information from an RTS frame as the most recent basis to update its NAV setting is permitted to reset its NAV if no PHY-RXSTART.indication primitive is received from the PHY during a NAVTimeout period starting when the MAC receives a PHY-RXEND.indication primitive corresponding to the detection of the RTS frame.” (IEEE802.11Revmd_D2.2)

## Slide 3: Motivation
After new RTS frame is introduced, RTS frame still need to retain in order to do channel protection for legacy STAs;
  An EHT STA sends an new RTS frame to EHT STA when preamble puncture exists or BW>160MHz;
  An EHT STA sends a RTS frame to a legacy STA, or to an EHT STA when BW<=160MHz and preamble puncture doesn’t exists
Since anyway RTS frame will be supported by an EHT STA, enhance RTS/CTS frame to support >160MHz bandwidth (without preamble puncture) neither add a new type of frame nor introduce more signaling overhead;
We propose to support both types of solutions.

## Slide 4: Scenarios and Benefits
Scenario 1: transmits RTS/CTS on a channel with BW>160MHz without preamble puncture
Two benefits can obtained in this scenario
  Benefit 1: NAV setting rule of RTS frame can be kept
  Benefit 2: RTS/CTS is low overhead compare with new RTS/CTS frame
Scenario 2: transmit other non-HT and non-HT duplicate control frames other than RTS/CTS
Many Control frame other than RTS/CTS be transmitted in non-HT or non-HT duplicated format, and scrambler sequence is used to indicate BW indication
  e.g. PS-Poll, CF-End, BAR, BA, …
The new RTS/CTS solution can not be used in this scenario, so we get another benefit of update RTS/CTS
  Benefit 3: Same BW indication as update RTS/CTS can be used in this scenario

## Slide 5: BW Indication using Scrambler Sequence
B3 in the scrambler sequence is used as BANDWIDTH EXTENSION bit, B3 combines with B5B6 is used to indicate PPDU bandwidth
  B3=0, and B5B6 = 0~3 to indicate 20, 40, 80, and 160(80+80)MHz respectively
  B3=1, and B5B6 = 0~1 to indicate 240(160+80) and 320(160+160)MHz respectively
  B3=1, and B5B6 = 2~3 are reserved for future use.
Pseudo random integer
BANDWIDTH EXTENSION
DYN_BANDWIDTH_IN_NON_HT
CH_BANDWIDTH_IN_NON_HT
B0 B2 B3 B4 B5 B6
B3 | B5 B6 | BW
0 | 0 | 20MHz
0 | 1 | 40MHz
0 | 2 | 80MHz
0 | 3 | 160MHz or 80+80MHz
1 | 0 | 240MHz
1 | 1 | 320MHz
1 | 2-3 | reserved

## Slide 6: Conclusion
A new control frame is needed to do channel protection for preamble puncture, but will lose the NAV setting rule of RTS frame;
After a new control frame is introduced, an EHT STA still needs to support both new control frame and RTS/CTS frames;
Propose to add bandwidth indication capability for BW larger than 160MHz in scrambler sequence;
  The indication neither introduce new frame type, nor signaling overhead
  The indication can be used for EHT target STA to save overhead while retain NAV setting rule of RTS frame
  The indication can be used in all existing control frames in non-HT or non-HT duplicated frames.

## Slide 7: Straw Poll 1
Do you support to indicate BW larger than 160MHz through scrambler sequence in non-HT or non-HT duplicated frames?

## Slide 8: Straw Poll 2
Do you support to use one more bit in scrambler sequence, which is B3, to indicate bandwidth larger than 160MHz in non-HT or non-HT duplicated frames?

## Slide 9: Straw Poll 3
Do you support to use below indication of scrambler sequence in non-HT or non-HT duplicated frames?
  B3=0, and B5B6 = 0~3 to indicate 20, 40, 80, and 160(80+80)MHz respectively
  B3=1, and B5B6 = 0~1 to indicate 240(160+80) and 320(160+160)MHz respectively
  B3=1, and B5B6 = 2~3 are reserved.

## Slide 10: Reference
[1] 11-20-0399-00-00be-bw-negotiation-protection-with-more-than-160mhz-ppdu-and-puncture-operation
[2] 11-19-2125-01-00be-eht-rts-and-cts-procedure