## Slide 1: NAV Setting in Multi-AP Operation
Date: 2020-04-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yiqing Li |  |  |  | 
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yifan Zhou |  |  |  | 
Meihong Zhang |  |  |  | 
Notes: September 2012

## Slide 2: Terminology
Below terminologies will be used in this presentation. Some of them haven’t pass motion, just use them here for simplicity.
  Sharing AP: an EHT AP which obtains a TXOP and initiates the Multi-AP coordination; [Motion 73] [1]
  Shared AP: an EHT AP which is coordinated for the Multi-AP transmission; [Motion 73]
  Sharing STA: a STA that associates with the sharing AP, and participates in the AP cooperation procedure;
  Shared STA: a STA that associates with a shared AP, and participates in the AP cooperation procedure;
  Shared TXOP: a TXOP during which AP cooperation happens
Note: a sharing STA or a shared STA may be a legacy STA depends on the AP cooperation procedure.

## Slide 3: Background
The concept of some simple AP cooperation scheme already be accepted
  E.g. Co-OFDMA, Co-TDMA, Co-SR
NAV rules need to be modified in UL AP cooperation procedure as mentioned in [2];
The reason is when sharing AP setup a TXOP, the shared STA set basic NAV, then later when the shared STA is triggered by the shared AP to do UL transmission in the same TXOP, the shared STA can not reply TB PPDU anymore;
Coop Init
Coop Resp
Trigger 1
Trigger 2
TB PPDU 1
TB PPDU 2
BA1
BA2
Sharing AP
Shared AP
Sharing STA
Shared STA
Can not be transmitted, because of basic NAV is not 0
Set basic NAV

## Slide 4: Solution Option 1
The Duration field of Coop Init frame sets a time that is earlier than the start time of TB PPDU frame;
The Duration fields of Trigger 1&2 are extended to set a time that covers TB PPDUs and BAs;
Before shared STA replies TB PPDU2, the basic NAV set by sharing AP already expires;
The duration value for Trigger 2 frame needs to be carried in Coop Init frame. Because shared AP is not the TXOP holder, it can not decide how to extend the TXOP.
Coop Init
Coop Resp
Trigger 1
Trigger 2
TB PPDU 1
TB PPDU 2
BA1
BA2
Sharing AP
Shared AP
Sharing STA
Shared STA
Duration set by Coop Init
Duration set by Trigger 1&2
Set basic NAV

## Slide 5: Solution Option 2
When sharing AP transmits the Coop Init frame, shared STA sets basic NAV base on that frame;
Later, when the shared STA is triggered by the shared AP, the shared STA can temporarily ignore the basic NAV if the last PPDU that cause the basic NAV update is transmitted by the sharing AP;
  The basic NAV is still there, the shared STA is not allowed to start contention before basic NAV reaches 0.
Coop Init
Coop Resp
Trigger 1
Trigger 2
TB PPDU 1
TB PPDU 2
BA1
BA2
Sharing AP
Shared AP
Sharing STA
Shared STA
Duration set by Coop Init
Temporary ignore the basic NAV if it is set by sharing AP
Set basic NAV

## Slide 6: Drawbacks of Solution 2
Solution 2 needs to change the NAV operation rules of shared STA, so it can not be used for legacy STAs
  A shared STA could be legacy STA in Co-OFDMA, Co-TDMA, Co-SR et.al;
If shared STA allows to ignore the sharing AP’s basic NAV when it receive a Trigger frame from shared AP, it will cause some problem
  E.g. when sharing AP’s TXOP initiate frame (which may not intent to form a shared TXOP) failed at shared AP side, shared AP may start a Trigger frame by contention. (see below figure)
RTS
RTS
RTS
CTS
Trigger
Sharing AP
Shared AP
Shared STA
Sharing STA

## Slide 7: Conclusion
NAV rules need to be modified in UL AP cooperation procedure because shared STA may set basic NAV by sharing AP, so the shared STA can not be triggered to do UL transmission;
Two potential options are provide for discussion
  Opt 1: Sharing AP set NAV step by step in UL AP cooperation procedure
  Opt 2: add rule to allows shared STA to ignore the basic NAV that set by sharing AP
Opt 1 is transparent to shared STA, so legacy STA may also involve into AP cooperation procedure;
Opt 2 can not be supported by legacy shared STA, and may also cause interference to sharing AP’s transmission in some case;
Opt 1 is preferred.

## Slide 8: Straw Poll 1
Which option do you prefer to for NAV setting in UL AP cooperation procedure?
  Opt 1: Sharing AP set NAV step by step in UL AP cooperation procedure
  Opt 2: add rule to allows shared STA to ignore the basic NAV that set by sharing AP
  Opt 3: Other solution
  Opt 4: need more discussion

## Slide 9: Reference
[1] 11-19-1262-08-00be-specification-framework-for-tgbe
[2] 11-20-0475-00-00be-coordinated-txop-sharing-in-ul