## Slide 1: Buffer Management for Multi-Link Device
Date: 2020-04-20
Authors:

## Slide 2: Background
802.11be defines a multi-link setup signaling exchange executed over one link initiated by a non-AP MLD with an AP MLD as follows:
  Capability for one or more links can be exchanged during the multi-link setup.
  The AP MLD serves as the interface to the DS for the non-AP MLD after successful multi-link setup
  NOTE 1 – The link identification is TBD.
  NOTE 2 – Details for non-infrastructure mode of operation TBD.
As per the discussion in the TGbe call, multi-link setup is association request/response exchange
In this contribution, we discuss the buffer management during association request/response exchange

## Slide 3: Background
During association request/response exchange, we have a Listen Interval field to help the AP to determine the lifetime of the frames that it buffers for a STA
  Listen Interval is carried in association request frame and benefits to the STA’s power save
  AP could reject the association request if Listen Interval parameter sent by the STA is not reasonable
After association, AP may delete buffer for the implementation dependent reasons, including the use of an aging function and availability of buffers where the aging function is based on Listen Interval filed
After association, AP aging function shall not cause the buffered BUs to be discarded after any period that is shorter than that indicated by the STA for which the BUs are buffered, in the Listen Interval field of its (Re)Association Request frame
  This aging function is independent of MSDU lifetime which also be used to discard the frames

## Slide 4: Listen Interval for Multi-link Device
However for a MLD, there may exist more than one STA.
Two options are provided for the Listen Interval field
  Opt 1： Listen Interval applies to the MLD level, no extra field is needed in the association request frame
  Opt 2: Listen Interval applies to the STA level, extra fields are needed in the association request frame
  Given that the traffic sent to a STA is routed by the MLD MAC address, not the STA MAC address, we prefer Opt 1
  Propose to reuse the existing Listen Interval field, but apply it to the MLD level
  Or add a new common field for all the STAs
In this case, the Listen Interval field is used to indicate that the AP MLD how often a STA in power save mode in a STA MLD wakes to listen to Beacon frames

## Slide 5: Listen Interval for Multi-link Device
According to the Spec, Listen Interval field is in units of beacon interval. However, now Listen Interval applies to MLD level where there are multiple beacon intervals
In this case, we propose the following two options
  Opt 1: the value of Listen Interval field is in units of the bacon interval corresponding to the selected link
  Opt 2: the value of Listen Interval field is in units of the maximum value of beacon intervals corresponding to the setup links
Since the selected link may not be supported by the client and no such report to AP MLD, we prefer opt 2

## Slide 6: Summary
We propose the AP MLD uses Listen Interval field in determining the lifetime of the frames that it buffers for a STA MLD
  We prefer that listen Interval field in the association request frame applies to the MLD level, not to the STA level

## Slide 7: SP 1
Do you agree that Listen Interval field in the (Re)Association Request frame sent by a non-AP MLD shall apply to the MLD level, not to the STA level in r1？

## Slide 8: SP 2
Do you agree that AP MLD shall not discard the buffered BUs to a non-AP MLD after any period that is shorter than that indicated by the non-AP MLD for which the BUs are buffered, in the Listen Interval field of its (Re)Association Request frame in r1?

## Slide 9: SP 3
Do you agree to reuse the existing Listen Interval field in the (Re)Association Request frame for the non-AP MLD in r1?

## Slide 10: SP 4
Do you agree that the value of Listen Interval field sent by the non-AP MLD is in units of the maximum value of beacon intervals corresponding to the setup links in r1?