## Slide 1: Midamble design
Date: 2020-04-29
Authors:

## Slide 2: Abstract
The TGbd group has agreed to investigate techniques to suppress discrete spectrum components in PPDUs with midambles [1]
This contribution describes and evaluates a technique based on midamble randomization
It is proposed to include midamble randomization in the design of 802.11bd PPDUs

## Slide 3: Recap – symbol randomization in 802.11ba
The 802.11ba PHY is utilizes ON-OFF Keying.
The TGba draft [2] recommends randomization of the OFDM symbol representing “ON” in order to suppress discrete components in the spectrum
Reference [3] introduced a low complexity symbol randomization technique. In a nutshell, a pseudo-random sequence of ’s is generated and applied to the ON signal resulting in a phase randomized ON waveform.

## Slide 4: Midamble Randomization in TGbd
It is proposed to utilize a method similar to that adopted by 802.11ba, consisting of generating a pseudo-random sequence of ’s and multiplying each midamble by one of these values
Suppose that a PN sequence consisting of has been generated. In the case of SISO PPDUs, the midambles are randomized as shown below

## Slide 5: Midamble Randomization in TGbd - MIMO PPDU
In case of MIMO PPDUs there are two alternatives
Option 1: different pseudo-random sequences are applied to the LTFs in a midamble
  The same phase shift must be applied to both layers

## Slide 6: Midamble Randomization in TGbd - MIMO PPDU
Option 2: the same pseudo-random sequence is applied to all LTFs in a midamble.
  The same phase shift must be applied to both MIMO layers

## Slide 7: Midamble and Data Randomization in TGbd
The data field symbols immediately following the n-th midamble and preceding the (n+1)-th midamble may also be multiplied by the same pseudo-random value as the n-th midamble [4]
The advantage of this method is that if the channel estimate used for the demodulation of the data is based only on the preceding midamble, then the midamble randomization is transparent to the receiver (i.e. the receiver could process the PPDU in the same way regardless of the value of )

## Slide 8: Midamble and Data Randomization in TGbd
One spatial stream
MIMO PPDU

## Slide 9: Remarks
The Appendix contains a theoretical demonstration that midamble randomization suppresses the discrete spectrum components.
In the MIMO case, randomization of the phase could destroy the orthogonality property of the P matrix, which is necessary for channel estimation.
The procedures suggested in slides 5 and 6 preserve the orthogonality of the P matrix because they are equivalent to multiplying zero, one or two columns of the P matrix by -1. These operations preserve the orthogonality of the P matrix.

## Slide 10: Generation of the PN sequence
Option 1: use the sequence defined in (17-25) of IEEE 802.11-2016. This is the sequence used to control the polarity of the pilot subcarriers. This sequence consists of 127 values and can be extended cyclically to any length
Option 2: generate a PN sequence by means of the LFSR described in Section 20.3.9 of IEEE 802.11-2016. If the shift register is initialized with ones then the same PN sequence as in option 1 above is obtained
Option 3: other PN generator

## Slide 11: Transmitter and Receiver processing
The complexity of the transmitter processing is low. The phase shift can be applied to the midamble LTFs in either time or frequency domains.
Receiver processing also has low complexity, as it is the reverse of the transmit processing, and may also be performed in time or frequency domains.

## Slide 12: Simulation results
The PN sequence has been generated according to option 1 in slide 7.
Preamble periodicity (worst case scenario)
Resolution bandwidth 3 kHz (worst case scenario)
PPDU bandwidth 10 MHz
No LTF compression
 | PPDU without midamble (Reference) | PPDU with midamble, no randomization | PPDU with midamble, randomization opt 1 | PPDU with midamble randomization opt 2
1 | 0 dB | 6.1 dB | 0.4 dB | same as opt 1
2 | 0 dB | 10.8 dB | 0.4 dB | 1.8 dB
 | PPDU without midamble (Reference) | PPDU with midamble, no randomization | PPDU with midamble, randomization opt 1 | PPDU with midamble randomization opt 2
1 | 0 dB | 6.1 dB | 0.4 dB | same as opt 1
2 | 0 dB | 10.8 dB | 0.4 dB | 1.8 dB
Maximum power over sliding 3 kHz window relative to PPDU with random data

## Slide 13: Summary
A low complexity technique to randomize the midambles has been described and it has been shown that it is effective in suppressing discrete components in the PSD
It is proposed to introduce this midamble randomization procedure in TGbd
Several implementation options were presented, having minor differences.

## Slide 14: Straw poll 1
Do you agree that the suppression of discrete spectrum components in PPDUs with midambles shall include a randomization of the midambles achieved by multiplying the midambles by a pseudo-random sequence of ’s?
[Note: The exact randomization procedure is the subject of the next straw poll]
Y: 11
N: 0
A: 10

## Slide 15: Straw poll 2
Which randomization method for PPDUs with midambles do you prefer?
Each LTF in a midamble is multiplied by a pseudo-random value .
  In the case of MIMO PPDUs, the same pseudo-random value is applied to both spatial streams.
  The data part of the PPDU is not randomized
  The method is illustrated in slides 4 and 5
All LTFs in a midamble are multiplied by a pseudo-random value The data symbols immediately following any given midamble are multiplied by the same pseudo-random value as said midamble
  In the case of MIMO PPDUs, the same pseudo-random value is applied to both spatial streams.
  The method is illustrated in slide 8
A 5/B 8/Abstain 23/

## Slide 16: Straw poll 3
Which method to generate the PN sequence used to randomize the midambles do you prefer?
Use the PN sequence defined in (17-25) of IEEE 802.11-2016 (this is the sequence used to randomize the pilots)
Some other method
A 18/B 0/Abstain 15

## Slide 17: Motion
Move to include the following text to section 3 of the 11bd SFD
“PPDUs with midambles shall be randomized in order to suppress discrete spectrum components. The midambles symbols shall be multiplied by pseudo-random values plus/minus one. The data symbols immediately following any given midamble shall be multiplied by the same pseudo-random value as said midamble. In the case of MIMO PPDUs, the same pseudo-random values shall be applied to both symbols of the midamble. The pseudo-random values are defined in (17-25) of IEEE 802.11-2016”

## Slide 18: References
[1] M. López and L. Wilhelmsson “Remark on PPDUs with midambles”, IEEE 802.11-20/0476r1 https://mentor.ieee.org/802.11/dcn/20/11-20-0476-01-00bd-remark-on-ppdus-with-midambles.pptx
[2] Draft standard 802.11ba D6.0
[3] S. Shellhammer et al. “WUR Power Spectral Density”, IEEE 802.11-18/0824r1, https://mentor.ieee.org/802.11/dcn/18/11-18-0824-01-00ba-wur-power-spectral-density.pptx
[4] Discussion in TGbd during the presentation of 11-20/0682r0 between IEEE SA member Rui Yang and the presenter

## Slide 19: Appendix
In this appendix it is shown theoretically that suppression of discrete spectrum components can be achieved by randomization of the phase of the midambles.
Notation
: data or pilot frequency domain symbol (M-QAM) corresponding to subcarrier and OFDM symbol number , which are assumed to be independent and have unit power
: LTF frequency domain symbol corresponding to subcarrier .
: phase shift in -th subcarrier due to GI/CSD (independent of the data)
: OFDM symbol duration, including the GI
: subcarrier spacing
: rectangular window, with value 1 if and 0 otherwise

## Slide 20: Appendix
: highest data subcarrier index
: The total number of OFDM symbols in the signal is
The following deterministic sequence is introduced to describe the baseband signal with midambles
Finally, a sequence of random phase shifts is introduced.
independent binary random variables with 1/2. These are the random phase shifts imparted to the midambles in order to suppress the spectral lines. These random variables are also assumed to be independent from the data symbols .

## Slide 21: Appendix
The baseband signal is written as the superposition of data and midamble symbols
where

## Slide 22: Appendix
The PSD of the continuous time baseband signal is defined as
For convenience, the following auxiliary functions are defined
(where )
With this notation, it can be verified that

## Slide 23: Appendix
The expectation in the expression for the PSD can be split into three terms:
=
+ +
Next, each of the terms on the right hand side of the equation is computed.

## Slide 24: Appendix
The computation of the first term relies on the assumption that , and the fact that .
=

## Slide 25: Appendix
The computation of the second term relies on the assumption that
=

## Slide 26: Appendix
The computation of the third term relies on the assumption that , and the facts that and
=

## Slide 27: Appendix
Collecting all the terms,
Note that
The PSD does not contain any discrete components
The PSD is independent of the proportion of midambles in the baseband signal
The PSD is independent of the value of the periodicity parameter of the midambles